## Slide 1
Deadlock & Livelock Detection in Power Controllers Using Under-constrained Formal Testbench
  Ipshita Tripathi, Qualcomm India Private Limited
  Rahul Gupta, Qualcomm India Private Limited
  Arumugam Velayoudame, Qualcomm India Private Limited
  Vinay Garipelli, Qualcomm India Private Limited
Simulation was still finding issues late in verification cycle in a newly developed power controller because of large number of corner scenarios
Formal Verification deployed because of exhaustive nature of formal to ensure robustness in verification effort covering all possible corner case scenarios
Formal deployed late in verification cycle with 5 weeks left to tapeout
Verification scope limited to:
    To check that power controller was able to aggregate votes correctly and move into Power Off/On states correctly
    To check correctness of control signal sequence
    To check that power off/on are always mutually exclusive events
Formal verification testbenches were deployed at the IP level to weed out bugs
Motivation
Main Idea
Power Controllers aggregate votes to go into Power Off/On mode from various different resources in the chip
Formal testbench was kept under-constrained w.r.t. votes being seen from various resources to be able to see a large number of random vote inputs & vote withdrawal combinations from different resources
Assertions were coded to check for correctness of sequence of control outputs
  Assertions were coded to keep in mind the under-constrained environment so as to minimize the false failures seen
    Liveness properties were added to check for deadlock conditions
    Safety properties were added to check that mutually exclusive events do not occur simultaneously
    Constraints were applied sparingly to enable maximum number of scenarios to be covered
DUT Details
The Under-Constrained Setup- Advantages and Limitations
Liveness properties for deadlock detection
Assertion Modelling Considerations in Under-Constrained setup
Legal Sequence of Inputs – Should result in PU/PD
Late arrival of vote – False Failure
Legal Backpressure conditions stalling forward progress– False Failure
B
A
F
C
A
C
B
D
E
F
PU/PD
A
C
B
D
E
F
Stall
Assertions need to be modelled to minimize the number of false failures seen
Late arrival of incoming votes could cause false failures
Backpressure conditions will lead to forward progress being impeded due to legal stall scenarios
Safety Properties for Livelock Detection
Safety Properties were coded to check
  That two mutually exclusive flags indicating sister FSM power Up and Power down scenarios are never asserted simultaneously
  Relaxed properties were also added which checked that in case these flags were asserted simultaneously, they should eventually move to one or the decision within finite time
This helped uncover scenario where sister FSM was continuously executing power up and power down states forever due to assertion of mutually exclusive events which would remain asserted simultaneously forever leading to livelock from which one could not recover
1
2
3
4
5
Ctrl Signal A
Ctrl signal B
Power ON
Power OFF
A & B if asserted together causes continuous execution of sister FSM
Appearance of forward progress while actually it is stuck in livelock situation with no way of exiting/stopping the FSM
Primary FSM
Sister FSM
Properties were coded which checked
    Forward progress of Power Down/Power Up decision each time the entire sequence of votes were seen
Uncovered corner case deadlock scenarios where the controller FSM remained stuck in a given state infinitely despite all votes arriving
Deadlock was seen when internal control flags were cleared inappropriately due to corner case scenario
Flag A
Flag A cleared incorrectly in corner-case
scenario causing unrecoverable deadlock scenario
Advantages:
  Helps test coded properties against a large set of inputs
  Helps uncover corner case scenarios which are difficult to hit in simulation which cause design issues
  Reduces the chance of accidentally filtering out a strictly legal scenario due to accidental over-constraint
Disadvantages:
  Can lead to seeing several false failures due to the extra input scenarios checked which are not strictly legal
DUT
All Possible Input Combinations
Under-constrained setup – Strictly legal + other input scenarios
False Failure
Design Bug
Strictly Legal Input
Strictly Illegal Input
Not Strictly illegal Input
LIGHT CONSTRAINTS TO FILTER STRICTLY ILLEGAL INPUTS
DUT
Blk B
Blk C
Blk D
Blk E
Blk F
Blk A
Number of Inputs: 150+
Number of Outputs: ~200
Number of Interlocking FSMs : Numerous
Number of Distinct Input Interfaces: 5+
Number of resources polled for voting: 5+
Number of wakeup events: ~20
High concurrency of incoming inputs!!
Large number of corner case scenarios!
Large number of corner case scenarios are possible as different resources can vote at random times to go into power Off/On
DUT will aggregate the votes internally only once a certain sequence of votes have been seen from the peripheral blocks
DUT will cause a power up/ power down sequence only if a legal sequence of incoming votes have been seen
  E.g. A-> B-> C -> D -> E -> F sequence of votes should cause decision to go into power down/power up
Inputs from each block are independent of the other
  Can vote to go into power down/power up
  Some resources do not have a two way handshake and can withdraw votes at random time
Assertion needs to be modelled so as to minimize the number of false failures seen
Results
6 corner case bugs were found within 3 weeks using under-constrained formal testbench
  4 of bugs were difficult to hit in simulation
  2 late critical bugs found
Bugs included livelock, deadlock and vote drop scenarios and fixes added to design robustness
Decision to deploy formal earlier in verification cycle to detect bugs early in design cycle so that more comprehensive verification can be carried out