## Slide 1: A Multi-perspective approach to IC power grid development for 7nm based designs
  Mahendrasing Patil
  Intel Corporation, Bangalore, India
  Ravi Teja Susarla
  Intel Corporation, Bangalore, India
  Surendra Boosam Kota
  Intel Corporation, Bangalore, India
Intel and the Intel logo are trademarks of Intel Corporation or its subsidiaries in the U.S. and/or other countries

## Slide 2
  Mahendrasing Patil
  Intel Corporation,
  Bangalore, India
  mahendra.patil@intel.com
  Ravi Teja Susarla
  Intel Corporation,
  Bangalore, India
  ravi.t.susarla@intel.com
  Surendra Boosam Kota
  Intel Corporation,
  Bangalore, India
  boosam.kota.surendra@intel.com

## Slide 3: A Multi-perspective approach to IC power grid development for 7nm based designs

## Slide 4: Abstract
IC Power delivery network is designed to provide required voltage to the cells performing logic operation. With advanced technology scaling there is increase in power density and metal wire resistances, causing higher IR drop. This can result in functional failures. Power grid impacts available routing resources, design rule violations and related layout cleanup effort, signal loading and power consumption.
While the chip designers have focused on aspects of SoC design, there is very less exploration on how the power grid impacts multiple design aspects.
This work focuses on highlighting aspects impacted by the power grid design.

## Slide 5: Outline
Motivation
Design of Experiments
PG Grid Evaluations
Analysis Results
Conclusion

## Slide 6: Motivation
Problem statement –
Increased power density and stringent technology manufacturing rules has made power grid design complex and challenging.
Traditional approach is based on only improving voltage levels.
It is very important to understand impact of power grid on different design aspects.
Motivation -
Study impact of power grid design on multiple design aspects and provide methodology framework for optimal 7nm power grid design considering different design aspects.

## Slide 7
Five PG grid options were chosen for evaluations – these options were derived considering
TSMCTM N7 Standard cell architecture which puts restriction M1 PG pitch –target to reduce M1 tapping distance
Local power grid layer selection – standard cell pin accessibility versus charge sharing
Routing resource effectiveness of via pillared grid versus continuous grid
Grid with lower impedance path to voltage sources (bumps) as well as to the decap network
An overdesigned grid to assess impact on routability, power dissipation and run times
Power grid evaluations

## Slide 8: PG Grid Evaluations - Baseline Option
Baseline option Strategy :
- Based on sample power grid from foundry
- Via pillar grid with via pillars (staples) on all layer between M9 and M1
- M13 layer is also staple layer
Via pillar – intermediate layers are used only for via overhangs – no continuous wires on particular layers
Via pillar
IR drop analysis summary
Major IR drop – M12, VIA0 and M0
TSMCTM N7 - 7nm standard cell library [1]
- is designed to allow better standard cell placement freedom by making two M1 straps closer
- For big cells, minimum 2 adjacent M1 tracks are reserved for M1 PG feed-through.
- Limits dual M1 PG net pitch reduction – causing high IR drop on M0 (~2%)

## Slide 9: PG Grid Evaluations - Option1 Grid
Option1 Strategy :
- Replaced adjacent dual M1 same net straps by M1 staples of power and ground staples (VIA stack).
- Staples on M1, M2, M6, M7, M10 and M11
- M1 same-net pitch is half of baseline option– reduced M0 tapping distance by half
IR drop analysis summary
M0 IR drop contribution down by half
reduced top layer IR drop contribution
VIA3 to VIA0 major IR drop contributors
Power net via pillar on the left M1 track
Ground net via pillar on adjacent right track
Lower static IR drop but higher dynamic drop than baseline option
Staples or VIA ladder on M1 and M2 resulting in high ohmic connection to local decap fabric

## Slide 10: PG Grid Evaluations - Option2/3/4 Grid
Option2 Strategy and IR drop summary :
continuous M1/M2 grid, staples on M6, M7, M10 and M11
M3 pitch reduced slightly
- Continuous M1/M2 helps charge sharing
Option3 Strategy and IR drop summary :
All layers continuous grid
Slight reduction in M3 pitch
Significant reduction in dynamic IR drop
Option 4 strategy and IR drop summary:
overdesigned grid
Doubled M2 PG density from option3
Reduction in static IR drop but increase dynamic drop

## Slide 11: Analysis Results
Proposed methodology based PG provides balanced voltage drop contour across all layers compared to any other options
Baseline Grid :
High DRC/shorts count – M2 overhangs blocking pin access and key layer to switch to higher layers.
Maximum routing resources available - Lowest signal loading, average power and router runtime
Inadequate IR drop performance
Option1 Grid (M1 and M2 via pillars):
High route times – jogs around many tiny M1/M2 DP geometries
Higher dynamic IR drop due to increased resistance to local decap fabric
Higher signal loading and power than baseline option
Lower DRC count - M1/M2 via placement avoiding signal pin blocking
Option2 Grid (M1 and M2 continuous):
Lower runtime and DRCs - improved pin access & continuous grid on DP layers
Lower average signal loading and average power than option1
Significantly lower dynamic IR - low impedance to decap fabric
Option3 Grid (continuous grid on all layers):
Increased signal load and power due to lower resources available, DRCs in control
Very good dynamic IR –
Option4 Grid (overdesigned grid):
Significant increase in signal loading, average power & router runtime
Dynamic IR drop impacted to increased loading and power density
Conclusion : Option3 offers right tradeoff with best IR drop performance and routability with reasonable compromise on runtime and power.

## Slide 12: Conclusion : Power Grid Design Impinging Issues
While the primary objective of power grid is to reliably supply required voltage and current to the logic cells, it should conform to below considerations
Standard cell architecture, Double patterning and coloring rules
Global vs Local power grid approach and charge sharing
  Global power grid should provide low resistance connection to the switching logic
  Local power grid should help during dynamic switching
Pillared grid doesn’t always provide more signal routing resources
Shouldn’t be overdesign :
  impacts available signal routing resources and increase DRC count and LV clean up effort as well as router run times
  Higher Signal loading and thereby total power consumption
Power grid design in lower technology nodes is becoming extremely complex and challenging due to stringent technology manufacturing rules and increase in power density. As a result, power grid design must be done carefully considering all the above aspects.

## Slide 13: References
Physical Design Challenges and Innovations to Meet Power, Speed, and Area Scaling Trend, LC LU, TSMC Fellow/Senior Director (R&D), ISPD 2017