## Slide 1
Coverage Improvement of Assertion Based SDC Verification
at Early Design Phase
Nozomi Yunokuchi (Renesas Electronics Corporation, Japan)
Himanshu Bhatnagar (Excellicon, Inc., US)
We’ve developed the method of ABSV to detect the SDC issues related to timing intent in early design phase.
    The coverage of earlier phase SDC verification is improved.
    The coverage improvement reduces the chance of big iteration loop caused by immature SDC.
    The automatic SVA generation with Excellicon’s tools dismisses concern about human error.
Summary
In order to generate assertion, we prepared the "Generation Rule Library" that contains rules for generating SVA for each SDC command.
Elements
  How to decide which nodes to evaluate during simulation
  Priority for simultaneous changes
  Evaluation signal selection rules to avoid generating unnecessary SVA
By preparing "Generation Rule Library“ :
  Large-scale circuits can be handled since analysis of the circuit structure is not necessary when generating SVA
  Minimizing simulation time overhead since it includes rules that do not generate unnecessary SVAs.