## Slide 1
Jae Hoon Kim, Yongdeok Kim, Wootae Kim, Hyung-Ock Kim, Joonyoung Shin, Jaewon Lee, and Jung Yun Choi
Design Technology, Samsung Foundry, Korea
Design Optimization and Implementation Methodology using Cells with Different Diffusion Breaks

## Slide 2: Motivation
Standard cells: Types of Diffusion Breaks
The performance (speed, leakage, power) of the STD cell varies depending on the types of diffusion breaks; LLE impact
Several types of diffusion breaks have been enabled to support different application (SDB: for lower power, MDB: for higher performance)
Frequency
Area
SDB
DDB MDB
High Performance
SDB
DDB
DDB
DDB
DDB
SDB
SDB
SDB
*MDB: To maximize perf (PMOS: SDB, NMOS: DDB)
MDB
*MDB
MDB
MDB
PC
RX
DB-2
Dummy PC
DB-1
DB-3
Double Diffusion breaks (DDB)
Single Diffusion breaks (SDB)

## Slide 3: Motivation
Goal: Achieving the Same-level of Performance with MDB/DDB Only Design Whereas Less Power and Less Area Cost
Taking best of both worlds with mixed MDB/DDB + SDB implementation
Fit-for-purpose cell usage (MDB/DDB: critical path, SDB: non-critical path)
Smaller power could result in better performance in power-limited scenarios
 | Library Option Comparison |  | 
 | MDB | MDB + SDB | SDB
Performance | 1.08 | ~1.08 | 1
Leakage | 1.20 | ~1.05 | 1
Area | 1.18 | ~1.04 | 1
F/F
F/F
MDB/DDB
SDB
Cell Type | 10nm | 8nm | 7nm | 5nm
High Speed | DDB | HSDB/MDB | MDB | MDB
Low Power/Area | SDB | SDB | DDB | SDB
Speed increase @Same Area
Speed increase @Same Area
Samsung Foundry Unique Solution

## Slide 4: Mixed Cell Implementation Methodology
Special filler
Special Filler
Refined Design Flow for Mixed Cell Implementation (ex. Mixed MDB/SDB)
Powerplan
Placement
CTS
Floorplan
Chip finish
Mixed Cell Placement
Special legalization (spacing) for design rule between SDB and MDB cells is required
Routing
Clock Tree Synthesis with MDB
Minimize clock latency and clock skew
P&R
ECO
Timing
Power
Filler Insertion (including special filler)
Three types of filler cells are required to finish layout (MDB/SDB/Special)
Special filler cell must be placed at MDB and SDB interfaces
SDB
DB-1
DB-1
MDB
DB-3
DB-2
DB-2
DB-3
Spacing
Rule
Mixed ECO Flow
Timing fixing respect to MDB/SDB spacing
Dynamic power recovery across MDB and SDB
Leakage power recovery inside each type
Synthesis
DCG/Genus
Cell Usage: Fit-for-Purpose
Use MDB for clock cells (clock-gating cells)
SDB for data path
F/F
F/F
MDB
SDB
SDB
DB-1
DB-1
MDB
DB-3
DB-2
DB-2
DB-3

## Slide 5: Smart Legalizer: Front-end DRC Handling
DRC Constraints
MDB and SDB cells have different diffusion break; boundary for SDB cell is aligned to PC, boundary for DDB cell is not aligned on PC center
Traditional legalization methodology, cell boundary based legalization, induces DRCs  smart legalization required
DR exists between DB-1 and DB-2/DB-3: additional spacing rule necessary
PC
RX
DB-2
Dummy PC
DB-1
DB-3
Cell boundary
PC misalign

## Slide 6: Results: Library-level Comparison
Chart: 
| Freq. 1 | Freq. 2 | Freq. 3
Mixed | 0.99526 | 0.98799 | 0.95994
Chart: 
| Freq. 1 | Freq. 2 | Freq. 3
Mixed | 0.95833 | 0.95833 | 0.83333
Chart: 
| Freq. 1 | Freq. 2 | Freq. 3
Mixed | 0 | 60 | 98
Chart: 
| Freq. 1 | Freq. 2 | Freq. 3
Mixed | 0.98582 | 1.1356 | 1.1557
Max Frequency Comparison; x-axis: target frequency, y-axis: max frequency gain.
TNS Comparison; x-axis: target frequency, y-axis: total negative slack gap.
Chart: 
| Freq. 1 | Freq. 2 | Freq. 3
SDB | 78.5 | 76.8 | 78.9
Mixed | 77.6 | 76.1 | 76.6
Utilization Comparison; x-axis: target frequency, y-axis: utilization (%).; red-line: mixed, blue-line: sdb
Leakage Comparison; x-axis: target frequency, y-axis: leakage current saving.
DRC Comparison; x-axis: target frequency, y-axis: # of DRCs; red-line: mixed, blue-line: sdb
Chart: 
| Freq. 1 | Freq. 2 | Freq. 3
 | 114 | 11 | 260
Mixed | 32 | 44 | 375
Total Power Comparison; x-axis: target frequency, y-axis: power saving (Internal, switching, leakage).
13.6% max freq. gain at Freq. 2
TNS gap increased gradually
UtilMixed < UtilSDB
LKGMixed < LKGSDB
PWRMixed < PWRSDB
Same-level of DRCs

## Slide 7: Summary
Several types of cells having different diffusion breaks have been enabled to support different application
We developed a comprehensive method for achieving the same-level of performance with MDB/DDB only design whereas less power and less area cost
  Cell usage guide
  Mixed cell placement methodology
  Filler cell development and insertion flow
  ECO flow
The results show the mixed cell implementation leads to improvements in timing, power, while maintaining the same-level of DRCs