## Slide 1: An Advanced Method of Routing Optimization with 3D Coupling Aware To Improve Timing
Motivation
Crosstalk caused by 3D coupling accumulates along a path.
  Coupling on clock nets causes severe timing degradation.
  Preroute timing estimation does not consider coupling.
Current EDA tools fix crosstalk by resizing or adding buffers which increases power, active area utilization, and run time.
A method is proposed to eliminate crosstalk delay caused by coupling considering congestion, 3D effects, and wiring dimensions on different layers. This algorithm is effective after detailed clock or signal routing.
Jialian Tang, Baoguang Yan, Fengfeng Wu, Mike Trick
Avera Semiconductor LLC & GLOBALFOUNDRIES
The method may be used after detailed clock or signal routing, considering both timing and physical information to calculate a scenario for shielding victims and rerouting aggressors.
The proposal costs only very limited runtime increase.
Different coupling scenarios, including 3D coupling, are considered.
The reroute method minimizes impact to timing, congestion, power and utilization.It reduces timing-closure iterations.
These techniques may be integrated with current EDA tools.
S1：When the victim and the aggressor are on the same layer while the local congestion is low, intra-layer shielding will be created to the victim, and then the aggressor will be rerouted to a different location.
Scenarios
S1
1st part is to determine whether the paths are crosstalk dominated (total crosstalk delay is greater than k ratio of the absolute value of slack). It could return 0,1
User can control slack multiplier and crosstalk delay threshold to minimize impact to existing timing histogram.
  Fix crosstalk if total crosstalk delay is larger than a ratio of total slack.
  Fix crosstalk if crosstalk delay on single net is larger than a threshold.
User can control density and congestion limits to minimize impact to DRC.
Run Time of the Flow
  It requires minutes to figure out target nets.
  It takes hours to reroute target nets.
  Iteration count can be controlled by user.
2nd part is to identify the victim net to be optimized where crosstalk delay is greater than the threshold value DTH.
It could return 0,1
3rd part is to calculate physical information for the coupled nets, considering congestion threshold CT.
It could return 1,2,3,4
S2: When the victim and the aggressor are on the same layer while local congestion is high, the wiring track of the aggressor will be replaced by a blockage, and then the aggressor will be rerouted to a different location.
S3: When the victim and the aggressor are on different layers while local congestion is low, the wiring tracks of the victim will be replaced by blockages, and then the aggressor will be rerouted to another location not near the victim.
S4: When the victim and the aggressor are on different layers while the local congestion is high, inter-layer shielding will be created between the aggressor and the victim nets.
Where (Within one violated timing path)
i: the ith victim net of the timing path
j: one of the aggressors contributing to the ith victim net
D(i): crosstalk delta delay of ith net (victim)
n: total number of the nets with crosstalk delta delay
Slack: slack value of the timing path
L(i): the mainly coupled routing layer number of ith net (victim)
L(j): the mainly coupled routing layer number of the aggressor net j
C(j): the local congestion value of the mainly coupled area of aggressor net j reported by tool
CT: the technical routable congestion threshold which can be adjusted by user.
k: a factor to filter crosstalk delay which can be adjusted by user.
DTH: a threshold value to filter crosstalk delay which can be adjusted by user.
Scenarios for different values of S:
S=0: Skip this net, no action applied;
S=1: Shield the victim net on layer L(i);
S=2: Block the original wire track of aggressor;
S=3: Block the projection track of the victim net on layer L(j);
S=4: Shield the victim on layer between the aggressor and the victim.
During timing closure, new setup violations were introduced by increased crosstalk delay from iteration n-1 to n. The crosstalk delta delay came from aggressors located on different layers.
Scenario 3 was dominant -- aggressors on different layers, low congestion. k=0.3, DTH=1ps, CT=0.1.
Lower coupling reduced variation on clock paths, and setup fails were reduced in iteration n+1.
In subsequent iterations, no unexpected new setup violations popped up.
Iteration | Total crosstalk delta delay of victim clock nets (ps) | Setup violation number | Setup WNS (ps)
n-2 | 55.737 | 4256 | -1100
n-1 | 33.283 | 1428 | -163.689
n | 57.577 | 21709 | -175.807
n+1 | 8.487 | 786 | -127.222
Xtalk Fix
14nm chip & Post-route Timing Iterations
Victim
Aggressor
Victim
Aggressor
VSS
VSS
...
Victim
Aggressor
Victim
Aggressor
Blockage
Other Nets
Other Nets
S2
Victim
Aggressor
Victim
Aggressor
Blockage
S3
Other Nets
Victim
Aggressor
Victim
VSS
Aggressor
Other Nets
Other Nets
Other Nets
S4
Adjust victims and aggressors by:
adding blockage,
shielding victims on the same layer, or
applying 3D shielding.
Timing
Congestion
ECO Routing
Partitioning
Floorplanning
Placement
Clock Tree Synthesis
Signal Routing
Timing Closure
Physical Design Flow
Coupling
Wire dimensions
3D shield victim
Adjust aggressor layer
Intra-layer shield victim
No action
Y
Block track
reroute aggressor
End
Victim layer congested
Aggressor layer
congested
Incremental
Timing
Timing analysis on routed design
N
Y
N
Y
N
N
N
Y
Reroute Target Nets
Aggressor/Victim
Same layers
Negative slack Xtalk dominated
Any action on any path
Start
Conditions:
The Method
Design Impact Handling
Coupling Mitigation Algorithm
Implementation Example
Programmable Algorithm
Summary