## Slide 1
Jae Hoon Kim, Wootae Kim, Naya Ha, Hyung-Ock Kim, Sunik Heo,
Hyunjeong Roh, Hayoung Kim, Yonghwan Kim, Hyunwoo Kim, and Jung Yun Choi
Design Technology , Samsung Foundry, Korea
Local Layout Effect aware Design Methodology for Performance Boost below 10nm FinFET Technology

## Slide 2: Motivation
The Indispensable Impact of Layout Context
The performance (speed, leakage, power) of the STD cell varies according to the layout context around the cell; refer to as local layout effect (LLE)
Device performance shifted by LLE is ever increasing in technology scaling down  not enough to model the performance of a transistor or cell in isolation
While the process has developed to minimize its impact, designer has considered it only in terms of robust design (multi-corner library, specialized cell place for WPE)
[FinFET stress proximity effects; courtesy of Synopsys blog]
[Well Proximity Effect, WPE]
Photo resist
Photo resist
STI
STI
STI
well
well ion implant
[STD cell delay variability induced by cell placement]
stdcell delay
occurrence
SS.lib
TT.lib
FF.lib
STA
NETLIST
SDC
PEX
Timing Signoff
[Multi-corner libraries]

## Slide 3: Motivation
Goal: Take Advantages of The Impact of LLE on Standard Cells
RX is one of the most representative parameter which could be under control in P&R and could give enough performance gain at the cost of implementation.
1. Tensile Increase mobility of nFET, which has efficacy of Idsat increase
2. Compressive Decrease mobility of nFET, which has efficacy of Idsat decrease
NOTE. LLE impact can be reversed depending on the process.
[Occurrence of RX shapes by transistors having different width]
Place the logic or filler cell in consideration of the implementation so that the LLE parameter have an optimized value for performance
1. Cells on timing critical regions: (a) L-shape RX maximize layout patterns that can boost the cell performance 2. Cells on non-timing critical regions: (b) Rectangular RX maximize layout patterns that can decrease the cell performance
[Occurrence of RX shapes by cell placement]
(a) cell on timing critical path
(b) cell on non-timing critical path
Tensile Larger Idsat
FIN1
FIN2
FIN3

## Slide 4: LLE-Aware Design Methodology for Performance Boost
Design Flow
1. PDK Update
P&R routing techfile update to get RX layer visible in P&R tool
Standard cell LEF is modified to have RX description
A set of new libraries characterized under different RX overlays could be prepared, or alternatives (ex. derating) could be exploited
Filler cell development (HP filler)
2. Legalizer Development
Tries to find the target cells that are in the timing critical path in all setup corners
Verify if there is empty space on its left and right sides
If empty, the HP filler will be inserted
If not, a new legalizer that can see the RX layer tries to make L-shape RX , if possible
[A new high performance (HP) filler cell: fewer fins at nFET]
3. Checker Development
During P&R: Verify whether the L-shape RXs are created at the adjacent of hold critical cells by the legalizer or by the HP filler insertion (clock tree, latch, and Flip-Flop)
During ECO: Because the STA tool already knows the information that the cell is in setup critical or hold critical, it will be incorporated into the next ECO script

## Slide 5: Experimental Results
Library-Level Performance Gain
 | A | B
Worst setup slack (pba) | 0.0948 | 0.1190
# of hold violation (pba) | 0 | 0
 | Mean | Standard deviaiton | Max
(B–A)/A*100 | 8.3% | 6.3% | 33.9%
(B-A)/Period*100 | 2.1% | 1.3% | 6.0%
(a) Slack changes
(b) Setup slack improvement per paths (# of paths: 100,000)
Setup Slack: 3.1% increased (worst setup slack), setup slack per path moved positive direction
Hold: No additional violation occurred
A checker prevents the HP filler from being inserted into the adjacent of cells on hold timing critical path
Timing QoR Comparison: Setup

## Slide 6: Experimental Results
Silicon-Level Performance Gain: LVCC Measurement
(a) Conventional Method
(b) Proposed Method
OCCT shmoo plot of frequency versus VDD
LVCC margin decreased by 11.11% at our test clock frequency

## Slide 7: Summary
In FinFET technology, LLEs and their impact on performance is not negligible.
We proposed a new LLE-aware P&R and STA methodology which could achieve performance boost respect to RX layer with new logical and physical views in commercial EDA tools
  PDK update
  Legalizer development
  Checker development
This performance improvement allows designers to sign off at higher frequency or explore design space effectively with higher level of AC performance.