## Slide 1: A Graph Based Modelling OF Multi Input Switching (MIS) in STA with Silicon Path Frequency Correlation
Amartya Mazumdar, Ulhas Kotha, Anshuman Seth,
Tezaswi Raja, Reecha Jajodia, Jaison Kurien, Sarvesh Sharma

## Slide 2
What is Multi Input Switching (MIS)?
Single Input Switching (SIS)
2-input NAND
P1
P2
Standard cell library timing models are SIS based
Does not capture real-time operations where multiple inputs may be active together
Multiple Input Switching (MIS)
MIS : More than one input switching simultaneously
Gate’s timing may be faster/slower than modeled by SIS
Parallel path  faster ; Series path  slower
2-input NAND
P1
P2
Guiding star !!

## Slide 3
MIS Aware Timing complexity
Alignment of inputs : Arrival time dependency
  Inherent pessimism
MIS causes both speed-up and slow-down. Speed-up effects are more  hold impacting.
Interacting signals slew and waveform shape impacts MIS
Depends on the input state: 0, 1, ↑,↓ . Lot of patterns to be simulated per lib-cell
Characterization of all required permutation is too expensive. High representation costs-library size.
Right balance of complexity for timing closure that avoids unnecessary pessimism

## Slide 4
The Proposed Algorithm
A1
A2
B1
B2
C
ZN
A1
A2
B1
B2
C
ZN
x
x
Input Pattern Generation + Spice
Input Pattern Generation :
  Find SIS patterns  Derive MIS patterns
  Represent logic as directed cyclic graph (DAG)
Standard cell logic DAG
AOI221 : ((A1 & A2 ) || (B1 & B2)) & C
Find this SIS pattern using DAG

## Slide 5
Chart: 
| 50ps | 40ps | 30ps | 20ps | 10ps | full_overlap
P1 | -13.0638 | -17.3646 | -22.072 | -27.2387 | -32.7462 | -38.5537
P2 | -17.0806 | -22.4832 | -28.3294 | -34.6378 | -41.3416 | -48.3838
P3 | -21.3399 | -27.8794 | -34.9525 | -42.5363 | -50.5006 | -58.8552
P4 | -14.3145 | -19.1056 | -24.0865 | -29.5692 | -35.2332 | -41.4072
P5 | -17.1284 | -22.561 | -28.4412 | -34.7439 | -41.3991 | -48.4538
P6 | -21.9173 | -28.7446 | -35.8668 | -43.5397 | -51.5574 | -60.1298
cLoad=30fF I/P trans=40ps PVT = FFG_1p15V_105c
% change in cell delay
MIS speed-up for AOI221 fall
speed up
Input waveform skew
Results
Pattern | Related Pin | MIS Impacting Pin | A1 | A2 | B1 | B2 | C1
P1 | A1 | B1 | ↑ | 1 | ↑ | 1 | 0
P2 |  | C |  |  | 0 | 1 | ↑
P3 |  | B1 & C |  |  | ↑ | 1 | ↑
P4 |  | B2 |  |  | 1 | ↑ | 0
P5 |  | C |  |  | 1 | 0 | ↑
P6 |  | B2 & C |  |  | 1 | ↑ | ↑
A1
A2
B1
B2
C
ZN
6 reduced patterns for AOI221 for A1ZN
Spiced for different input waveform skew
High MIS impact when all || paths activated : P3 and P6
AOI221 : ((A1 & A2 ) || (B1 & B2)) & C

## Slide 6
Handling Non-Inverting Logic
Spice-Excitation:
  For Fall MIS, the PUN need to be excited.
  Hence, in Spice, PDN and PUN pattern need to be swapped.
Spice-Measurement
  For fall MIS, measurement Fall_at_input to Fall_at_output.

## Slide 7
Handling Inversion with-in the logic: !((!(A1&A2))|(B1&B2))
A1, A2 are in stage1.
A1,A2 related output fall will trigger || PUN in stage 1.

## Slide 8
STD CELL MIS Coefficients – 7nm/FFG_0c_1p16V
Results

## Slide 9
Results
Slack degradation when MIS is incorporated in PrimeTime.
4th Quadrant shows paths with negative slack with MIS.
0.5% paths in the design need to be reviewed and fixed.
MIS impact on STA (Hold) of nVIDIA based design

## Slide 10
Pessimism Reduction
A lot of these paths can be pruned, deep datapath. Minimal likelihood of aligned input waveforms on all cells.
Partial overlapping windows. For A2ZN transition, the input waveforms at pin A1 and B are not transitioning
Input pins window alignment for cell AOI21

## Slide 11
Chart: 
Pattern 1 | 1.6949 | 0 | 0 | 1.7094 | 0.86207
Pattern 2 | -0.87719 | 0 | -1.1696 | -1.7241 | -1.7391
Pattern 3 | -1.7241 | -1.7391 | -0.86957 | -1.7391 | -4.3478
Silicon Path Frequency Correlation
Identify MIS susceptible paths from MIS PT sessions
Generate Pdelay patterns from TETRAMAX for SIS and MIS and generate ATE data. The silicon path delay is obtained from failing frequency for SIS and MIS
Overall speed-up/slow-down on path is computed and is being correlated with PrimeTime.
Y : % change in frequency
X : Chip Designator
Speed up
Slow down

## Slide 12
Novelty
MIS is computationally expensive. Presented method reduces the number of computation.
The algorithm supports both speed-up and slow-down.
Future Work & Summary
Silicon proven failures due to MIS
Reduced pre and post silicon miscorrelation  Improved silicon yield.
Reduced guardband.