## Slide 1
Tile-Based Automated Pipeline Floorplanning
Greg Ford – Avera Semiconductor
Region Tiling
Background
As designs get larger, there is an increased need to pipeline signals traversing longer distances
  Pipeline stages can become a system level performance bottleneck, so being able to insert an optimal amount is critical
General placement algorithms often produce unbalanced pipe placement
Most pipeline planning requires fixed start/end points, and pre-placement
Solution
Guide placement so pipe stages are well spaced along path
  Pipeline paths will need to be logically traced to understand the association between source/destination and interceding pipe stages
  Design will need to be placed (though not optimized), in order to know source and destination locations to guide placement along the physical path
Assess pipeline path depth to ensure optimal stage count
  Gauged by maximum stage distance, based on clock frequency and ps/mm characteristics of repowering.
Method
Power Results
Conclusion
Use of pipelining for timing closure is becoming more common as designs continue to get larger
Placing pipeline stages balanced along their path allows for closure with an optimal number of pipeline stages
  Using excess pipeline stages can impact system performance
Tracing pipeline physical paths, and pre-assigning pipeline stages to tiled placement regions allows for an automated balanced solution
  Reductions in WNS/TNS/Power, with a slightly higher initial placement runtime
Start with coarse global placement
  No assumption that locations for source / destination of pipeline paths are known
Iterate through all pipeline flops by name
  Trace forward / backward to overall source / destination for the pipelined path
  Generate a physical placement path between source and destination
    Store result for entire path; no need to process the same path multiple times
  Select balanced positions along physical path
    Abstract positions into local tiles
Timing Results
Runs with and without regions taken through CTS/Routing flow for final optimization comparison
  Using pipeline regions reduced leakage power by 26%
  20% Lower HVT usage compared to baseline run
  38% Lower ULVT usage compared to baseline run
Runs completed using 100um pipe tile regions
  10% higher runtime with regions, in global place
  WNS cut in half; pushed below fixable threshold
  TNS for pipeline paths reduced by 12%
  TNS for all paths reduced by 5%
Local tiles are used as placement constraints to give global placement a degree of flexibility in its solution
Tile size allows for a tradeoff in flexibility
  More tiles add to placement complexity and increase tool runtime
  Scale up tiles based on overall path lengths
    Deeper paths need less granularity
Tiles simplify physical path generation
  Once a path has been generated between two tiles, all other paths between the same tiles reuse the same physical path
Optimizing Pipeline Stages
The optimal number of pipeline stages for each traced source / destination path can be computed
  Start with the total physical distance traced from source to destination
  Determine maximum stage distance from clock frequency and repowering ps/mm
    stages = ceil(path_dist / max_stage_dist) - 1
Often, there will be combinational logic in the path from the source and/or the path to the destination
  Use maximum stage distance between pipe stages to cover distance as efficiently as possible, and use a lower head/tail distance to give extra time for logic depth