## Slide 1
DAC 2019
Timing Closure for an EFPGA IP inside an SoC

## Slide 2: Speedcore™ eFPGA
High density, high-performance FPGA
  Up to 2M LUTs
  Variety of BRAM, LRAM, and DSP IP
Cortex-A75
Private L2
DynamIQ Shared Unit
Shared L3 Cache
ACP
Agile System Cache
Cortex-A55
Private L2
TCZ TrustZone Controller
DDR Controller
MMU
PCI Express
100G Ethernet
SATA
DDR Controller
MMU
MMU
CoreLink CMN
… to integrate in your SoC
  Programmability for your SoCs and your customers
AXI/ACE-Lite Interfaces
  Integrates like any other SOC IP core
Extremely Customizable
  Number of LUTs and FFs
  BRAM, LRAM, and DSP density
  LRAM and BRAM widths and depths
  Customize DSP functionality
  Process technology (Current: TSMC16, TSMC7)
Speedcore eFPGA IP

## Slide 3: ACE: Achronix CAD Environment
Project Setup &Compile
Floorplanning & Placement
FPGA Program & Snapshot Debug
Complete FPGA Design Suite
Full Verilog, SystemVerilog and VHDL support
Full STA support, with OCV derating & multiple corners
  Using industry-standard SDC files.
GUI and TCL scripting
Built-in Logic Analyzer
Full placement and floorplanning support.
Supports all current simulators
Protected/encrypted IP support
Partnerships with HLS providers
Notes: Project setup with ACE is relatively straighforward. The IP Configuration tool allows the user to generate RTL and constraints for any of the library functions ranging from simple RAM memory or shift register wrappers to highly complex logic such as DSP-based FIR filters. The synthesized design goes through ACE design flow which includes place and route, timing analysis and bitstream generation.
The floorplanner perspective provides an interactive feature set to analyze and optimize the place and route of a design and included design search, selection and highlighting tools for design analysis.
A user can analyze his design in hardware using real-time system in-debugger inside ACE called Snapshot. When trigger conditions are met, Snapshot relays information for monitoring signals from the FPGA through JTAG. ACE displays this information in the waveform viewer and can be saved in standard .vcd format.

## Slide 4: Timing Closure: Problem Statement
SoC timing closure is generally a complex task — a task that is further complicated by an eFPGA (embedded FPGA) IP in the SoC. In this case there are no traditional I/O buffers at the interface of the FPGA fabric to the host ASIC that create a clear boundary from a timing perspective, nor does the end user control the logic connecting to the eFPGA instance as they would with a standalone FPGA mounted to a PCB.
With an eFPGA, the programmable block may be inserted anywhere inside an ASIC, meaning that the individual eFPGA ports may connect to other blocks within the ASIC, or to buffers connecting to external pins. Further complicating the process is the fact that the design host in the eFPGA can and will change over time, possibly years after the ASIC was designed.
Rather than leaving it to design teams to develop a process, it is important to provide a clear and defined methodology for achieving timing closure for the eFPGA inside the ASIC as well as extend support for industry-standard timing analysis tools.

## Slide 5: Boundary Tile
Boundary tile
  The interface between the logic, DSP, or embedded memory tiles and the ASIC.
  Includes clock selects, loopbacks, and bypassable registers.
Example Loopback Path
Bypassable Register
Clock Select Mux

## Slide 6: Simple Timing
The timing between ASIC logic and FPGA logic terminates at register boundaries
  ASIC / Speedcore delays do not depend on the FPGA design.
ASIC Timing closure is owned by the ASIC integrator, who uses standard tools (e.g. PrimeTime).
  .lib files representing setup/hold/clock-to-q to/from boundary flip-flops are provided by Achronix to the ASIC designer.
FPGA Timing closure is owned by the FPGA integrator, who uses ACE.
Output
Datapath
Input
Datapath

## Slide 7: Advanced Timing
No register boundaries between the ASIC and the FPGA.
  Timing closure is shared between the ASIC integrator and the Achronix ACE compiler.
  The .lib files from Achronix represent a range of flip-flops locations, to correlate to timing closure in ACE.
  All data and clock insertion delays are provided to ACE with familiar SDC commands:
    set_input_delay, set_output_delay, set_clock_latency
    These commands are generated via Achronix-supplied PrimeTime scripts.
Note
  The selection of Advanced vs. Simple timing mode is done by the FPGA designer. You don’t have to choose at ASIC design time.
Output
Datapath
Input
Datapath

## Slide 8: Advanced Timing
The timing closure process is iterative:
  Choose a target frequency and, determine how much of the clock cycle will be used by the ASIC logic.
  Run ASIC timing closure using an industry-standard tool (e.g., PrimeTime) with the Achronix-provided budgetary lib files.
  Extract the ASIC portion of the delays on each wire, and provide them to ACE via constraint files, following the template provided by Achronix.
  Runs a suite of design through ACE to confirm that timing closure has been met for each one.
  If timing cannot be met for one or more of these designs, modify the FPGA design or go back to step 1 .
Output
Datapath
Input
Datapath

## Slide 9: Advanced Mode #1 – Clock from ASIC
ASIC Integrator:
  Do ASIC timing closure using industry-standard tools and the Speedcore .lib files.
  Extracts the ASIC portion of the delays on each wire, using the scripts and methodology provided by Achronix.
    Data: Td1, Td2, Td5, Td6
    Clocks: Tc1 through Tc6
  ACE determines Td3, Td4, and Tc7 as part of FPGA design flow
Clock Source
Speedcore
data_in
data_out
clk_in
Tc1
Tc2
Tc3
Tc4
Tc5
Tc6
Tc7
Td1
Td6
Td2
Td5
Td3
Td4
out
Close timing before tapeout
Close timing during FPGA design

## Slide 10: Advanced Mode #1 – Clock from ASIC
FPGA Designer:
  Provide the ASIC-owned constraints to ACE, following the template provided by Achronix.
  Compile FPGA designs as normal.
# Constraint File Example
create_clock -name CLK -period Tp [get_pins CLK_GEN/out]
create_clock VCLK -period Tp
set_clock_uncertainty –setup 0.05 CLK
set_clock_uncertainty –setup 0.05 VCLK
# Clock Delays
set clk_max_rising [expr 1.05*(Tc1_Mr + Tc2_Mr + Tc3_Mr + ...)]
set clk_max_falling [expr 1.05*(Tc1_Mf + Tc2_Mf + Tc3_Mf + ...)]
set clk_min_rising [expr 1.05*(Tc1_mr + Tc2_mr + Tc3_mr + ...)]
set clk_min_falling [expr 1.05*(Tc1_mf + Tc2_mr + Tc3_mf + ...)]
set_clock_latency -source -late -rise $max_rising [get_clocks CLK]
set_clock_latency -source –late -fall $max_falling [get_clocks CLK]
set_clock_latency -source -early -rise $min_rising [get_clocks CLK]
set_clock_latency -source -early -fall $min_falling [get_clocks CLK]
# Data Delays
set worst_data_in_delay [expr 1.05*(Td1_Mr + Td2_Mf + Td4_Mf + Td5_Mr)]
set input_delay_rise [expr $worst_data_in_delay + $clk_max_rising - $CRPR1]
set input_delay_fall [expr $worst_data_in_delay + $clk_max_rising – $CRPR2]
set_input_delay -clock VCLK -rise -max -add_delay $input_delay_rise [get_ports data_in]
set_input_delay -clock VCLK -fall -max -add_delay $input_delay_fall [get_ports data_in]
Clock Source
Speedcore
data_in
data_out
clk_in
Tc1
Tc2
Tc3
Tc4
Tc5
Tc6
Tc7
Td1
Td6
Td2
Td5
Td3
Td4
out
Close timing before tapeout
Close timing during FPGA design

## Slide 11: Advanced Mode Example #2 – Clock from FPGA
Clock Flexibility
  Clock source(s) drive Speedcore directly.
  More flexibility: the FPGA designer chooses the actual clock for FPGA and ASIC logic at design time.
Steps:
  Same as before …
  ASIC designer closes timing using industry standard tools
  FPGA designer implements constraint files using Achronix-provided tools, and runs a set of designs to confirm FPGA timing closure.
Notes:
  ACE correctly handles the fact that the CLK pin is now an output that can be selected by the users design.
  More modes are available, if needed by the application.
Clock Source
Speedcore
data_in
data_out
clk_out
Tc2
Tc3
Tc4
Tc5
Tc6
Tc7
Td1
Td6
Td2
Td5
Td3
Td4

## Slide 12: Summary
clk_in
Tc6
With embedded FPGAs, clock paths can be shared across time and space, between the ASIC integrator and the FPGA designer.
  And the selection of Advanced vs. Simple timing mode is done by the FPGA designer. No need to decide at ASIC design time
The ASIC designer uses standard Static Timing Analysis (STA) tools to close timing in the ASIC, and to collect delay information for ACE.
The FPGA designer uses industry standard SDC files with ACE to do FPGA timing closure with the knowledge of ASIC data and clock delays.
Clock Source
Speedcore
data_in
data_out
Tc1
Tc2
Tc3
Tc4
Tc5
Tc7
Td1
Td8
Td2
Td7
Td4
Td5
out
Shared Timing Path
Td3
Td6

## Slide 13
DAC 2019
Timing Closure for an EFPGA IP inside an SoC