## Slide 1: Current Flow Modelling in HDL for Mixed-Signal Co-Simulation Analysis
Lakshmanan Balasubramanian1, Vijay Kumar Sankaran2, Sushmitha T G3, Abhishek K3, Sunita Tirlapur3
1Texas Instruments (India) Pvt. Ltd. 2Cadence Design Systems (I) Pvt. Ltd. 3KarMic Design Private Limited

## Slide 2: Acknowledgements
Setu Kumar, Ryan Smith, Alvaro Caicedo, Tobias Edstrom, and Hagen Graf of Texas Instruments for their hands-on application of the current mode handling in behavioural models
Jagdish C Rao, Ajith Subramonia, and Sunil Kelahatti of Texas Instruments, India for their motivation, encouragement and consistent support to transcend the unknown
Qingyu Lin, Junwei Hou, Yanfei Shen, Amit Mangla, and Vishwajeet V Betai of Cadence Design Systems for their collaboration on several tool, flow and methodology aspects

## Slide 3: Motivation & Problem Statement (1/2)
Verilog-AMS wreal data type enables real numbered modelling of quantities (also VHDL & System Verilog real)
Existing modelling methods and associated connect modules (CM) or interface elements (IE) used for widely available digital and analog mixed-signal (DMS & AMS) co-simulation solutions are primarily dealing with modelling of “potential” or “voltage” and equivalent quantities that are consistent across simulators Not suitable for “flow” or “current” and equivalent quantities
CM at mixed-signal simulation boundary of interest are E2R & R2E When only voltage / potential are considered, they are just number converters  Most commercial simulators treat it the same for both voltage and current modes
Current direction changes across hierarchical boundary  Event driven simulators cannot automatically handle this
When “flow” or “current” or equivalent quantities are modelled similar to “potential” modelling methods, the models are not directly composable with “electrical” or equivalent “lower level abstraction” analysis tools like SPICE or Spectre circuit simulators
Only means to analyse right current flow is to keep both the current source and load sides in SPICE partition of AMS co-simulation  Computational cost is huge
Dynamic handling of currents and voltages is also not possible

## Slide 4: Motivation & Problem Statement (2/2)
Proposed herein is the only method that enables a correct “flow” or “current” modelling in real number that is consistent with SPICE conventions resulting in models that are easily composable and are directly replaceable in-place with SPICE or device level abstraction
+
-
-
+
+
-
+
+
+
+
+
-
+
+
E2R
-
-
R2E
How to model?
Simulation functional failure
Electrical / SPICE
Wreal model

## Slide 5: Proposed Solution
Define conventions for direction of current flow in real numbered (RN) models
Define consistent connect module definitions to handle flow across mixed-signal abstraction boundary
Goal, for interface flow quantities
  Enable consistent digital (event driven simulator) & analog (SPICE based circuit simulator) mixed-signal co-simulation
  RN Model composability
  In-place replacement of RN models and SPICE implementation
Method to handle dynamic V & I quantities
  Given RN model limitations, any interface is either V or I at a given point in time

## Slide 6: Methodology Proposed Flow Conventions (1/2)
Systematic derivation of current directions
Interface direction implies whether it is a source or load, not current direction itself
Current direction is to match between SPICE & behavioural (RN) model  Not possible to match always
Output current direction of RN model kept consistent between SPICE & RN model  To keep sanity and composability
Input of RN model should be consistent from previous stage output
Handle the current inputs internal to the model, per conventions to be aligned
CM modelling to be consistent
DMS behavioural model proposal
Output flow same as that of the actual circuit (SPICE)
Input flow opposite to that of actual circuit behaviour
CM proposal
E2R to invert the current direction
R2E to preserve the current direction
Notes: Implementation of the opposite conventions might work too, however they are less intuitive and their composability concerns are not comprehensively analysed

## Slide 7: Methodology Proposed Flow Conventions (2/2)
+
-
-
+
+
-
Electrical / SPICE
Wreal model
+
+
-
+
+
-
+
-
-
-
+
-
+
+
-
-
+
-
-
+
E2R
-
-
R2E
+
-
E2R
+
+
R2E
-
+
E2R
+
+
R2E

## Slide 8: Methodology Dynamic Potential and Flow Handling
Full dynamism (between potential and flow quantities) cannot be supported with scalar RN models
Conditional dynamism is targeted
Current bias inputs to analog IPs: Usually static
Analog Test Bus (ATB): A critical context of importance with dynamism controlled by known signal state
Existing CMs modelled such that a static configuration between voltage and current mode is supported
  Using verilog module parameter to define and control the mode
  Configurable at simulation elaboration stage  Static for a given simulation
SPICE
SPICE
A
B
C
D
V
I
V
I
VAMS (wreal)

## Slide 9: Methodology Dynamic V & I Handling in Simulator
Define an internal signal to control the mode configuration
Use parameter for a static configuration at elaboration stage
Use the model controlling signal to dynamically configure
  Based on an appropriately identified ATB control & select signals
Simulator enhancement possible  Collaborating with EDA partner

## Slide 10: Methodology Dynamic V & I Handling Prototype
Manual: Identify the dynamic mode control
module ATB ( out)
…
output out; wreal out; // Controlled by ctrl_sig
...
ctrl_sig = !C & D;
…
endmodule
Semi-automated: Use the following TCL command-set to control the mode dynamically
stop -create -object top.atb.ctrl_sig -execute {force top.e2r_dyn_vi__R2E_local__electrical.currentmode_sig [value top.atb.ctrl_sig]} –continue

## Slide 11: Evidence
Targeted DMS & AMS co-simulation test cases developed on which the proposed methods applied and validated  Event driven digital simulation showing mode switch on a given signal interface
Being applied in mixed-signal SoC development, for design and integration verification
Results in significant improvement in design & integration verification cycle-time for AMS contents involving current reference & ATB paths (100x)
Mode switch: V to I
Mode switch: I to V
ctrl_sig
p
p_$flow
r2e_dyn_vi
In voltage Mode
ctrl_sig
p
p_$flow
r2e_dyn_vi
In current Mode

## Slide 12: Summary
Developed a flow direction convention and modelling method for RN models
  To be consistent, composable and in-place replaceable with implementation and SPICE simulation models
Developed a method for controlled dynamic handling of potential (voltage) & flow (current) in a given path
  Semi-automated Prototype built and validated
Limitations & Future scope
Applicability and extension for bidirectional interfaces and multiple driver scenarios under study
Complete automation of controlled dynamism based on the prototyped method is underway
Full dynamism is not possible with scalar RN models
Possible extension to VAMS standard & interception to proposed SV-AMS standard