## Slide 1: Multimodal CDC Analysis
Author Name | Affiliation | Email
Maël RABÉ | STMicroelectronics Student / CDC team member | mael.rabe@st.com
Jean-Christophe BRIGNONE | STMicroelectronics CDC team leader | jean-christophe.brignone@st.com
Paras Mal JAIN | Synopsys Director R&D | parasmal.jain@synopsys.com
Ankush BAGOTRA | Synopsys Sr.Manager, Application Engineering | ankush.bagotra@synopsys.com

## Slide 2: Context
Clock Domain Crossing checks
  Used tool: SpyGlass CDC by Synopsys
Complex designs
  Multiple IPs
  Several clocks
  Test & debug logic
Current CDC approach: Usually done through multiple runs with one mode at a time
  Mode: set of propagated clocks (Ref. Figure 1 for four different modes)
  Main modes: functional, test, debug.
  If two clocks of the same mode: priority given to main clocks like PLL clock to get as close as final usage conditions in this mode.
Figure 1: Different Modes
Clk 1
Clk 2
Sel_A
0
1
Clk 3
Clk 4
Sel_B
0
1
4 combinations → 4 modes
Pessimistic approach
Somewhere in the design…

## Slide 3: Motivation
Current CDC analysis approach has 2 main issues:
  Many constraints necessary to choose which clocks to propagate → time consuming
  Choosing means not to analyse the other combination: CDC issue not in Mode1 while it exists in Mode2 (Ref. Figure 2)
  → coverage < 100% → Deteriorated Quality of Result (QoR)
1
Figure 2: Missing CDC paths due to modal analysis
A new Analysis Flow to reach Maximum Coverage with Minimum Effort using Multimodal Analysis
THE NEED

## Slide 4: Multimodal Analysis Principle
Principle:
  All clocks propagate at the same time
Advantages:
  No clock propagation constraints required anymore → time-saving flow
  All clock combinations in the scope → coverage = 100%
    CDC found anyway in figure 3
Close collaboration between ST CDC and Synopsys teams
  No need for multiple modes specification
  Innovative capability for automatic mode detection and CDC analysis
  Results applicable to all modes in single run
Figure 3: Multimodal coverage

## Slide 5: Multimodal Specific Issues
SpyGlass behaviour:
  SpyGlass infers a new clock at clock muxes output
Same clock set propagates due to common enable logic → if muxes are balanced, no CDC should be reported without mode specification (Ref. Figure 4)
  Called « CDC false paths »
Example of CDC false path (if α = γ)
Figure 4: Double Mux Configuration

## Slide 6: Modal vs MM flow
Clocks definition
Specifications
SpyGlass detection
Clocks definition
Structural CDC analysis
False paths eviction
Specifications
SpyGlass detection
Structural CDC analysis
Clocks propagation definition
Mode
1
2
n
Clocks definition
CDC Coverage : 100%
CDC Coverage : 100%
Constraints Setup
Structural Check
Incremental Modal Analysis
MultiModal Analysis

## Slide 7: Modal vs MM Resources
Runtime
N
N
k men.week
1
<<
<< k men.week
Incremental Modal Analysis
MultiModal Analysis
N : number of modes ; rt : runtime ; a : error chance
CDC constraints set
Users & licences
Analysis duration
Error prone setup management
N * a
<< N * a
1

## Slide 8: False Paths Eviction
Double mux configuration example
Configuration Inference
Automatic identification of double mux configurations
Eviction Analysis
Automatic eviction of paths where Mux outputs share the same domain
Report & Debug
Report for exceptions and coverage for debug
PROBLEM SOLVED !
Faster !
Easier !
More efficient !
Constraints setup
False Paths Eviction
CDC Analysis
Coverage : 100%
Multimodal CDC Flow
Rule clock_info05d
Constraint same_domain_signals

## Slide 9: Case Study
Test case:
  64 bits CPU Sub-System
  State-of-the-art asynchronous interfaces (FIFO, HandShake (HS))
  ~125k registers
  44 clock domains

## Slide 10: Results
SpyGlass Rule | Default Violation Count | Violation Count With False Paths Eviction
Ac_unsync01 (Scalar unsynced) | 1722 | 933
Ac_unsync02 (Vector unsynced) | 1041 | 1010
Ac_glitch03 (CDC glitch) | 2214 | 1506
Ac_sync01 (Scalar synced) | 275 | 999
Ac_sync02 (Vector synced) | 202 | 227
Constraints setup
False Paths Eviction
CDC Analysis
Coverage : 100%
Multimodal CDC Flow

## Slide 11: Summary
Less constraints (-25%)
Less resources & time
Better debug
Multimodal analysis in SpyGlass CDC offers 100% CDC coverage with:
Increasing complexity of circuits
Multi-CPUs Sub-systems
Increased clock domains and their interactions with multiple modes
Only the CDC paths of main modes are analyzed
Deteriorated Quality of Result
Security & safety controllers
Debug logic
DFT
Lower CDC coverage
Systematic debug needed
Exhaustive CDC analysis in all modes
Modal Analysis
MultiModal Analysis

## Slide 12: In the Future…
Idea: using formal analysis to find
  mux outputs sharing the exact same clock (double mux configuration)
  other CDC false paths configurations
Automatic, reliable
What do we have today?
Module “CDC Mode Pruning” in development by Synopsys
  Handles clock exclusivity situations, glitch free muxes, FSM drivers…
  Tested on large CPU sub-systems
Formal analysis assistance