## Slide 1
Machine Learning Based Timing Arc Prediction For AMS Design
Eric Hsu (erhsu@nvidia.com) Ting Ku (TKu@nvidia.com) An-Jui Shey (anjui.shey@empyrean-tech.com) Jason Xing (jason.xing@empyrean-tech.com)
Motivation
Success Story
Case Setup
Runtime & Peak Memory Usage
 | Training | Testing
# of cells | 411 | 30
# of arcs | 90,040 | 6,774
# of non-arcs | 1,696,088 | 15,124,093
 | Runtime (mins) | Peak Memory (GB)
Training | 45:51 | 50.2
Prediction | 7:16 | 64.8
Chart: 
| BD1 | BD2 | BI1 | BI2 | BI3 | BN | BU | GC | HB1 | HB2 | HB3 | HB4 | HP1 | HP2 | IS | NA1 | NA2 | NV1 | NV2 | NV3 | NV4 | NV5 | NV6 | OS | PL1 | PL2 | TS1 | TS2 | TS3 | UP
FP (orig) | 86 | 59 | 23 | 18 | 17 | 77 | 1 | 11 | 76 | 73 | 4110 | 3710 | 338 | 338 | 101 | 241 | 32 | 268 | 104 | 1275 | 147 | 173 | 1 | 12 | 263 | 263 | 15 | 15 | 0 | 532
FP (incr) | 4 | 9 | 0 | 2 | 0 | 0 | 2 | 2 | 29 | 32 | 105 | 154 | 36 | 36 | 6 | 58 | 6 | 34 | 18 | 38 | 11 | 16 | 0 | 1 | 33 | 33 | 21 | 21 | 0 | 511
Timing Arc Existence Prediction |  | 
Original/ Incremental | Predicted: NO | Predicted: YES
Actual: NO | 15,111,407/ 15,123,385 | 13,464/ 1,486
Actual: YES | 515/ 13 | 2,766/ 3,268
Timing Type Prediction | 
Arcs with timing type in .lib | 3,281
Arcs with timing type predicted | (84.30%)/ (99.60%)
Matched | 2,745/ 3,247
Mismatched | 19/21
Timing Arc Training & Prediction Usage Flow
Implementation & Algorithm
Training set
Test set
Lib process,
generate P/N feature/label
Prediction
Input features
Analysis Report
Word Vectorization
NLP
Output labels
Learning
MLP/ADA
Test cross validation
pass
Lib database
Predicted Timing Lib
Confusion Tables for arc existence & types
Missing Arcs Distribution by cell
Conclusions
Booth: #651
Found significant number of real missing arcs in live projects
Reduce number of false positive missing arcs significantly which make it useable at nVidia
Reduce runtime significantly which can enable interactive prediction
Incremental training for better accuracy and immediate feedback for “what-if analysis”
Able to predict timing types
Can be expanded easily to cover train and inference of other timing arc attributes, such as timing sense and conditional arc attributes
ML Classifiers Evaluated:
- MLPClassifier, used in latest implementation
- AdaBoostClassifier, DecisionTreeClassifier, …
Input ML features (9)
- Cell name, pin_name/direction, related_pin_name/direction
- Pin_properties – clock, drive_current, function, is_pad, three_state, …
3 Major Timing Arc Labels
- Timing types (17), combinational, etc
- Timing sense (3), positive_unate, etc
- Conditional arc (4), clock_gating_flag, etc
Timing Arc Prediction Flow:
- Predict timing types with probability
- Train arc existence threshold as control parameter
- As arc existence feature based on above threshold
Training flow (comprehensive):
  Partition training set to fixed number same size subset
  Loop through all subset
  Remove a subset and then build a model
    Evaluate above model using the subset as test set
    Keep the model with best score
Training Data Set
Model
Select the best score model
Incremental Training
Weight processing
Incremental Training data Set
ML Model
Updated Model
Application flow (timing arc prediction ):
Testing data Set
(cell name, pin name, pin direction)
Timing Arc Prediction
Validate arc based on library
No
Report missing arc?
Incremental Training process
Validate missing arc is real?
Yes
Yes
Generate .lib
No
Training flow (incremental):
  Train weight as control parameter
  Expand incremental training set based on weight
  Generate prediction model
  - To handle the mounting timing characterization/validation challenges of custom cells needed for analog and mixed-signal (AMS) design; designers rely on manual arc creation and base on design knowledge.
  - To eliminate error-prone manual effort in arc creation, automation in timing arc prediction through machine-learning approach offer many advantages:
    History based cross check on arc contents reduces missing or incorrect entries.
    Suggestion based use case to assist cell owners decision making.
  - In-house “proof of concept” project of Machine-Learning based solution on arc existence prediction only.
  - Further collaborated with Empyrean to develop the additional capabilities in Qualib :
    Approach for incremental training.
    Predict arc attributes such as timing type, timing sense …
   Qualib is a Comprehensive Memory/IP/STD QA/Evaluation tool provided by Huada Empyrean Software Co., Ltd