## Slide 1: Data Analytics Engine For Design Area Analysis And Tracking
Akshay Barapatre

## Slide 2: Motivation / Challenges / Problem Statement
PPA data is historically not available for newly developed IPs. It is necessary to track design metrics for each IP through IP development phase as well as SoC implementation phase and make sure that we meet Cost of Build (CoB) estimate.
We run multiple experiments to decide correct PPA optimization strategy. This includes varying cell drive / Vt usage, power and area optimization knobs in tools, clock tree synthesis strategies, etc. Currently we don’t have a comprehensive tool/mechanism to track and compare design metrics from different runs across different stages.
We need a tool with following features to ease data analysis:
    Ease of configuration: All selection filters (Run, IP names, Stage) should be picked up from loaded data. Manual configuration shouldn’t be required.
    Ease of deployment: Process of deploying tool should be environment independent. It should have minimal or no dependency on external libraries/ scriptware.
    Ease of analyzing wide range of area information: User should be able to load area reports from multiple runs and its stages (synthesis, placement, CTS, etc). Tool should enable generation of comparison plots for selected runs/stages.
    Depth of data: Users should be able to deep dive into area trends for selected IPs/runs/stages with absolute and normalized plots.
    Ease of sharing: Dashboard should be easily integrated on webpage or shared over email.
    Design independent: Dashboard should be independent of process node, size and type of design.

## Slide 3: Proposed Solution: Methodology

## Slide 4: Proposed Solution: Methodology

## Slide 5: Proposed Solution: Tool Dashboard

## Slide 6: Proposed Solution: Use case-1
Low leakage power is USP for IoT devices. In an effort to reduce leakage power, it was proposed that always on logic (High Vt HVT cells) would be operating at $HVT_H Volts (High HVT voltage) in active mode and $HVT_L (Low HVT voltage) Volts in sleep mode. However frequency of operation would same in active as well as sleep mode.
Lowering voltage increases cell delay. Lowering operating voltage might lead to an area increase to meet performance.
Leakage power is directly proportional to standard cell area. Leakage power gain due to voltage reduction might be negated by standard cell area increase. It was critical to analyze area impact of $HVT_L to make a correct decision.
We ran experiments with both sleep mode enabled (HVT Voltage = $HVT_L) and disabled (HVT Voltage = $HVT_H). We loaded data from both runs in area analytics tool.
Area growth in HVT logic was around 2-3%. Leakage power due to voltage reduction outweighed increase due to area growth.

## Slide 7: Proposed Solution: Use-case 2
0 MHz synthesis area numbers are used as a baseline to quantify the impact of timing criticality on IP area. We identify top IPs with highest area growth and deep dive to understand its cause.
Memory controller IP saw an increase of 56% in total standard cell area. Memory controller was known to be timing critical, however its impact was identified only by comparison with 0MHz run. Drill down plots for it showed that combinational area was increasing by 100%.
Such an area analysis combined with timing analysis, led us to identify a particular design fix. Reduction in timing criticality due to this change is now expected to reduce combinational area increase to ~50% instead of existing 100%.

## Slide 8: Summary / Conclusions
Conclusions:
  Data analytics tool described in this presentation is currently deployed in synthesis flow.
  Data analysis of experiments (with and without sleep mode enablement) done on interactive dashboard helped us conclude that enabling sleep mode optimization has acceptable (~2-3%) impact on Always-ON module area. This has led us to decide that targeted devices can operate at proposed lower voltage always on voltage in sleep mode.
  Interactive dashboard helped in quantifying area impact due to timing criticality in memory controller. Design change was driven to mitigate area growth and timing criticality.
Future scope: We plan to make below enhancements in future:
  Standard cell Vt profile plots.
  Standard cell drive strength profile plots.
  Power profiling.