## Slide 1: DETERMINING THE PREFERRED METHODOLOGY FOR TIMING ANALYSIS AND SIGNOFF ON MIXED SIGNAL DESIGNS IN FINFET TECHNOLOGY NODES
KRISHNAN SUKUMAR, AMD INDIA
HARIPRASAD TT, AMD INDIA
DAVID NEWMARK, AMD US

## Slide 2
MOTIVATION
A modern SoC includes a wide variety of mixed signal designs and memory arrays
Array macros are important components in the CPU subsystem
Multi voltage designs are a norm to meet the Power target
Clocking and Power management units are becoming complex to get the best Perf/Watt
SerDes along with General Purpose I/O are also important elements in the modern SoC
In order to meet ‘PPA’ (Power-Performance-Area) targets, a significant portion of the design effort is spent on timing analysis and closure
So, for mixed signal designs, choice of Timing methodology plays an important role
Notes: A design must meet all the timing constraints to function at the intended clock rate while ensuring power targets are met.
In the design cycle of an IP, design changes, power and area optimization along with timing analysis go concurrently.
In such a scenario coming up the right methodology for timing analysis of an IP is in itself challenging and this problem has become more complex at FinFET technology nodes. Timing is therefore a crucial aspect of the design cycle.

## Slide 3
MAIN IDEA
Need of the hour is to come up with the preferred timing methodology for different designs
Facilitates efficient timing closure of various blocks and thereby for the top-level macro
Cell-based STA | Transistor-based STA
Higher capacity | Higher accuracy of timing (closer to H-Spice)
Faster turnaround time for reasonable size of design | No pre-characterization of cells required
Provides good ECO and debug features (size_cell/swap_cell) for timing and power closure | Layout optimization like sharing active across logic cells will not hinder timing flow
Better Variation modeling | No need of black box extraction, can work with flat extracted netlist
Multi Mode Multi Corner (MMMC) analysis and closure possible | Easy to create timing .lib/.db for extra PVT corners as pre-characterization of cells are not required
Notes: We mainly look at the Cell-based and Transistor-based Static Timing Analysis methodologies.
For different types of designs, we determine which of these two is suitable, based on the salient features of each methodology and certain design parameters (mentioned in the following slides).

## Slide 4
Evidence – slide 1
Let us look at two types of designs, the ‘Clock Generator’ and the ‘Power Supply Monitor’, and also deduce the preferred timing methodology for these designs by considering various parameters
Both the designs go into the processor core which typically operates at high frequencies (about 3-5 GHz)
Designs 1 and 2 are both multi voltage, high frequency designs with a large number of critical timing paths, a large instance count and high effort needed to achieve PPA targets
Since the frequency target is a constant across corners, fixing setup/hold for one PVT corner can result in a hold/setup violation at another PVT corner
Fixing timing violations along with tight power budgets can call for last minute ECO fixes
Hence, cell-based STA is used for timing analysis and closure

## Slide 5
Evidence – slide 2
We will look at the results for the ‘Array macros’ and the ‘Refclk macros’ as well
Array macros are primarily used in the cache and consist of differential circuits, bit cells and other sequential circuits and Refclock macros are low frequency designs used in the Video Decoder and System Management Unit of the chip
Array macros (Design 3) have a large number of critical timing paths (>250), and a pretty high instance count (about 500)
They are designed to meet stringent PPA targets, which means critical paths need to be skewed and hence standard cells can’t always be used
Refclock macros (Design 4) represent relatively smaller designs with fewer number of critical timing paths (about 10)
Both the designs are primarily composed of custom cells and hence accurate transistor analysis is required
Hence, transistor-based STA is used for timing analysis and closure
Notes: For the Refclock designs (Design 4), fixing setup violations is not a problem as operating frequencies are of a few hundred MHz and appropriate min delay buffers are used to close hold violations.
The timing methodology on these designs should verify that load and transitions are within the permissible limits.

## Slide 6: SUMMARY
PREFERRED METHODOLOGY SOLUTIONS
Enables ease of debugging failures on different IPs
Can also be easily adopted to a multi voltage scenario
SERVES AS A TEMPLATE
Selecting an appropriate methodology can be challenging
Proposed solutions provide a convenient and reusable template
VALUE ADDITION
Timing solutions can be deployed across the VLSI industry
Can be seamlessly used across IPs and technology nodes
ACCURACY AND
TURN AROUND TIME
Proposed timing solutions have enabled accurate timing analysis and closure
Enabled timely high quality IP releases thereby facilitating on time SoC tapeouts
CONFORMAL LEC
  Using the preferred timing methodologies has also enabled us to
    Efficiently handle the timing aspect of custom designs from
    3rd party IPs also
    Drive convergence across various design teams
PREFERRED TIMING METHODOLOGY
Notes: As we see, there are a plethora of benefits obtained by using the preferred timing methodologies for different designs.
Facilitating on time SoC tapeouts will ensure that the SoCs are in the market on time.

## Slide 7
  The information presented in this document is for informational purposes only and may contain technical inaccuracies, omissions and typographical errors. The information contained herein is subject to change and may be rendered inaccurate for many reasons, including but not limited to product and roadmap changes, component and motherboard version changes, new model and/or product releases, product differences between differing manufacturers, software changes, BIOS flashes, firmware upgrades, or the like. AMD assumes no obligation to update or otherwise correct or revise this information. However, AMD reserves the right to revise this information and to make changes from time to time to the content hereof without obligation of AMD to notify any person of such revisions or changes.
  AMD MAKES NO REPRESENTATIONS OR WARRANTIES WITH RESPECT TO THE CONTENTS HEREOF AND ASSUMES NO RESPONSIBILITY FOR ANY INACCURACIES, ERRORS OR OMISSIONS THAT MAY APPEAR IN THIS INFORMATION. AMD SPECIFICALLY DISCLAIMS ANY IMPLIED WARRANTIES OF MERCHANTABILITY OR FITNESS FOR ANY PARTICULAR PURPOSE. IN NO EVENT WILL AMD BE LIABLE TO ANY PERSON FOR ANY DIRECT, INDIRECT, SPECIAL OR OTHER CONSEQUENTIAL DAMAGES ARISING FROM THE USE OF ANY INFORMATION CONTAINED HEREIN, EVEN IF AMD IS EXPRESSLY ADVISED OF THE POSSIBILITY OF SUCH DAMAGES. ATTRIBUTION
  © 2019 Advanced Micro Devices, Inc. All rights reserved. AMD and the AMD Arrow logo and combinations thereof are trademarks of Advanced Micro Devices, Inc. in the United States and/or other jurisdictions. Other names are for informational purposes only and may be trademarks of their respective owners.