## Slide 1: Rapid IP and SOC Power Dissipation Analysis By Leveraging Emulation
Hojin Jo
Jaewon Jeon
Hyeongjin Kim
Hyunjae Woo
Changjun choi
Youngsik Kim
Seonil Brian Choi
Samsung Electronics Co., LTD.

## Slide 2: Motivation
Requirements for IP and SOC power aware designs
  To predict accurate power estimation to correlate with a silicon to have an appropriate power specification, using real world applications is required
  To identify weak or hot spots in a physical implementation to have robust design, measuring average power and detecting peak power events are required
Limitation of simulation based power estimation
  Real world applications are not used for power estimation due to significantly long simulation
    Simulating Graphics benchmark Egypt_f1759 is expected to run 6 months
    * Long simulation
SAIF
FSDB
Power
Analysis Tool
Average Power
Benchmark
Simulation
(with dump)
Power Optimize
Low Power Implementation

## Slide 3: Main Ideas
Step 1: Fast power estimation flow with emulation (without SDF)
  Extract a large number of cycles of raw switching activities with emulation for real applications
  Estimate power consumption based on zero delay emulation
  The proposed flow has 3000x speedup compared to simulation based power estimation
Step 2: Power correlation flow with silicon (with SDF)
  Identify candidate peak regions and perform SDF aware simulation to correlate with a silicon
Prepared Data
Emulation
(with dump)
Post
Processing
SAIF
WTC(NTC)
Search Peak Region
Power estimation
Average Power
Peak Power
WTC(NTC) Search Peak Region
Post
Processing
SAIF
(Peak region)
FSDB
(Peak region)
FSDB
Re-simulation with SDF
Physical Verification
Predict Silicon Power
* Faster flow than simulation base * Only toggle count data = NTC, Toggle count data with weight table = WTC
* SDF: Standard Delay Format

## Slide 4: Evidence: Proposed Power Aware Design Flow (Step 1)
Search peak power regions rapidly
  Search peak power periods using emulation with weighted toggle counts (WTC), which provides rough estimation
  Achieve a plot similar to real power consumption based on the toggle using Liberty power characterization
  Identify weak designs regions in pre-silicon
  10x speedup compared to simulation
    7days(inaccurate result) -> 17 hours(accurate result)
Estimate accurate peak power consumption
  Generate SAIF and FSDB to have accurate power estimation
  Calculate power consumption with power estimation tool (PT-PX) and Liberty Design Kit
Previously unable to search the peak power regions from simulation based power estimation
* NTC, WTC and Power ratio correlation graph
* Emulation and Silicon correlation graph

## Slide 5: Evidence: Proposed Power Aware Design Flow (Step 2)
“Glitch” aware power estimation
  To increase power estimation accuracy compared to actual power consumption in silicon, “Glitch” is required to consider
  Re-simulate the peak regions with intermediate status information in FSDB which are identified and generated from Step 1
  During re-simulation, SDF (Standard Delay Format) is utilized to consider the power consumption caused by glitches. It can also search time periods when a sudden current surge (IR-Drop or Dynamic Voltage Drop) may cause design instability.
Be able to predict an appropriate power envelop and architect robust power networks before a tape-out
Prepared DB
* Verilog file
* FSDB
* SDF
(Standard Delay Format)
FSDB Re-simulator
Generate FSDB with SDF
Peak Power
with Glitch
Physical Verification
Adjust
Physical ECO
Predict
Silicon Power

## Slide 6: Summary
Developed fast power estimation flow
  Enabled accurate peak power and average power estimation along with real world benchmark suites, which was not possible in simulation based power estimation
  Achieved fast power estimation by leveraging emulation in power aware design flow in a pre-silicon stage
Enabled early design decisions related power information in Pre-Silicon
  Developed a glitch aware power estimation flow assisted by emulation
  Predicted an appropriate power specification such as PMIC requirements
  Enabled to architect robust power networks