## Slide 1: Early LVS Paradigm Shift to LVS with Novel Methodology LVS – Signoff Layout vs Schematic
Authors : Karthik Kodakandla, MuraliMohan Thota
Company : Texas Instruments

## Slide 2: Motivation
In the current low nanometers’ era, where design & manufacturing complexities are multifold, it is very imperative for physical designers to plan & execute efficiently to curb exhaustive mode of final stage closure & to meet ever reducing design schedules.
Of all the Design signoff closures, physical verification aspects like Design Rule Check(DRC), Layout vs Schematic(LVS) are vital manufacturability & functionality checks respectively, any early assessment, analysis, feedback on these can bring significant change to design cycle times.
In Industry, LVS is the last targeted item owing to
  difficulty in assessing & addressing complicated LVS issues/results in early stages with design issues,
  Complexity of current flow owing to shorts/opens in the designs & Ips in development stage.
These complexities increase exponentially with the design size, design type (mixed signal) with multiple IPs, custom-signals, power-domains. Hence,
i. Can we reduce effort during final stages wrt LVS closure ?
ii. Rather than just a closure aspect, can we use it to for early feedback during design stages ?
iii. Can the signoff closures be made more easier ?
Addressing these can help not just in quicker closure but also ensuring time for other checks to close qualitatively.
In this paper, we present a novel LVS flow/methodology which helps in assessing multiple design aspects like power-grid & custom-routing sanctity, cell-placement & IP correctness in early-stages, also indirectly helping in quicker ESD & mixed-signal spacing checks, IO ring correctness while overriding above complexities.

## Slide 3: Proposed Solution
LVS, in literal sense, just checks for logical to physical correctness i.e., even incorrect/incomplete logical connections with exact incorrect/incomplete physical data is correct with checks’ characteristics. Has nothing to do with sanctity check of functionality.
The same principle along with divide & conquer approach is the essence of the Early LVS flow.
With this flow, complete routed SOC layout can be reduced to placed design containing only power-grid & no signal routing in layout (no logical & physical connection of signals).
Now the flow checks for correctness on power-grid only, thus dividing & enabling to close power grid, IO, core placement & signal routing separately.
Above concept provides us the ability to start the LVS flow on power-routed placed layout in early stages of design avoiding late setbacks or feedbacks.
Most importantly, this flow brings in significant change to signoff layout closure of complex designs with multiple mixed signal IPs, power-domains, incomplete IPs, new platforms, tight schedules.

## Slide 4: Flow Explanation across design stages
.
Early LVS flow enables us to start assessing power-grid, IO, Core-placement & signal routes separately.
Placed design can be starting point, wherein design contains floorplan with IOring, IPs, Core-cells placed, Power & custom routed with appropriate logical, physical connections.
Corresponding Schematic netlist contains all logical connections including signals but layout contains signals in trial route/incomplete stage-which wouldn’t match with schematic. Hence, netlist needs modification.
For us to assess power-grid, signal nets have to be removed from layout & schematic netlist. Similarly, based on data to assess, layout & schematic need to be modified. If IPs are incomplete, they can be black-boxed. Snippet for regular netlist to reduced netlist. Signals pins are removed, only power pins are retained.
In next stages, we can start looking at signal routes. In the initial routed DBs, there would be many signal shorts/opens. These can be bypassed by removing layout & schematic connections that have issues & continue with LVS.
By end of this stage, all the issues get resolved, leaving only few shorts/opens to be assessed at the final stage.
In this stage, Complete power-grid, cell & IO placement can be
checked for LVS correctness (without signal connections).
This can be repeated till we freeze Floorplan, power-routing.
Starts with higher count of violations, eventually reduces.
Cell_name Instance_name (
.a (x1), .b(x2), .y(y),
.VDD (VDD),
.VSS (VSS))
Cell_name Instance_name (
.VDD (VDD),
.VSS (VSS))
By final stage, all the issues are already resolved, leaving behind with rerunning the flow for final signoff.
This flow helps not just in catching IP or grid issues early, but also indirectly ensures smoother final stage, which eventually enables designers work on other final-stage closures.

## Slide 5: Early LVS Flow across Design Stages
IO RING
Power-routed
Placed Design
First Routed DB
with Signal routes
Floorplan/Power-grid Stage
Routing Stage
Final Stage
Generate Reduced Netlist
(Removing nets logically and physically)
Black-boxing Incomplete IPs
Power-grid shorts/opens fixed
Base DRC through pseudo filler
GDSII to LEF issues
Power-grid logical, physical corrections
Violations
(High count)
Shorts/ Opens/ anyother
Nets in concern – Logical & physical removal
Violations (Moderate count)
Final Stage
Routed DBs
Fixes &
Feedback
No Black Box
Correct Config file options
No violations
IO, Power & Custom grid,
baseDRC, corrections
Cleaner IO layout
power/custom grid
Cleaner signal
Connectivity
Signal conn.
corrections
Clean, Predictable
& no iterations
Signal nets not routed
Early Feedback
Fixes

## Slide 6: Issues resolved with the flow
a. Direct Benefits :
With Early flow on placed design :
  lef to gdsii issues : Custom-Decap had .lef to .laff mismatches. PLUS & MINUS were opposite amongst these files.
  DVR issues : IP DVR issues were highlighted, which were present on floating node.
  Incomplete IPs : Few modules were not final, hence black-boxing helped by-pass these during analysis. Need not wait till final releases.
Flow on complete SOC layout :
  Verilog to gdsii issues : Few IPs had ports with [] in verilog vs () in .gdsii.
  Floating gate violations wrt new IP ports : Few ports requires connections on both the ports of same pin-name.
b. Indirect Benefits :
  Shorts on the power-grid may not be directly evident from the Innovus/PnR (these can be due to improper OBS/blockages or markers due to dummy shorts with blockages) or anyother extraction tool.
  Power network based LVS makes it easier to catch these as it shows violations related to the instances it connects.
  Mixed-Signal Voltage Spacing (MSVS) violations’ count in the preliminary stages can be high due to any such shorts & would be difficult to trace as the violations propagate to all instances connected to these nets.
  ESD checks need early assessment wrt shorts/opens for quicker closure of ESD peer submissions enabling early layout feedback.
  Overall, this flow helped in resolving LVS issues by pre-final stages, easing power-grid, ESD, MSVS checks’ closures.

## Slide 7: Summary
With conventional LVS, designers can only run on complete SOC layout & towards last stage of pre-final or final stages, wherein a designer has to spend stipulated time in already existing tight final stages.
Conventional flow has just been a closure aspect & never used to provide early feedback during design stages.
Early LVS is altogether a new & novel, technology independent methodology that enables designers run LVS at any state of design & close strategically, making signoff easier & smoother.
Flow has been able to provide feedback to power-grid & PnR designers with base DRC corrections, shorts, MSVS violations’ cleaning, which eventually helped in closing LVS within two days of receiving first routed DB on RTL frozen netlist & all backend checks within 1 week.
Most importantly, this strategic & generic (adaptable) flows bring in significant change to signoff layout closure of complex designs with multiple mixed signal IPs/blocks, power-domains, new platforms, tight schedules.