## Slide 1: Systematic Power Routing Strategy To Meet Design Reliability Target for Ultra-Low Power SoCs
Apurve Chawda, Vivek Joshi, Subhadeep Ghosh, Venkatraman Ramakrishnan

## Slide 2: Motivation / Challenges / Problem Statement
Motivation:
  Standard EM practice is based on only individual metal leads checks based on Javg threshold.
  This does not consider aggregate reliability of all SoC leads.
  The design failure rate should be measured across different SoC elements.
  For low power designs with multiple power domains, the number of power/ground nets at the top level increases with multiple primary domains.
Challenges:
  Predictable power grid closure for SoC EM reliability.
  Effective resource utilization of multiple top level nets because of multiple always on domains and corresponding nets.
  Unpredictable secondary routing resistances resulting with pg-pin based signal routing of secondary nets.
  Difficult ECO implementation of secondary power routed cells late in the cycle in congested areas.
Robust SoC Powergrid for safety critical and high reliability design
Comprehensive SoC power grid design methodology for EM reliability requirement
Power grid design for complex mixed signal SoCs with multiple power and voltage domains
Optimal resource allocation for multiple power and ground nets at top layers
Handling of secondary power routing of secondary routed cells to get predictable resistances with low variance
IP level power grid hookup requirements for reliability constraints

## Slide 3: Proposed Solution – Analytical and Coherent Powergrid Design
Analytical power grid design for SoC EM reliability
Reliability-aware IP integration at SoC
Detect all the memories present in the design based on the power pin
Group memories that are close to each other based on user specified value
Draw power grid structure for the continuous pins of each memory grouping
Add power routes for non-continuous pins of each grouping
Memory power pins require fixed interval tapping to meet the memory internal reliability constraint.
A floorplan independent localized grid connecting top layers is made on top of memory pins
  Floorplan independent grid eliminates any manual intervention with any floorplan change
Power hookup of other IPs are done according to individual IP’s reliability constraints
Notes: Remove metal and power switch  elements or components

## Slide 4: Proposed Solution – Secondary Routing and Switch Expansion
Net wise utilization is targeted for the test case based on the current loading of each net
  More than 5 types of power/ground nets are routed in the top layers.
  VDD1 supporting majority of domains is given more resources in comparison to VDD2.
  VDD3 is given minimal resources as it is required only for special cells. It is locally routed only on top of special cell columns.
Top-Via is distributed into more frequent smaller vias to ensure frequent tapping to lower layers.
  Via distribution helps in lower resistances in the lower layers resulting in IR drop improvement by over 50% in the lower layers
Secondary Power Routing
Identification of the dominant secondary net and percentage usage of secondary power routed cells for each power domain
Row site creation at regular intervals based on the percentage of secondary routed cells for each domain
Pre-routing of dominant net connecting standard cell rails on the created row site for each power domain
Other class of secondary routed cells (minority ones) are pg-pin signal routed for each power domain
Optimum Top Layer Resource Allocation
METn
Top Layer
VDD3 routing on top of special cells

## Slide 5
FIT of every component below a threshold value ‘y’ is ignored.
The FIT assessment of every component is done and bottlenecks are identified.
The average current density and the current distribution of the bottlenecks is varied to reach an acceptable FIT value.
Results / Analysis
EM FIT Based Power Grid Design
Secondary Power Routing
Lower resistances and narrower spread for pre routed secondary pg nets.
Predictable resistances resulting in better current distribution is seen with pre-routed secondary pg pins independent of PnR iterations.
No pg pin routing required in ECO cycle with pre-routed secondary pg nets.
Optimum Resource Allocation
Proposed Solution
Prior Art
Resistance
Count
A better top-via distribution is achieved by varying the top metal layer width.
Using smaller top-via resulted in frequent tapping to the lower layers.
Resistances in the high resistive lower layers improved by frequent tapping.
The IR drop in the critical lower layer improves by over 50% because of the frequent tapping.
Lower resistance also help in overall reliability improvement.

## Slide 6: Summary / Conclusions
The proposed solution considers the overall SoC EM reliability instead of single metal lead’s EM threshold
The correct by construction solution helps in significant cycle time reduction over earlier iterative and reactive refinement of the power grid methodology.
This solution enables floorplan independent power grid creation for integrated IPs based on the IP EM compliant integration spec.
The current loading wise top layer resource allocation and optimization against the earlier methodology of equal resource distribution helps in improving the IR drop in all the metal layers.
The predictable secondary power routing resistances through an optimized row site creation helps in power grid robustness in comparison to the previous unpredictable pg-pin signal routing solution.
The pre-routed secondary power routing solution helps in ease of secondary power routed cells’ ECO implementation which becomes cumbersome with the earlier pg-pin signal routing solution in congested areas.