## Slide 1
An Effective Method to Accelerate Timing ECO for Large Scale Hierarchical DVFS Design
Jincheng Wang (Jincheng.Wang@unisoc.com) Xiao Yong(yongxiao@empyrean.com.cn) Jianlin Li (lijl@empyrean.com.cn) Senhua Dong (dongsh@empyrean.com.cn)
Introduction
For the DVFS design, designers will encounter critical interface timing violations at top level due to more voltage combinations. It has to run flatten ECO to consider the SI/transition effects inside system level.
While, the increasing SoC design scale (over 100M instances) and timing signoff scenarios under advanced technology will bring massive design and timing data.
The capacity of ECO tools becomes to the main bottleneck of top level timing eco. It takes designer so much time and effort to fix the left critical timing violations manually.
An effective method to extend the capacity of ECO tools is necessary for designer to accelerate the automatic flatten timing ECO in top level.
Challenges for DVFS Design
Top Level ECO Based On Condensed Timing Data
Condensed Timing Data Extraction
Instead of processing all STA timing, we propose a method to extract condensed timing data from STA and do top level timing ECO based on it.
1. For scenarios using same corners, merge timing reports to one scenario.
2. For merged scenarios, extract global slacks of setup and hold violation related points; extract RC parasitic of setup/hold violation related nets.
Successful Story
Conclusions
Due to the capacity limitation of EDA tools, the massive design and timing data is one of the biggest challenge to top level timing ECO for large scale hierarchical DVFS design with multiple scenarios.
We proposed an effective method to extract condensed timing data from STA, then according to the data, used ICExplorer-XTop to do top level timing ECO. From the results, it can greatly save the time without accuracy loss.
12nm, 50M instances, 32 scenarios
The proposed ECO flow will include:
1. Run top level flatten STA
2. Extract condensed timing data from top level flatten STA
3. Import condensed timing data and top design data into ICExplorer-XTop
4. Timing eco and export ECO commands
5. Start another ECO iteration
Based on the condensed timing data eco flow, we also did some experiments on the memory saving (Pro mode).
Under same hardware resource, it can support 60 scenarios to cover more violations and keep more margins.
Memory Saving
MCMM ECO Flow
Partial STA graph with violations only
Whole STA graph
Customized MCMM ECO Flow
Top Flatten Signoff STA
Top Flatten Design Data
ICExplorer-XTop
Timing ECO
ECO Commands
Condensed Timing Data
Next Iteration
 |  | Traditional ECO | Condensed timing data based ECO
Run Time | Run STA | 8 h | 8 h
 | Write timing data | - | 50 min
 | Timing ECO | > 24 h | 3.3 h
 | 1 iteration total | 1.5 day | 12.5 h (↓60%)
Hold Violations |  | 2849  1200 | 2849  287
7nm, 140M instances, 16 scenarios
 | Traditional ECO | Condensed timing data based ECO
Run Time | N/A | 18.2 h
Hold Violations | N/A | 10425  1023
The customized method can finish top level timing ECO of 100M+ instance design within 1 day, while the traditional timing ECO solution cannot handle it at all.
The run time of top level timing ECO iteration has reduced 60%, from 1.5 days to ~12 hours.
Benefit from only saving the necessary timing information on the related pins, Pro mode can achieve +20% reduction in memory usage and faster run time.
Chart: 
| 20 sce | 40 sce | 60 sce
Normal | 430 | 680 | 860
Pro | 370 | 520 | 650
Chart: 
| 20 sce | 40 sce | 60 sce
Normal | 260 | 380 | 780
Pro | 220 | 310 | 350
Memory (G)
Run Time (min)
Booth:
#651