## Slide 1
Machine Learning Techniques for minimizing PVT Corner Analyses and Library Validation
By: Prateek Pendyala, Akash Hegde, Suryansh Sahota
[prateek.pendyala,suryansh.sahota]@intel.com, akashh@andrew.cmu.edu
Traditional timing signoff tools rely on design analysis at a number of extreme PVT corners to address impact of static and dynamic voltage variations.
Tool-based timing closures are not realistic: either too pessimistic or optimistic, not yielding the true maximum delay of the circuit elements.
Any incremental library characterization for a new PVT corner requirement, has a turnaround time of several weeks.
Competitive production schedules of IPs/SoCs limit the accuracy of characterized library files, thus compromising their reliability.
2. This work proposes a flow which leverages machine learning (ANN), to validate existing libraries & obtain accurate characterization results at new PVT corners “instantly”, after training.
Existing characterized libraries are sampled for timing & power metrics as per output capacitance and input slew for all cells, to build ML models, for prediction at new corners.
Can be implemented on both, NLDM (Non Linear Delay Model) as well as CCS (Composite Current Scaling) libraries.
Characterization errors in libraries, appear to the user as a high deviation w.r.t predicted value from the model.
3. Artificial Neural Network as Prediction Model
For each cell, neural network models are trained by minimizing the error function, where x is the input features, w is the weights and is the target timing (cell_fall/rise) or power (cell_fall/rise) metrics and is the total number of library data points used for training.
To evaluate the effectiveness of the trained network, we measure , normalizing gives, , and calculate correlation factor, for all samples.
4. Performance Results of Prediction Model & Comparison with Golden Library Data
Cell delay prediction at new voltage corner with 𝐍𝒆𝒖𝒓𝒐𝒏𝒔∊{𝟐𝟒,𝟒𝟖,𝟗𝟔,𝟏𝟗𝟐} gives an NRMS error & correlation of 4% and 0.99, respectively.
Internal power prediction at new voltage corner with 𝐍𝒆𝒖𝒓𝒐𝒏𝒔∊{𝟏𝟐,𝟐𝟒,𝟗𝟔,𝟏𝟗𝟐} gives an NRMS error & correlation of 6.1% and 0.95, respectively.