## Slide 1
A Low-Power Triple-Vdd Dual-Core Motion Estimation Chip Design and
Implementation for a Wireless Panoramic Endoscopy
Abstract
Jian-Lin Zeng1, Tsung-Yi Wu 2 and Ching-Hwa Cheng1 (chengch@fcu.edu.tw)
1Dept. of Electronics Engineering, Feng Chia University
2Dept. of Electronics Engineering, National Changhua University of Education
In this paper, a low-power motion estimation chip is proposed for a wireless panoramic endoscope system. This design consists of the motion estimation system and is implemented by a Hierarchy Dual-Vdd design technique. There are two parts to the architecture of the motion estimation chip. The first part is the one-dimensional processing element array for calculating the absolute differences. The second part is the adder tree that is used for computing the sum of the absolute differences. On the proposed Hierarchy Dual-Vdd technique, the circuit was separated into three voltage domains by using clustered voltage scaling. The high voltage maintains the performance of the circuit and the low voltage reduces the power consumption. The effective technique is decreasing the power consumption without reducing the performance of the chip. From the full-function chip’s measurements, the dual voltage core can reduce the power consumption by 20%~30% in different clock frequencies.
Medical care advancement has enhanced the level of technology, especially in minimally invasive surgery. Fig. 1 shows a scene of minimally invasive surgery (MIS) [1]. MIS prefer their patient’s surgical wounds to be smaller, and patient feels more comfortable after surgery. However, the MIS surgeon’s visualization is limited as use single-lenses endoscope. Meanwhile, the inconvenient vision angle due to improper VGA screen’s locations. This shortcoming can be improved if surgical vision area can be expanded and free. Hence, this research proposed VGA display system is wirelessly and can be portable closed to patient’s body. The surgeon’s vision then can be naturally follow up their hand’s operations. A wireless panoramic endoscope (WPE) system was developed to be applied in MIS as shown in Fig. 2. The WPE has two lenses, as without video and power cables, the VGA screen is easily movable to a convenient vision location. However, the battery usage duration becomes a major challenge of the WPE as long-time examination requirement. The other issue of WPE’s temperature needs to be well controlled as closed to patient’s organs. Hence, WPE requires low power consumption.
Introduction
We propose a hardware design for the motion estimation used in video compression applications. the WPE power consumption can be well deduced for designing a low-power ME. The design architecture has a conventional adder tree or a Divide-and-Conquer adder tree that is used to compute the sum of absolute difference (SAD). Because a Divide-and-Conquer adder tree can reduce the computing time of the circuit, using it can improve the circuit performance. The accumulator and the SAD contrast device are shown in Fig. 3, 4. We then use the divide-and-conquer adding tree to calculate the sum of the absolute differences obtained from the conventional adder. In our architecture of motion estimation, there are conventional and divide-and-conquer adders.
Figure. 1. The scenes of skewed vision in MIS. [1]
A low-power and high-compression video encoder design is included in WPE. This paper focuses an effective video motion estimation mechanism is adopted within video encoder for saving transmission power. The proposed wireless panoramic endoscope system is shown in Fig. 2. The wireless panoramic endoscope system has two cameras, an encoder, a transmission system, and a computer with a video stitching system. However, the battery has a short life because operating the wireless endoscope consumes a lot of power. The transmission efficiency is limited by the bandwidth. It takes a lot of power consumption to transmit data when the data isn’t compressed. Therefore, image compression is necessary.
(a) A scene of MIS. (b) The proposed wireless endoscope.
Figure 2. The proposed wireless panoramic endoscope system for minimally invasive surgery.
(a)
(b)
Figure 2.
Motion Estimation Chip Design
The designed circuit gate-level synthesized by using TSMC130nm and 180nm technologies, the Prime-Power. The circuit logic synthesis result is shown in Table 1. The experimental results show that our proposed architecture can process 931 frames per second for the CIF format. This architecture also can process 45.5 frames per second for the HDTV video resolution.
Table 1. The designed circuit logic synthesis results
Clustered voltage scaling is an effective technique in reducing power consumption. On the low-power design technique, the ME chip has separated into three voltage domains by using the Hierarchy Dual Vdd (HDual-Vdd) clustered voltage scaling technique. The high voltage maintains the performance of the circuit while using the low voltage reduces the power consumption. The effective techniques in reducing the power consumption without reducing the performance of the circuit. We separated the circuit into two voltage domains by using clustered voltage scaling. The high voltage maintains the performance of the circuit, and the low voltage reduces the power consumption, as shown in Fig. 5.
Proposed Hierarchy Dual-Vdd CAD Tool
Step1: We make the decision tree by finding out all the modules from the RTL.
  Figure 5. A schematic diagram of clustered voltage scaling technique.
Step2: Find all the critical modules from the timing path report, which has a minimum slack time.
Step3: Find the brothers module from the other modules, which belongs to the high voltage domain that is highly relevant to the critical modules.
Step4: Place the critical modules and their brother modules into the high voltage domain, and place the other modules into the low voltage domain.
Figure 6. The proposed HDual-Vdd low-power design flow.
Figure 7. HDual-Vdd design tool (a) the original design (b) build decision tree from design hierarchy (c) hierarchy transformation
Figure 8. In-path critical-module is shown by gate-level circuit.
Figure 9. Four operating relations of brother-module
Fig 3. Schematic diagram of finding out the images contextual association
Fig. 3. Processing Element
Fig. 4. The architecture of the motion estimation circuit
Triple Voltage ME Chip Design
The low-power dual-core motion estimation chip, the chip’s structure is shown in Fig. 10. The dual-core ME design voltage-domain are separately into three major portions, the high-voltage (VDD-HIGH) and low-voltage (VDD-LOW) for dual-core ME core. The VGA output display module is put in a specific region, and without need to be processed by HDualVdd.
Fig. 10. Dual-Core ME Chip Architecture
Fig. 11. Dual-Core ME performance and power analysis
Fig. 12. Triple-Vdd chip’s performance and power analysis
Fig. 13. Back-end process in physical design stage of this chip.
Chip Measurements & Verifications
Fig. 14. (a) Voltage domain assignment of target chip.
(b) Die’s photo taken from a microscope.
Fig. 15. Chip works in BIST mode
Fig. 16. The fully chip function verification
The dual-voltage design can reduce power consumption by 30% when compared with the high-voltage design. And 20% reduction when compared with the low-voltage design as shown in Fig. 17.
Conclusions
We describe the whole process using the clustered voltage scaling technique to achieve the low power consumption. From the proposed low-power motion estimation chip, the dual voltage core can reduce the power consumption by 20%~30% in different clock frequencies. A wireless endoscopy can be developed based on this technology. The proposed technique extends the battery life while optimizing the image quality. The system integration will be validated by an endoscope system using the proposed low-power video compression technology
Fig. 17. Power reduction compared with the high- & low-voltage