## Slide 1
A Smart RTL Linting Tool with Auto-Correction
Khaled Salah, Ph.D.
Technical Lead at Emulation Division
Khaled_mohamed@mentor.com
56th Design Automation Conference, 2019.

## Slide 2: Motivation
2
Linting is a type of static code analysis, used to grub and detect any suspicious construction and problematic patterns in software/Hardware codes.
Due to increasing the complexity in modern circuit design and consequently in RTL code, linting becomes an initial stage in the complete line of the formal verification techniques.
Conventional linting tools produce reports for the issues that don't comply with specific code guidelines. These reports have a large numbers of errors and warnings which have to be solved and handled manually.
In this work, we propose a linting tool with an auto correction capability for some errors and warnings at RTL level such as timing violation problems and mismatch between simulation and synthesis. This can speedup the verification process.
The tool is built using Python. It has been tested on OpenCore certificated projects and it provides short execution time.

## Slide 3: Main idea: The Handled Issues1
3
Issue | How the tool works | An example
Incomplete sensitive list | Detects each always. Then, predicts the signals that have to be assigned in sensitive list of combinational blocks. Finally, compares them with the actual signals assigned in the list. In case of the mismatch, tool replaces sensitivity list signals by an asterisk (*). | 
Unused/Underived signals/ports | It Checks the declared ports and signals if they are assigned to any blocking/non-blocking (<=/=) assignment, any condition or any sensitivity list. In the case of the non-assignment signal/port to at least once to any logic value, it removes automatically anything related to that signal/port. | 
Missed statements such as (else) or Non-full case | It introduces a fast detector to if statements with missed else statement precisely. It introduces a fast detector to incomplete case statement precisely. | 

## Slide 4: Main idea: The Handled Issues2
4
Issue | How the tool works | An example
Timing violation by Glitch transition | Instantiating library specific ICG (Integrated Clock Gating) cells called through specific modules | 
Before Linting
After Linting

## Slide 5: Evidence1
5
The proposed tool has been implemented using python with an easy graphical user interface (GUI) as shown in the Figure below.
Its input file is modified in a new created file and it reports the position of each detected issues as shown in the Figure below.

## Slide 6: Evidence2
6
Issues | Selected files | # of lines | # of detected/ corrected items | Execution time (Sec)
Latches missed default | Ethmac | 399 | 1 | 0.01
 | reed_solomon_decoder | 869 | 1 | 0.0156
Latches missed else | ecg | 1227 | 8 | 0.07
 | sdcard_mass_storage_ controller | 1207 | 32 | 0.04
 | sockit_owm | 419 | 25 | 0.02
 | uart2bus | 667 | 15 | 0.03
Unused signals/ ports | rx_enqueue | 875 | 4 | 0.0312
 | tx_dequeue | 976 | 4 | 0.035
Each issue has been tested based on OpenCore's certification projects codes as shown in the below table where it shows the short execution time of linting.

## Slide 7
Thanks