## Slide 1: Improve Hardware Assurance (HwA) using FPGA IP in your ASICs and SoCs
DAC 2019

## Slide 2: Hardware Assurance is Critical for ASICs and SoCs
Everyone has their own reason
  Creating components for defense
  Creating component for critical infrastructure
  Protecting the valuable IP of the company
  Protecting the revenue stream of the company from counterfeits
  . . .
But the challenges are the same
  Fraudulent Products: Cloning, Counterfeiting, re-cycling, overproduction
  Malicious Insertion: logic bombs, Trojan kill switches, back doors
  Tampering: reverse engineering, side-channel scanning
  Emerging Threats: new security attacks, new side-channel attacks, new vulnerability exploits

## Slide 3: Motivation 1/2
Critical Hardware Failures Leading to Security Breaches
  Spectre and Meltdown: Spectre and Meltdown are a trio of variations on a speculative execution vulnerability that affects nearly every microprocessor-based chip manufactured in the last 20 years. The fundamental vulnerability exists at the hardware level and cannot be patched although there are software workarounds. But these workarounds hurt performance. The flaws are so fundamental and widespread that security researchers are calling them catastrophic. If exploited, attackers can get access to data previously considered completely protected.
Critical Loss of Public Communications Services
  Paradise fire: The Santa Clara County Central Fire Protection District says a communications vehicle it dispatched to the Mendocino Complex, the largest wildfire in California’s history, was rendered essentially useless after Verizon reduced data speeds to a fraction of what firefighters needed. In this case, the loss of public communications was not the result of a security breach, but it easily could have been.

## Slide 4: Motivation 2/2
Critical Security Failures
  Mirai botnet caper: Internet service in the northeastern US was nearly shut down in October, 2016 through a DDoS (distributed denial of service) attack. Mirai malware turns networked Linux devices into remotely controlled “bots” by identifying vulnerable IoT devices, breaking into them, and infecting them with malware. In this particular example, infected IoT hosts included printers, IP cameras, residential gateways, and baby monitors. The resulting DDoS attack shut down more than 70 major Web sites including Airbnb, Amazon, CNN, Comcast, DirectTV, github, HBO, Netflix, Starbucks, Twitter, Verizon, and Yelp.
Creepy Security Failures
  Video baby monitor hacks: While capable of operating on the public internet, baby monitors are almost never intended to be reachable externally. However, researchers from security consultancy Rapid7 found seven devices were susceptible to straightforward attacks, “trivial” to any competent hacker. There have been multiple hacking attacks on baby monitors in recent years. In 2013 and 2014, it appears the same man had found a way to hurl abuse at babies and their parents through Foscam baby monitors.

## Slide 5: FPGA IP for Hardware Assurance
Cortex-A75
Private L2
DynamIQ Shared Unit
Shared L3 Cache
ACP
Agile System Cache
Cortex-A55
Private L2
TCZ TrustZone Controller
DDR Controller
MMU
PCI Express
100G Ethernet
SATA
DDR Controller
MMU
MMU
CoreLink CMN
Speedcore eFPGA IP
FPGA IP is a block of reconfigurable logic that can be configured to implement any datapath
Minimize exposure of critical IP by loading it into FPGA block of the chip at the end of supply chain
FPGA IP allows security engineers to adapt their system designs to changing security landscapes

## Slide 6: FPGA IP Minimizes Exposure in Supply Chain
FPGAs excel at dealing with HwA risks because of the concept of “chain of trust” or “chain of security”
FPGA IP considerably shortening the length of the supply chain exposed to key IP
FPGA IP compartmentalizes the design, reducing the number of fingers and hands touching the key IP
Reduces the risk of fraudulent products
Core Design Team
SOC Integration
Backend Design
Masks
Chip Foundry
Test and Packaging
Board Assembly
Shipping and Storage
Deployment or Customer
Key IP mapped to eFPGA
Key IP
Chip
In house
Out Sourced

## Slide 7: FPGA IP to Thwart Reverse Engineering
ASIC and SoC designs that instantiate critical design elements in on-chip FPGA IP are more secure and fundamentally harder to reverse engineer than hardware designs built from gates and wires
Critical design IP literally does not exist on the chip until the FPGA IP block authenticates and decrypts the bitstream (design) and loads it into the configuration memory
Critical IP can be added later, even after the devices are in the field—sometimes years after, which means that large sections of the manufacturing and supply chain will never come into contact with these critical IP blocks, even in their encrypted form
SRAM-based FPGA IP also naturally provides protection against physical attacks – As soon as the device is powered down, the datapath is lost and the design effectively ceases to exist in that device

## Slide 8: FPGA IP to Thwart Malicious Insertion
Regular structure of FPGA IP makes Malicious Insertion harder
Any additional circuits will stand out in tightly packed regular structure
The location of logic and data routing of key IP is not known so the attacker does not know where to place Trojan
Placing Trojan in every cell blows up the area of the block
For further protection multiple instantiations of the same design can be created so that there are different but equivalent versions to make attacking harder

## Slide 9: FPGA IP for Adapting to Emerging Threats
ASIC and SoC designs that incorporate FPGA IP can be upgraded for many purposes including security
New attacks can be deflected by adding or modifying an IP block specifically designed against the new attack
Protocols can be updated if vulnerabilities are exposed
Side-channel attacks can be deflected by changing the algorithm implementation
For further protection multiple instantiations of the same design can be created so that there are different but equivalent versions to make attacking harder

## Slide 10: FPGA IP for Additional Hardware Resilience
In addition to traditional security issues, reconfigurability provides a mechanism to address other issues
Quality Escape – The introduction of product defects, deficiencies, vulnerabilities, or product inadequacies either by mistake or through negligence during the design, production, or post-production handling of a device or system that degrades the product's performance at any time over its entire life cycle
Reliability Failure – Mission failure in the field caused by environmental factors, possibly factors that are unique to military and aerospace environments, such as particle strikes, device aging, hot-spots, and numerous other hazards

## Slide 11: Securely Loading Bitstream into Embedded FPGA
Embedded FPGA must be ultra-secure if they are going to hold the critical IP
Strong encryption of bitstreams (designs) to protect the IP
Strong authentication to only load bitstreams (designs) signed by trusted source
Trusted key store based on Physically Unclonable Functions
Embedded FPGA supplier can provide bitstream security integrated in the eFPGA IP block or SoC developer can use their own hardware root of trust and security architecture

## Slide 12: Authors
Raymond Nijssen VP of Systems Engineering raymond@achronix.com
Quinn Jacobson Strategic Architect quinnjacobson@achronix.com
Steve Mensor VP of Marketing steve.mensor@achronix.com