## Slide 1: STA compatible Netlist CDC Methodology
Ulhas Kotha, nVidia India Pvt. Ltd.
Pratik P Suthar, nVidia India Pvt. Ltd.
Ravindra Nibandhe, Synopsys India Pvt. Ltd.
Ankush Bagotra, Synopsys Inc.
NVIDIA CONFIDENTIAL

## Slide 2: Why Netlist CDC is Critical for nVidia Now? Motivation for Netlist CDC
NVIDIA CONFIDENTIAL
Tool Requirements
Ability to consume 1Bn gates + Netlist
Ability to reuse existing PrimeTime based STA flow Setup
Ensure PT Compatibility
Attribute & Collection based reporting
Comprehensive CDC Verification
Setup, Synchronization, Convergence, Integrity, Power Aware CDC Checks
Design Team’s Challenges
External ASIC, Netlist IPs
Access to only Netlist
CDC mandatory for vendor and SoC sign-off
Advanced DFT and Low Power Insertion in Netlist
Script base Low Power Cells insertion
Complex DFT Logic in Netlist
ECO and Hand Instantiated Netlists
Significant design changes near tape out
Derivative Design spin-off from netlist
Hand instantiated data path for High Speed Designs
Merging of multiple flops
Growing Design Complexities
Tool & Flow Expectations
Notes: This slide talks about Design team’s challenges, Growing design complexities and expectations from EDA

## Slide 3: Limitations with STA based CDC analysis
Missing constraint support for CDC
Convergence Issue
Paths across Asynchronous clocks are not reported by PT
For asynchronous untimed paths, glitches can cause meta-stability
NVIDIA CONFIDENTIAL
clk_A
D1
clk_B
X
F1
F3
F2
clk_A
D2
clk_B
A
F6
F8
F7
clk_B
D1
D2
X
Y
01
01
11
10
10
10
10
01
Other challenges:
No noise reduction leading to high designer review time
No segregation of violations according to type of path
Runtime
No waiver application/backtracking inside the tool
clk_A
A
clk_B
C
clk_A
D
clk_B
A
F1
F2
Quasi-static signal – No synchronizer required
Notes: This slide talks about limitations/challenges with conventional STA based CDC analysis.

## Slide 4: VC SpyGlass Netlist CDC Flow
Netlist Read
CDC Setup - Constraints
Netlist CDC Analysis
Debug
(Interactive TCL)
NVIDIA CONFIDENTIAL
PT Setup
CDC Checks
Data Sync, Convergence, Glitch, Redundant Sync identification
Reports & Debug
infer_cdc_crossings to generate and analyze crossings
write_cdc_paths with synchronization details to match PT unsync crossings
report_cdc command to report Crossings/Glitch/Convergence issues in single report under specific tags
read_file –netlist –top $design
source ./$design.tcl
check_cdc –type setup/sync/struct
Debug
(Interactive TCL)
Notes: This slide explains VC flow as well as guides that each stage is relevant/correlates with PT.

## Slide 5: CDC Issues found in the Netlist Flow
SETUP_CLOCK_GLITCH: Glitch prone clock path (other than ICG).
CDC_COMBCONV_FVUNCHECKED: Same domain synchronized signals converging on combinational gate.
SYNCCDC_UNSYNC_NOSCHEME: Crossings involving clock as source point.
ASYNCRST_UNSYNC_NOSCHEME: Reset not synchronized using methodology compliant synchronizer cell.
NVIDIA CONFIDENTIAL

## Slide 6: Case Study Results & Summary
NVIDIA CONFIDENTIAL
Design Complexity
Graphics SoC Netlist with 6 sub systems
Design size ~1.5 billion instances
1647 asynchronous clocks
Correlation with PrimeTime
~99.99% correlation with clock pins, crossing and constants
CDC Analysis
Full flat run for CDC analysis
143 million CDC crossings
CDC data sync detection :127 million synchronized crossings
Clock glitch analysis – 1.8 million glitch prone signals in design
Summary
VC SpyGlass CDC reuses the existing PrimeTime based STA flow setup and constraints with a strong correlation of clocks, constants, and crossings with PrimeTime
Compared to conventional STA flow, Netlist CDC flow with VC SpyGlass CDC helped us to increase coverage with additional checks for synchronization, convergence, and glitch
Notes: This slide has details of GA100 performance and numbers for crossings/glitch analysis.