## Slide 1: A novel methodology for Fast PDN sign-off by slicing long-vectors
Udayakumar Yedakuppam (Infineon Technologies)
Soenke Grimpen (Infineon Technologies)
Dileesh Jostin (Ansys)
Manali Khare (Ansys)

## Slide 2: Motivation
Long vector simulation has become increasingly common in automotive domain to stress all parts of a chip to ensure a robust grid
Vectors are made available late in the design cycle and turn around time is high, resulting in very few use case scenarios being analyzed
Traditional sign-off tools demand machines with large memories ; shortage of resources during tape-out phase forces to take a conservative approach resulting in non-optimal power mesh
In the present work we introduce a methodology to overcome the longer TAT for such simulations using RedHawk-Seascape. We also show how big data analytics can be used to create actionable outcomes for PDN optimization and improve design performance.

## Slide 3: Slice VCD and do multiple parallel simulations
Slicing
Single VCD File
Sliced VCD(1) simulation
Sliced VCD(2) simulation
Sliced VCD(3) simulation
Sliced VCD(n) simulation
Parallel Runs
Vector split into smaller segments and simulation carried out on each of them parallelly
Take advantage of the Big-data Elastic-Compute architecture which allows to run big designs on regular CPU cores spread across compute-farm (no need to reserve huge machines)
Gives huge performance benefit, especially when the VCD duration is long
Increased coverage enabling multiple patterns to be analyzed with short TAT
Potential to eliminate slices with low coverage in terms of switching activity and impact to design performance

## Slide 4: How to select the simulation window ?
Simulation window (500ns) is identified by cycle selection based on power consumption from a vector of few microseconds
  For RedHawk-SC run this was inherited from RedHawk cycle selection
  RedHawk-SC is being enhanced to do this natively
Scenario scoring
  In addition to power based cycle selection, other metrics like grid resistance, static drops, timing margins etc. can be used to score the vector
t
. . . . . . . .
Powers of each cycle
The cycle with worst power is selected
Activity Profile – Full VCD
Selection of Top N Windows purely
based on activity
Grid Criticality
Scenario Scoring
Timing Criticality
Selection of top 1 window based on
different metric weightages
Power

## Slide 5: Using big-data analytics to stitch results
  Concept of guard-band is introduced to create overlap at the slice boundaries to enable accurate stitching
  Stitching methodology is built using the APIs that allow deep access to the simulation database
  Functions are created to generate combined heatmaps and waveforms from time sliced simulations results
Instance IR
HeatMap
Waveforms
Simulation(1)
Results Stitching
Simulation(2)
Simulation(3)
Simulation(n)

## Slide 6: Why to add guard band ?
Presim Time
Dynamic simulations with package require settling time to initialize capacitor charge and inductor current
  Allow LC oscillations to exponentially decay (called presim time)
  Traditionally this is determined by couple of initial dynamic runs, thereafter remains fixed for rest of the simulations
  For this chip presim time was identified as 50ns

## Slide 7: How to select slicing time for long vectors (500ns) ?
Number of slices can be decided by user depending on the compute resources available
  For a design which takes 10 workers for dynamic simulation, we can have the following configurations
    5 slices of 100ns => 50 workers (5x speed up compared to single slice run)
    10 slices of 50ns => 100 workers (10x speed-up with double the resources)
  Resources vs Time trade-off
Each slice will have to accommodate the presim time resulting in simulation overhead
  For cases discussed in previous point the performance gain will be 3.7x, 5.5x respectively
Chart: 
| 0 | 5 | 10
Y-Values | 0 | 5 | 10
Y-Values2 | 0 | 3.6667 | 5.5
#Slices
Relative speedup
With presim

## Slide 8: Slicing : Quality of Results
3 slices run Inst DvD heatmap
2 slices run Inst DvD heatmap
Worst Instance DvD heatmaps match well between 3 slices and 2 slices runs
Good dynamic drop correlation :
99.27% instances show drop difference < 2mV
3 slices v/s 2 slices drops scatter plot and histogram

## Slide 9: Evidence : Correlation and Performance gains
RHSC with Time Slicing is 4.4x faster than RedHawk
Dynamic results are correlating well with traditional tool : 99.95% instances show difference < 5 mV
 | RedHawk | RedHawk-SC (10 slices)
Technology / Design size | 40nm/ ~ 7 million instances | 
Vector duration | 500ns | 
Simulation time step | 20 ps | 
Run (wall) time till simulation | 4 hours | 3 hours
Simulation run (wall) time | 58 hours | 11 hours
Total run (wall) time | 62 hours | 14 hours

## Slide 10: Summary
Proposed and demonstrated a methodology to analyze long vectors and optimize PDN
Results available in hours compared to traditional approaches while meeting the accuracy criteria
Enables multiple sign-off runs without impacting tape-out schedule
Future work
Combine multiple functional vectors to increase coverage
Select best scenarios using machine learning algorithms
Explore methodologies for feedback to timing engine
Explore approaches for speed up
    Moving pre-simulation starting point to dc average value of the demand current
    Relaxing timestep during pre-simulation period