## Slide 1: A Method to Build Clock Tree Comprehending Switching Activity to Address DVD in an SOC
Authors : Atul Garg, Venkatraman R
Company : Texas Instruments

## Slide 2: Problem Statement
Meeting dynamic voltage (IR) drop (DVD) goals in designs has become challenging with the complexity of the power-grid, and power-management
  Conventional low-skew (balanced) clock trees aggravate the simultaneous switching scenarios, hence increasing DVD
Usual approaches to handle DVD like placing additional decaps, drawing thick power network grid etc. may not be desirable due to the leakage power and routing/area overheads
We use a method to optimally stagger the switching of sequential cells comprehending toggle-activity on them in a timing-aware fashion to reduce dynamic-IR drop without impacting design timing performance
  The proposed method uses ILP to identify optimal skew scheduling
  Solution seamlessly integrated and assessed using conventional EDA solutions
The focus of defining clock skews is on the clock anchor points (CAPs) that exist in the design
  CAPs can be invariant points in the clock tree like registers, module boundaries, muxes used for timing mode selection, etc

## Slide 3
CAP | Toggle Density | Possible Scheduling for CAP based on slacks |  |  | Not desirable | Not Desirable | Desirable | Desirable
 |  | Max delay schedule | Default | Max early schedule | Schedule | Schedule | Schedule | Schedule
I | 10 | +3 | 0 | -1 | +3 | -1 | -1 | +3
J | 40 | +2 | 0 | -2 | +2 | -1 | 0 | -1
K | 80 | +3 | 0 | -2 | +3 | -2 | -2 | 0
L | 100 | +3 | 0 | -2 | +3 | -2 | +3 | -2
Desirable scheduling scenarios are where the switching is staggered over a wide range
Clock Scheduling Comprehending Toggle Density
For a clock timing graph (as shown in the figure):
Collect slacks on INi (input) & OUTi (output) of ALL CAPs
Define range of schedule possible for each CAP as the range between Min{INi} and Min {OUTi}
Quantise the allowed/possible skew range for the design considering all CAPs and design constraints into specific buckets of schedule points
Use Integer Linear Programming to maximise the schedule assignment at each bucket (i.e. maximise spread) while minimising the total toggle in each bucket
Scheduling with uniform toggle activity - Illustration

## Slide 4: Results: Design Information & Basic Parameters
We used the proposed method on a 800K instance, 100K register-count 65nm design.
We derived skew schedules with an allowed skew of 800ps (+/-400ps), with a resolution of 200ps
  Allowed skew buckets (schedule points) = 5
  Run time for LP to generate skew intent is about 10 mins
Design was optimised and analysed for IR-drops with and without these skew schedules in Cadence® tools
  Conventional clock skews allowed during CTS = 100ps (design constraint)
Basic timing parameters were similar or better with the proposed skew schedules
Timing Parameters | Default Method | Proposed Method | Comments
WNS/TNS/FEP (2 setup views) | 0.98ns/192ns/1149 | 0.97ns/30ns/375 | Better Timing
WNS/TNS/FEP (3 hold views) | 5ns/12ns/25 | 5n/13n/44 | Similar Timing
Area Density | 56.035% | 56.125% | Negligible impact

## Slide 5: Results: Clock Tree Delay Profiles
Clocks at Registers
Clocks at Registers
CTS - Default Method
CTS - Proposed Method
Clock tree synthesis is done with and without the proposed skew schedule
The distribution of clock arrivals on registers is seen to be correspondingly spread-out
  ~900ps clock skew with the proposed schedule achieved
Negligible clock area increase (<<1%) is seen in CTS
Clock scheduling intent achieved without impacting basic design Quality of Results (QoR) parameters of timing, area and power

## Slide 6
Results: Dynamic IR-drop & Peak Currents
Total instances with DVD more than ~55mV are decreased from 26% to 11% with proposed method
Dynamic Peak Current is also decreased from 676mA to 546mA with proposed method
We also see a reduced number of dynamic IR-drop hot-spots with an improved spatial distribution
The approach results in overall improved dynamic IR-drop and peak currents
CTS - Default Method
CTS - Proposed Method
Peak current = 676mA
Peak current = 546mA