## Slide 1
IC designers face increasingly complex IP and time-to-market pressure. They demand accurate and consistent design information between different views of the IP (RTL, documentation, IP-XACT). Missing or erroneous information in IP-XACT files or documentation can cause expensive delays and re-spins. Proving equivalence between design views is time consuming and error prone. Traditional simulation methods are not well suited for this. As directed tests require verification engineer to think of potential problems and write test cases to catch them . This presentation shows how formal methodology solved the consistency problem. Formal Register Verification (FRV) application automatically generates assertions from IP-XACT and document spreadsheet and proves equivalence against the RTL design. Formal Connectivity Checking(FCC) application generates assertion based source, destination and enable signals.
Abstract
Solving IP Quality Challenges in Complex IP
Models tested using traditional verification methods
Solving IP Quality Challenges in Complex IP
Kalyani Challa
Synopsys Inc., Mountain View, CA
DAC 2019
Solving Test Mux Consistency Check with FCC
FCC Use Flow
FCC Results
FRV Use Flow
FRV Results
Formal methodology enabled comprehensive validation ensuring accurate and consistent design information between RTL, Documentation, and IP-XACT views of the IP
Achieved high confidence and saved time compared to simulation. Released IP to customer in shorter time.
Formal found corner case bugs that would be difficult or impossible to find in simulation
Does not require knowledge of potential sources of mismatches
  Formal tool automatically generates assertions from IP-XACT files and connectivity tables
  Formal tool exhaustively proves equivalence and provides counter examples for mismatches
  Formal methods enabled high confidence quality within tight time constraints.
Conclusion
Solving IP-XACT Consistency Check with FRV