## Slide 1
With the increased complexity of Intel Client SoC design,
  the hierarchical reset architecture has become very complex
  increase in reset signaling complexity with the emergence of multiple reset domains
  create new verification challenges that aren’t addressable by RTL simulations.
Because of the different flavors of IPs
  independent “reset domains” can be created by complex reset sequences or reset structures
  metastability and reconvergence issues similar to the failures seen in asynchronous CDC.
  tangible need to provide automated, exhaustive structural and functional reset signaling checks.
Abstract
4. Asynchronous wrongly connected to data without synchronizer
5a. Reset crossing to flop with no Reset port
First Implementation of exhaustive reset verification done on PCIE Subsystem for Client SoC
Additional checks improved the Quality Sign Off
Bugs Uncovered after reset verification
  Wrong Reset Propagation
  Power Control logic interpreted as Reset
  Reset is always active high
  2nd Flop with no set/reset pin
  Reset wrongly used as reset pin
  Set to Set domain crossing not synchronized
  Set to Reset domain crossing not synchronized
  Combinational Logic in reset path
  Async reset used in sync mode
Rohit Kumar Sinha, Intel India
Enabling Exhaustive Reset Verification in Intel Design
6. Data crossing reset domains
Reset Tree Evaluation
  Power On Reset, Watchdog Timeout reset
  Debug reset, Software reset, and Loss of Clock reset.
  Construction Issues
Reset Domain Crossing
  Application of resets- Sync/Async Behaviour
  Same reset used as both sync/async in a single module leading to synth vs sim mismatches
  Combinational Logic in Reset Path
Reset Convergence & Reconvergence
  Reset splitting and converging
  Reset bus synchronizers reconverging
Reset tree
rst
clk
conv_rst
rst
Exhaustive Reset Verification
Summary: Bugs found due to exhaustive reset verification in PCIE Subsystem
  1. RESET combo glitch: This could lead to a glitch in the reset path due to combo logic
5b. Same reset port with side_input and multiple resets
  2. RESET convergence Issue appears when reset get split and converge
split
reconverge
  3.RESET is always active HIGH
active high
Reset domain 1
Reset domain 2
Evidence: Additional Metastability Risk Uncovered
Partition | #Cell Count | Number of SIPs | Number of HIPs
aux_logic | 2577 | 7 | 0
Fabric | 3108 | 13 | 0
PHY | 3696 | 9 | 5(clock compensator, phy, clock control unit)
Controller | 17554 | 16 | 18(HIPs)
Comparison on the reset coverage