## Slide 1: Hybrid Configurable Platform for HW&SW Co-development and Co-validation
Hyunjae Woo
Youngsik Kim
Seonil Brian Choi
Samsung Electronics Co., LTD.

## Slide 2: Motivation
Related Works
  Pure SoC Emulation
    It is 1000 times faster than simulation
    But it is not fast enough to develop SW on OS
    Because it takes about 12 hours to boot-up Android
  Hybrid SoC Emulation
    CPU and Memory are virtualized to accelerate
    It is 15 times faster than Pure SoC Emulation and takes about 50 min to boot Android
SW development is on hold until full SoC is ready
Hard to find complex bugs in an early stage of development
Not enough time to fix bugs discovered in real Apps on OS
  As the IP developers perspective both HW and SW
    Too Late to co-development, co-validation and co-verification.
    Waste time to debug other IPs which are not interested, such as DPU, Audio and ISP.
Not enough time

## Slide 3: Main Idea
Introduction
  IP Hybrid Configuration Platform.
    IP development with real software on OS
    Easy to setup : Integrating an interesting IP with ready-to-use configurable platform
    Easy to focus on IP in system level validation
Focusing on Target IP
  Verified QEMU based on Common OS system
  Only put Target IP and related memory sub-system at emulator
    Saving Time to debug other IPs
    Saving emulator capacity
    Saving compilation time
    Fast boot up because all other IPs
    are allocated at the Virtual side

## Slide 4: Validation Platform
GPU IP Development
  Starting with verified QEMU Platform
  Just add IP Target IP, GPU HW, FW and Driver to the platform
  HW&SW co-validation through Running real Benchmarks and Apps
Notes: The Target IP has own firmware to control Job Managements, KMD(Kernel Mode Driver) and UMD(User Mode Driver)

## Slide 5: Evidence
Notes:   The result images are captured from QEMU-hdlcd, The screen resolution is 640x480
  It takes around 10min reached Android home screen

## Slide 6: Summary
  Becoming de facto IP level platform for an early SW development
  - Let IP develop to focus on IP itself by virtualizing the rest of SOC system
  Slim and time efficient platform for IP development
  Reached Android Homescreen in 10 minutes (5x faster than Hybrid SoC emulation)
  Ran GFXBenchmark Manhattan 1080p at 1~2 min/1-frame rendering
  Enabled SW/HW co-verification in Pre-silicon
  SW development at pre-silicon stage for firmware, Kernel mode driver and User Mode Driver for IP
  Functional validation at pre-silicon stage with real application
  Discovered various bugs among HW, Kernel Mode Driver and User Mode Driver at pre-silicon stage