## Slide 1: Pin FMEA of TPS65313 device using analog fault simulation
Tulong Yang[1], Vijay Kumar Sankaran[2], Chanakya K V[1], Ayesha Chowdhury[1], Tahsin Alim[1], Samir Camdzic[1], Sumit Kumar[1], Amit Bajaj[2], Victor Zhuk[2]
[1]Texas Instruments [2]Cadence Design Systems

## Slide 2: Background & motivation (1/2)
Device/IC Pin Failure Modes and Effects Analysis (Pin FMEA) is an integral part of designs targeting mission critical applications
  automotive, industrial, defense, aerospace to name a few
Quantifiable analysis is performed considering device/IC internal failure modes (package and bond wire related) and failure modes external to device/IC (pin soldering and EVM interconnect related)
  factors such as severity, likelihood and detectability of the failures used to calculate Risk Priority Number (RPN) to assess the risk associated with defined failure modes
Traditionally performed by manually introducing defects or faults at the device boundary pins
  manual faults insertion may not comprehend the defect universe, as well as time consuming
  no control on simulation performance optimization in terms of inserting faults at a required time interval
  automated analog fault generation and simulation techniques
In addition, automated analog fault generation and simulation could be extended to support validation of different device/IC level safety analyses
  Fault Tree Analysis (FTA) and Dependent Failure Analysis (DFA)
  failure Modes, Effects and Diagnostic Analysis (FMEDA) and Design Failure Mode and Effect Analysis (DFMEA)

## Slide 3: Background & motivation (2/2)
Pin FMEA verification is required for all automotive products in safety applications per ISO 26262
  Existing methods of Pin-FMEA verification is complicated and the setup is time consuming
Verification evidence has to be collected for external audit and at times shared with major automotive customers
Example: For 64-pin device Pin FMEA, we need ~250 unique simulations and
~1.5 man-month worth of effort
1) Floating pins
2) Pin short to VDD
3) Pin short to VSS
4) Pin short to adjacent pin
Pin-FMEA Cases:
Total # of simulations:
4n-6 (VDD & VSS adjacent)
4n-7 (Otherwise)
Where n=number of device pins

## Slide 4: Prior work for Pin FMEA
Traditional method:
  Usually requires creating a new test bench for Pin FMEA
  Requires addition of switches for each pins and each adjacent pin on the test bench
  Requires 4n-7 number of define conditions that needs to be added to the test bench

## Slide 5: Proposed method: overview
Cadence tool (Legato) provides a transistor-level simulation capability that can be enabled in an analog test methodology to improve test coverage by identifying critical test patterns
We can utilize this tool to automate the verification on device level and use this for efficient Pin FMEA verification
Pin name(s) or net name(s) can be specified where the fault (open/short) will be injected automatically
Injected faults can be simulated in parallel to optimize the run time
Pass/Fail status can be extracted from the log file based on device specific safety goals
DUT
Fault Type | Parameter
Open | 1G Ω
Short | 10 mΩ
Pin-FMEA

## Slide 6: TPS65313 Pin FMEA case (1/4)
DUT
Test Bench
External Component
Driver
Checkers
Stimulus
Pin-FMEA Results
Fault List
Faults are injected automatically into the DUT netlist, bypassing the test bench
Does not require modification on existing test bench
Assert Violations
Checker Pass/Fail

## Slide 7: TPS65313 Pin FMEA case (2/4)
// PIN # 1 AVIN
FaultList_Shorts_1_0 faults resBridge=0.01 {
bridge {
FaultList_Shorts_1_0_bridge_1 ( simTopTestBench.VIN simTopTestBench.AVIN ) r=resBridge
}
}
FaultList_Shorts_1_1 faults resBridge=0.01 {
bridge {
FaultList_Shorts_1_1_bridge_1 ( simTopTestBench.AVIN simTopTestBench.VIN_SAFE )
}
}
`include fault_list.scs
MySweep sweep faults=[FaultList_Shorts_1_0 FaultList_Shorts_1_1 FaultList_Shorts_1_2]
{
tran tran stop=5m errpreset=moderate
}
Shorting VIN with AVIN
Sweep command to run multiple fault simulations at once. This example runs 3 fault simulations.
Bridge fault value

## Slide 8: TPS65313 Pin FMEA case (3/4)
Waveform of AVIN pin shorted to its adjacent VIN pin through 10 mΩ auto-inserted bridge/short fault
  expected behavior: no damage to DUT, device operational
10 mΩ
10 mΩ
VIN
AVIN

## Slide 9: TPS65313 Pin FMEA case (4/4)
Feature | Traditional | Using Analog Fault Injection
Total simulation | 150 | 150
Setup complexity | Complex | Simple
Effort estimate (40-pin) | 30 days | 1 day
# of test bench files | Variable | 2
Test case / tasks re-use | Yes | Yes
Compatibility | Manual | Any Test Bench
Test bench modification | Required | Not Required
UVM, ADEXL, AnalogLib, GUI, Command Line, SV, VAMS..

## Slide 10: Why this method?
Compatible with any Test Bench. Pure Spectre, AMS, UVM, Block level, Chip level.
Run Pin FMEA simulations seamlessly
Robust Solution. Requires Minimal-to-No scripting. Support by Cadence.
No Test Bench Switches Required
Existing Test Case, Tasks & Checkers can be re-used
Significantly Reduce Setup Time
Why this Method?
Why This Method?

## Slide 11: Summary (1/2)
Conclusion
  On TPS65313 device TI saved about 3 weeks effort using Cadence’s analog fault simulation tool compared to the traditional method
    Comprehensive fault list that accounts for the fault universe of the device
    Simplified setup with the number of simulations remaining the same as in traditional Pin FMEA methods
  Direct Fault Analysis using industry standard Spectre simulator
    Sweep analysis to inject faults independently on each pin and observe the effect
    Distributed fault simulations across multiple cores enables the regression
Results
  Setup and analysis effort is reduced compared to traditional methods
    30 days to 1 day for a 40-pin device
    Use the existing test bench to performance the simulation
    No additional switches and define conditions required for each pin
      Testbench reuse possible from functional verification maintaining compatibility

## Slide 12: Summary (2/2)
Limitations
  No pin location based automatic fault list generation using layout
    Needed to optimize fault list generation as we need to short only the adjacent pins and not all combinations of pins
  Restricted to using same set of asserts and checkers for all pin short faults
    Using different checkers for different shorts not so direct and pursuable
Future Scope from Cadence
  Potential expansion of analog fault simulation application to similar related analyses
    FTA, DFA, FMEDA and DFMEA
    Functional Safety Analysis