## Slide 1
Satish Kumar Dinavahi, Anukul Rangarajan — Qualcomm India Pvt Ltd Srinivas Velivala, Gurpreet Singh Lamba — Mentor, a Siemens Business
Faster Physical Verification Signoff Convergence in P&R using Calibre RealTime Digital
Challenges
Faster PV signoff closure at various exit points is critical to meeting SOC tapeout deadlines
At advanced nodes, DRC closure is increasingly iterative, and at times non-convergent
DRC-clean often requires immediate and interactive signoff DRC feedback on manual edits made in P&R
Current signoff DRC flow is not optimized for manual DRC fixing flow
P&R environment is more abstract, with only required layer information for IPs (P&R DRC flow cannot catch all signoff DRC errors)
The Calibre® RealTime Digital (RTD) interface delivers immediate signoff-quality DRC analysis in P&R during floorplanning and routing stages, enabling P&R engineers to achieve signoff DRC convergence, reducing both PV cycle time and computing resources.
Solution
Calibre signoff in P&R with Calibre RTD
Break the traditional flow of exiting P&R for signoff feedback
Achieve signoff DRC inside P&R environment
Calibre RTD features that help in-design fixing
  Custom DRC recipe creation
  Windows-based (300-500k polygons)
  IP GDS/OASIS merge
Calibre RTD DRC flow
Calibre Signoff DRC
Manual fixing
Calibre RealTime Digital
In-Design DRC
In-Design fixing
Place & Route Tool
GDSII
99% DRC clean
Value proposition
  Base checks in P&R
      Check new IPs for base violations and boundary conditions in P&R environment
      Last-minute base changes in design can be checked with high confidence
  Metal checks in P&R
    Interface DRC by reading IP or partition GDS enables faster closure of IP integration
    Window-based metal DRC validates fixes and catches new unintended DRC errors
    Identifies LEF vs GDS issues
  Identifies tech file limitations
Calibre RTD can use the metal geometries inside IPs for DRC and show the metal geometries in P&R during DRC debug
Fixing becomes very intuitive and engineers can instantly validate the fixes
For complex DRC rules, engineers get feedback within a few seconds compared to hours of standalone run
Saves at least 3-5 PV iterations during every critical milestone
Provides Calibre signoff confidence and convergence in P&R
Metal Interface DRC violation without and with the IP metal geometries seen in P&R
LEF VS GDSII mismatch. P&R DRC indicates no DRC violations, but Calibre RTD shows an actual DRC violation
Summary
Without Calibre RTD, typical DRC fixes for all the listed use-cases requires a Calibre DRC run with a TAT of 12-24 hours
PV fixes applied using the Calibre RTD interface help achieve signoff convergence inside the P&R environment
Reducing DRC closure cycles and using check recipes helps targeted layer/region-wide checking/fixing
Calibre RTD GDS/OASIS read ability expands DRC coverage to
  Base DRC validation in P&R environment
  IP/Memory/Std cell interface DRC
  LEF vs GDS mismatches
Calibre RealTime Digital
Innovus integration
Polygon count | Rules | Errors reported | Runtime (secs)
19230 | 864 (M1-M4) | 340 | 7.5
490000 | 864 (M1-M4) | 9905 | 102
173180 | 7870 (all checks) | 46490 | 131
39598712 | 864 (M1-M4) | 2136970 | 1194
Polygon count | Rules | Errors reported | Runtime (secs)
45834 | 839 (M1-M4) | 3115 | 15.82
434844 | 839 (M1-M4) | 3031 | 115.861
984722 | 839 (M1-M4) | 2828 | 287.021
2002487 | 839 (M1-M4) | 2419 | 588.928
1336441 | 1355 (M1-M8) | 3044 | 401.766
2002487 | 1355 (M1-M8) | 2436 | 585.909
1336441 | 1355 (M1-M8) | 1393 | 328.666
ICC2 integration