## Slide 1
PROBLEM STATEMENT
In the Client SoC world, IP designs are sourced from both internal and external channels and IP vendors often provide collaterals generated by multiple vendor tool. As a results, at the time of SoC Integration, SoC team faces multiple challenges in handling incompatible or non-consumable IP abstract model collaterals Therefore, to deal with such problem, there is a tangible requirement that SoC team develop a methodology which could support different flavors of CDC abstract collaterals such that the dependencies on IP designers are minimal while analyzing the asynchronous design issues.
HOW
In this paper, we will present the prominent challenges that we faced while implementing Hybrid Abstract Methodology wherein abstraction collaterals from multiple vendors are imported for the hierarchical CDC verification in the SoC
Abstract
Challenges: Implementation of Hybrid Hierarchical CDC Verification
Below is the comparison of the performance and the rules violation with three difference techniques of abstraction – 1. Flat CDC Verification 2. Selective Abstract Modeling 3. Full Abstract Modeling.
Rohit Kumar Sinha, Intel India
Hybrid methodology-An innovative methodology for hierarchical CDC Verification
HYBRID HIERARCHICAL METHODOLODY must be implemented with correct IP configuration
Top Vs Block constraints must be consistent
Clock Tree and Reset Tree must be validated using the baselines Flow
Automation of Abstract Constraints Translation must be validated thoroughly and all the issues with difference in the constraints interpretation must be addressed
Hybrid Methodology essentially means that SoC designs can consume the mixed abstract data collaterals generated by any industry standard cdc verification tool. Using hybrid methodology, CDC verification can be done with utmost quality and it eradicates the dependency on the IP vendor to provide the abstract model collaterals generated from SoC or Subsystem Compatible vendor tool. Therefore, the sign-off CDC tool flows need not necessarily be the one that was recommended from SoC design team but IP team or subsystem team are free to use any vendor tool for their CDC signoff in the bottom-up SoC CDC closure.
HYBRID METHODOLOGY
Results
Enabling Mixed and match CDC Hierarchical Verification
Automation to translate multiple vendor abstract modeling collateral
Ability to consume multiple vendor CDC abstract models
Step 1: Obtain the CDC Collaterals from IPs. Chose the baseline CDC flows based on the Top Level CDC Flow (Subsystem or SoC)
Step 2: Black Box the IPs whose CDC collaterals are not from the same from Baseline CDC Flows
Step 3: Translate through automation the IP’s CDC abstract model constraints into the baseline CDC flow format
Step 4: Selective abstraction for the subIPs which are not complex, such as globals
Evidence: Bottom Up SoC Hierarchical Hybrid Methodology
Main Idea: Implementation of Hybrid Hierarchical CDC Verification
IP1 (SIIP)
IP2 (HIP)
IP3 SIP External
IP4 Global IP
CDC verif. With Vendor1
CDC verif. With Vendor2
CDC verif with selective abstraction
CDC verif done flat at SoC level
SubSystem CDC Verification
Collateral file representations are different or ports are defined differently from vendor to vendor
Asynchronous clocks are interpreted differently
Interpretation of related ports concatenation to the same clock group name.
Multiple ports definition even with different clock grouping and Abstract port forming combo path to output ports
Abstract port bus width declarations behavior mismatches
Virtual clocks stamping for output ports interpretation is different in case of functional clock group name stamping.
Virtual clock definitions issues while porting into different too flows
PHY Logic
External Logic
Pcie controller
Custom Logic
Router
Primary Fabric Logic
Gasket
TEST CASE TO IMPLEMENT CDC HYBDRID HIEARCHICAL FLOW: 10 SIPs with cell count 400K & 18 HIPs
Hybrid Methodology Guidelines
Hybrid method must be implemented with the following guidelines-
correct IP configuration
    It is highly important to generate the abstract model using the correct configuration so that the correct intent of the IPs are captured and hence consumed at the higher level
Top Vs Block constraints must be consistent
    In the bottom-up approach, it is highly important to resolve all the parameters mismatches between block and Top-level
Clock Tree and Reset Tree must be validated using the baselines Flow
    One of the prerequisite to enable hybrid methodology to ensure that clock and reset are correctly propagated and domain are correctly defined using the respective tools
Constraints Validation
    Automation of Abstract Constraints Translation must be validated thoroughly and all the issues with difference in the constraints interpretation must be addressed
Subsystem
Partition1
IP1
#(2, 16)
IP2
#(3, 48)
Partition2
IP4
#(2, 24)
IP2
#(1, 16)
IP3
#(1, 4)
SoC Design
Transparent Hierarchical Data Model
Custom Hierarchial Data Model
Bbox the IP block
Translated the interface constraints into abstract model.
Generating the abstraction based on SoC Requirement
External IP1
Summary: Advantages
CDC Closure cycle reduced drastically by implementing Hybdrid Methodology
Automation to translate CDC constraints helps in faster closure
Major performance benefit and can be scalable for different SoC architectures
Selective Abstraction helps in early CDC closure for Mixed methodology
Verified IPs (RTL, configuration, constraints, waivers) are reused across projects
ADVANTAGE
Summary: Pitfalls
Constraints Interpretation is not consistent between vendor tools
Configuration for IP integration is different from configurations used for verification
Complex CDC schemes across hierarchical models are not being validated
Multiple Vendor CDC constraints must be well-understood for mixed methodology
Complex hierarchical blocks are not being modelled correctly. For sync cells must be validated
Mixed Methodology – collaterals(mainly constraints & waivers)) must be validated before importing
PITFALLS