## Slide 1: Power Grid Analysis For Huge Graphics Designs Using Big-Data Elastic-Compute Solution
Kanthi, Basavaraj J basavaraj.j.kanthi@intel.com , Intel Corp
Ananthanarayanan, Anand anand.ananthanarayanan@intel.com , Intel Corp
Farooq, Mohammed mohammed.farooq@intel.com , Intel Corp
Thota, Srinivas srinivas.thota@intel.com , Intel Corp
K, Harikrishnan harikrishnan.k@intel.com , Intel Corp

## Slide 2: Motivation
IR analysis of SOCs/IPs with >3B nodes consume significant compute, are debug intensive and have a long TAT
Distributed machine execution is currently used to run <4B node count designs and is limited by:
    Longer throughput for die IR convergence
    High compute usage
    Designer productivity in terms of viewing/debugging violations [interactive debug is extremely limiting]
    Cannot be run for more than 4 billion nodes
Elastic compute solution has the following benefits:
  Enables elastic compute and can scale to 100s of cores across machines
  Enables evaluation of multiple switching scenarios in Dynamic analysis
  Decreases turnaround time for any large designs.
  Open DB access allows creating custom API/heatmaps, data analytics.

## Slide 3: Elastic Compute Solution offerings
Multi-billion node handling:
  Faster run-times and better compute utilization.
Multi-cycle scenario:
  Increased coverage, more accurate analysis.
Open access:
  Allows creating custom API.
  User experience:
  Faster debug – increased execution efficiency.

## Slide 4: Result Comparison with existing sign-off tool – TAT and Compute
Machines
Time
Distributed  1632 core hours
tLaunch
tAnalysis
tDebug
256GBx16
256GBx16
…
256GBx16
256GBx16
256GBx16
…
256GBx16
256GBx16
256GBx16
…
256GBx16
3 hours
8.5 hours
48 hours
tAnalysis
tDebug
3 hours
48 hours
Elastic  348 core hours
1
2
…
16
Cores
1
120
Only 1 core needed to debug full chip results
Importing database < 1 minute
Time
3x TAT benefit
5x core-utilization benefit for run
192x core-utilization benefit for results review
Elastic compute soln
Notes: 3 flagship products moving to 3rd gen elastic compute architecture.

## Slide 5: Voltage drop maps comparison with sign-off tool
RH Node voltage map of m0
RH-SC Node voltage map of m0
Dynamic IR
Static IR
Elastic compute
Current sign-off tool
Elastic compute
Current sign-off tool

## Slide 6: Conclusions
Elastic compute solution enables power integrity analysis for huge designs with excellent TAT and memory scaling.
Access to database enables gathering detail data which assists in better power grid design and optimization.
Improves execution efficiency by reducing IR drop convergence time.