## Slide 1
Sandeep Torgal, Anand Kumaraswamy — GLOBALFOUNDRIES & Avera Semi Fady Fouad, Gurpreet Singh Lamba, Jeff Wilson — Mentor Graphics
Tackling the increasing challenge of IR drop & EM fails in advanced technologies with a push-button solution
Motivation
Power structure design is becoming more challenging with advanced technologies
Objective
Easy, automated flow to lower resistance
  Metal width pre-determined
  Best approach = insert additional vias
Challenges
Traditional custom scripts too complex and time-consuming
Different stacks, complex spacing rules, different enclosures, via count per width…
  Direct impact on reliability and yield
  Increasing resistance from narrower metals
Push-button solution: PowerVia
Analyze design, extract user-defined nets per connectivity
Identify candidate locations for via insertions
Calibre® YieldEnhancer tool adds DRC/LVS-clean vias at these locations
  Use foundry inputs to determine “valid” insertions
Different net types can be targeted
Output can be OASIS/GDS or incremental DEF format
Multiple custom options:
  Skip fixes on selected requirements (e.g., shield lines)
  Analog-specific features (controlled edits on metals)
  Can use custom flow to link to CDL (netlist)
  Priority selection of specific via type (large, bar, small)
Results
The blocks went through manual intervention to add as many vias as possible before the PowerVia flow was available.
The “#vias added” results are over and above the manual insertions
There is significant via addition even at final stage, and a ~5-10% improvement in EMIR results using the PowerVia flow
Mentor (add’l feedback from other customers):
Adding more vias using the PowerVia flow on power nets showed a reduction in current density violations count up to 68%
Summary
Enable switching between via types
User-customization on ratio of via types to be used
“Via patterns” insertion
Shield Nets skip
 | Size (sq.um) | ∑ vias added | #vias added (via1, via2, … via10)
Block #1 | 4400 | 7162 | 0, 0, 1761, 1958, 735, 430, 304, 1841, 133, 0
Block #2 | 1500 | 2057 | 0, 0, 88, 418, 86, 306, 438, 701, 18, 2
Block #3 | 12600 | 9494 | 0, 0, 0, 6398, 696, 480, 480, 1440, 0, 0
Future Scope
PowerVia automation flow targets DRC/LVS-clean via insertion to reduce IR and EM issues
PowerVia flow is a push-button solution that works with different foundries (incl. TSMC, Samsung, GF) and different technology nodes
  Rules come from foundry, identification is by Calibre® nmDRC™ tool, insertion is by Calibre® YieldEnhancer tool
PowerVia flow is a utility inside Calibre tree
  Customers can select foundry and metal stack
Flow can be run at IP/macro/memory/chip - any level and any stage of the design
Limitation: In hierarchical EM-IR flows, design teams must enforce running PowerVia at each hierarchy
Max via insertion
On Differential Nets
Increase design reliability
Reduce IR drop
Calibre platform
Connectivity-based extraction
GLOBALFOUNDRIES
stack/specs/DRC rules
Calibre YieldEnhancer
DRC/LVS correct by construction via insertion
PowerVia flow
output: via DB
CORE ENGINE
Net extraction/via addition rules are automatically generated controlled by stack definition
Input DB
GDS/OAS
Techlib.tcl
Config data
User controls
Technology-specific info
Layer stack definition
Net extraction rules
Via addition
PWR/GND intersection extract by NET
Power Via addition process
Single/stack
Output via DB GDS/OAS
Layer Map
Drawn layer definitions
VIA Variables
Via size, enclosure, spacing, etc…
Text Layers
Connectivity definitions
Input: editable by user
Input: technology files provided to user
input: input DB
DRC run for validation