## Slide 1: SOC System Bus Performance Monitors (SPMs)
Samsung Electronics
Hyungtae Park
Seunghyun Song
Jisu Yang
Hyunsun Ahn
Seonil Brian Choi
Synopsys
Sihyun Kim
Namho Heo

## Slide 2: Motivation
SOC Performance Verification
  Ensure SOC level performance running multimedia content thru Image system, Display system, Video codec, Image scaler, etc.
  Require an emulation based solution to overcome slow simulation for the multi-frame with high-resolution image content.
  Measure performance between bus interfaces (AMBA bus ports) and memory controllers
Limitations
  Complexity of SOC bus fabric is extremely increasing with several hundreds of IP’s and multiple layers
  Traditionally performance is monitored at bus masters (or only from a source) which prevents from analyzing performance such as theirs bottlenecks and QoS of intermediate bus layers
Require better system bus performance analysis with intermediate performance monitors
Notes: Convert Samsung specific terms to generic ones such as TEXI, TRAX

## Slide 3: Main Idea #1: Develop SPMs Supporting Multi-Protocols
Enabling performance analysis supporting various standard and internal bus protocols
  System level performance is measured with standard buses (AMBA AXI/ACE) and internal buses to meet target latencies and throughputs
  Developed System Bus Performance Monitors (SPMs) for a master and a slave AXI, modified ACE and internal bus protocols
Building a bus performance analysis configuration is automated
  SPMs for each protocols are automatically integrated to a node in a system bus with a multiple layers where performance is required to monitor.

## Slide 4: Main Idea #2: Monitoring Simultaneous Traffics
Monitoring matrix (multi-masters) based traffic patterns
  Simultaneous traffics from multiple masters are propagated to every node of a bus fabric in a matrix format.
  The traffic patterns are generated such that an information on a destination address can identify the source of the traffic from a master
  The number of performance monitors (#SPM) are the number of nodes in a bus fabric and layers (N) * the number of masters (M).
  Post-processing is conducted after collecting performance data from all SPMs to measure latencies, throughputs, and multiple outstanding traffics (MO)
M0.pm
M1.pm

## Slide 5: Performance Analysis with SPM
Latency, throughput, and multiple outstanding traffic count are measured and analyzed for each bus layer (See Figure).
Latency
  The number of clock cycles from a master to a destination thru each bus layer are measured.
  Average and peak latencies are analyzed to optimize an idle latency when a single master is used and to detect QoS congestion or bottleneck when multiple masters are used
Multiple Outstanding Traffic Count (MO)
  Max MO is analyzed to detect if a design spec is met to support multiple simultaneous traffics within a given throughput requirement
Throughput
  Throughput inefficiency such as dummy traffics is detected, which occurs by a bus fabric to compensate bus width mismatch or meet a burst size for a memory controller

## Slide 6: Summary
SOC bus fabric becomes complex
  Performance analysis requires a significant amount of time and expertise.
Developed System bus performance monitors
  Covered various bus protocol monitors (AMBA AXI and internal bus protocols )
  Conducted Matrix-based performance diagnosis
Performed more advanced system bus analysis
  Able to analyze an idle latency in a system bus using a single master
  Identified average and peak latencies and multiple outstanding traffic numbers to find traffic congestion.
Future works
  Developing performance big data analysis system
  Applying to a mobile SOC project
Notes: Remove all schedules