## Slide 1: Synthetic Traffic Based Performance Verification (STB-PV)
Samsung Electronics
Seunghyun Song
Hyungtae Park
Hyunsun Ahn
Seonil Brian Choi
Synopsys
Sihyun Kim
Namho Heo

## Slide 2: Motivation #1
Introduce SOC Performance Verification
  SOC level performance analysis with multimedia content thru camera system, display system, audio system, video codec, etc.
  There are a number of multimedia IPs to generate traffic into the system bus.
For SOC Performance Verification
  Bus fabric
  Multimedia IPs
  Test Vector for each IPs
  Performance monitor
  Memory controller
PM
PM
BUS
MEMORY
CPU
MM
IP1
RTL
MM
IP2
RTL
MM
IP3
RTL
MM
IP4
RTL
MM
IP5
RTL
MM
IP6
RTL
MM
IP7
RTL

## Slide 3: Motivation #2
Performance verification process
Build Emulation Platform
Generate Test Vector
Complete Bus Configuration
Update Latest RTL
Performance Verification
Update Latest RTL
    Since the complexity of a system bus increases significantly, a high quality performance verification is hard to achieve for a given time.
    A significant amount of efforts are required to build a complete bus performance verification environment.
    A real use case content is not available in an early stage of project.
    Specifications of IPs on bus fabric are frequently updated.

## Slide 4: Main Idea
Concept
  STB-PV
    Synthetic Traffic Based Performance Verification.
Detail
  Traffic Generator
    Use traffic generators that generate synthetic traffics like real multimedia IPs.
    Traffic generators make various burst size and length traffics randomly.
  Automation
    At least 20 traffic generators should be user for SOC performance verification. These components is attached to the system bus.
    Use automation script for these connections.
    Automation is based on the pre-defined configuration file which includes connection points.
    Reduce time to build traffic generator configuration.
PM
PM
BUS
MEMORY
CPU
MM
IP1
TG
MM
IP2
TG
MM
IP3
TG
MM
IP4
TG
MM
IP5
TG
MM
IP6
TG
MM
IP7
TG

## Slide 5: Evidence
Apply to SOC PV
  Apply STB-PV to the latest SOC projects
  Covered various verification areas with STB-PV
    System bus maximum total throughput.
    Measure maximum memory utilization.
    Each bus master’s peak and average latency.
    System memory management unit performance drop ratio.
    Bus QOS knob tuning.
  Reduce PV configuration time
    2 weeks compared to 2 months to configure and measure system bus performance and DRAM utilization.

## Slide 6: Summary
Bus Performance Verification Efforts
  A significant amount of efforts are required to build a complete bus performance verification environment.
STB-PV
  Use traffic generator which is configured automatically.
Goal
  Reduce bus performance verification time.
  Easy to make re-production environment for specific issue or bug.
Future works
  Enhance traffic generators
    Add burst pattern generation like real traffics.
    Add request delay option like real IP’s internal processing time.