## Slide 1: Sign-Off Driven Design Closure for a Mixed-Signal SOC
Authors : MuraliMohan T, Karthik Kodakandla, Atul Garg, Sanjana Sundaresh, Nagarjuna Ganji, Ajoy Mandal, Gaurav Varshney
Company : Texas Instruments

## Slide 2: Problem Statement
In the current low nanometers’ era, where design & manufacturing complexities are multifold, it is very imperative for physical designers to plan & execute efficiently to curb exhaustive mode of final stage design closure & to meet ever reducing design schedules.
Conventional approach to handle timing complexities with multiple modes, corners (MMMC), operating-points (OPPs) has been optimizing timing in single merged mode resulting in miscorrelation between PnR timing & signoff STA, leading to laborious closure iterations. Similarly, late signoff assessment & action on violations wrt DRC, LVS checks adversely impact schedule & exposes layout to surprises, quality gaps. This unpredictable strategy affects design’s original performance, power, area and schedule (PPAS) goals.
In world of large number of multi-timing-closure-scenarios, the engineering change order (ECO) is becoming inevitable to achieve design timing closure. This concern is attributed to the fact that it requires lot of manual efforts and iterations. Therefore, it is more important to start the design with highest correlation with respect to sign-off margins.
Of all the signoff closures, physical verification aspects like DRC, LVS are vital manufacturability & functionality checks respectively, any early assessment, analysis, feedback on these can bring significant change to design cycle times.
In this paper we demonstrate a correct by construction strategy that addresses timing and layout complexities by bridging gaps and anomalies between optimization, sign-off tools and flows.

## Slide 3: Proposed Solutions
Understanding tool’s capabilities, limitations play an important role in driving design utilization & routability & hence reducing manual effort in layout closure.
For the entire design convergence and timing closure, especially under current multi-corner multi-mode design, efficient and sign-off driven flow is introduced in order to improve the timing closure in the last mile to timing signoff.
Early LVS : LVS, in literal sense, just checks for logical to physical correctness i.e., even incorrect/incomplete logical connections with exact incorrect/incomplete physical data is correct with checks’ characteristics. The same principle along with divide & conquer approach is the essence of the Early LVS flow.
With this flow, we checked for correctness on IO, Core layout & power-grid, thus dividing & enabling to close power grid, IO, core placement first & then signal routing separately (like never before).
Bringing signoff into P/R tool with Tech .lef improvements, Standard cell-layout feedback, appropriate routing blockages for shorts, DRC reduction with early routing/DRC assessment were key items that helped in reducing layout issues substantially.

## Slide 4: Proposed methodology for timing closure
Optimization
Signoff
Common constraints across flow
Dominant mode corners
Based on library and PTV (selected the worst setup and hold corners)
All signoff modes and corners
Through the flow
timing Correlation
Constraints Validation
Signoff timing tool
Minimum ECO Loops
The proposed methodology aims to create a flow where the timing iterations between optimization and signoff is close to none
SI delay, load, slew
Accurate Flow Setting
Comprehending Signoff MetalFill

## Slide 5: Early DRC, LVS Assessment and Closure Flow
IO RING
Power-routed
Placed Design
First Routed DB
with Signal routes
Floorplan/Power grid Stage
Routing Stage
Final Stage
Generate Reduced Netlist
(Removing nets logically and physically)
Black-boxing Incomplete IPs
Power-grid shorts/opens fixed
Base DRC through pseudo filler
GDSII to LEF issues
Power-grid logical, physical corrections
Violations
(High count)
Shorts/ Opens/ anyother
Nets in concern – Logical & physical removal
Violations (Moderate count)
Final Stage
Routed DBs
Fixes &
Feedback
No Black Box
Correct Config file options
No violations
IO, Power & Custom grid,
baseDRC, corrections
Cleaner IO layout
power/custom grid
Cleaner signal
Connectivity
Signal conn.
corrections
Clean, Predictable
& no iterations
Signal nets not routed
Early Feedback
Fixes

## Slide 6: Summary
We have implemented the proposed flow on 800K instance-count, 100K register-count design with 3 SOC timing modes, 6 interface modes.
We could establish a very good timing closure correlation between optimization flow and sign-off flow resulting in almost closed design thus impacting design cycle in a positive way.
Early LVS is altogether a new & novel methodology that enables designers run LVS at any state of design & close strategically, making signoff easier & smoother.
Flow has been able to provide feedback to power-grid & PnR designers with base DRC corrections, shorts, Mixed-signal voltage spacing violations’ cleaning, which eventually helped in closing LVS within two days of receiving first routed DB on RTL frozen netlist.
Most importantly, these strategic & generic (adaptable) flows bring in significant change to signoff layout closure of complex designs with multiple mixed signal IPs/blocks, power-domains, new platforms, tight schedules.