## Slide 1
Block Level Boundary Constraint Validation with Top Context
Patricia Fong – Avera Semiconductor
Supporting Value: Scenario Walkthrough
Week 1-3: Block Work
Week 4: Realization of Constraint Issue
Week 5 – 6: Rework of Block
Motivation
In hierarchical timing, blocks usually proceed through Place-and-Route (PnR) ahead of the Top Level.
  It is most likely that block constraints were created earlier in the process and may not be as mature while PnR is proceeding; therefore, not as accurate or capture critical paths.
When top level is ready for PnR and better understood, we should ensure all signals coming to/leaving the block are captured by block timing.
Timing tool does not have a built-in feature and is deferred to other constraint checking tools .
  The tool doing the timing sign-off (the timing tool) is the preferred way to verify block and full chip timing signals correlate.
  Constraint Checking Tools add another layer of complexity and additional licensing
Solution: Idea
What needs to be done as early as ZWL:
Checking on the Input Side of Block1
  BLOCK0_CLKA and vi_CLKA are the same expected clock.
  BLOCK0_CLKA and vi_CLKB is not the expected clock. Alert needed.
  No timing NA on the block port. Alert needed.
Checking on the Output Side of Block1
  vo_CLKA and CLOCK_A are the same expected clock
  No timing NA on the block port. Alert needed.
  vo_CLKB and CLOCK_A is not the expected clock. Alert needed.
Top
BLOCK1
BLOCK0_CLKA
BLOCK0_CLKA
BLOCK0_CLKB
CLKA
“NA”
CLKB
vi_CLKA
vi_CLKB
“NA”
CLOCK_A
CLOCK_A
CLOCK_A
ü
ü
û
û
û
û
Solution: Method
Top Level Report Block Level Report
Option 1: List of Groups Option 2: Group by Keyword
set clk_hier_group [list \ set clk_hier_keyword
“BLK0_CLKA vi_CLKA” \ [list CLKA CLKB ]
“BLK1_CLKB vi_CLKB” ]
Final Check Report
Step 1: A script that is run in both Block level and Full-Chip Timing as soon as ZWL to produce reports with information of the clock at the port
  Use timing tool to extract launch clock name at the port of the Block from Top Level timing run and save into a report
  Use timing tool to extract virtual clock names at the port of the Block from the Block timing run and save into a report
Step 2: Another script to take in both reports and interpret the data to do the comparison
  Additional information is given to match top level clock names with the block level names with either explicit clock names or matching a pattern
  A report will be written out to notify mismatches or missing clock info
Block gets missing or incorrect clock port constraint.
Block goes forward with PnR – placement, clocking, routing – that would not meet top level timing
t > setup time
Block
Top
Block
û
Usually blocks will start PD work before top level due to top level being dropped later and more preplacement work needs to be done to top level before it goes through the placement tool.
With missing or incorrect clock port constraint, placement of logic could be unideal and weak drivers and wire codes used.
Depending how long top level takes to catch up, blocks may be far along through placement, clocking, and PD checks if the block is small or simple enough.
When top is post-placement, timing can indicate if port timing will meet setup/hold requirements.
When top level is ready, usually just past PnR and with full chip or with block abstracts, one discovers the path inside the block is late due to incorrect constraints allowing the path inside the block to be longer than allowed.
One can use ILMs or ETMs to get a first hint of a longer path inside the block.
This would indicate that better placement, buffers, drive strengths , or wires is needed inside the block to meet setup timing.
Wiring on lower layers and coupling can occur if the path was not deemed necessary and would need improvement
After updating the constraints for the block timing to realize the tightened requirement, at worst, the block has to go back through PnR and clocking to accommodate new placement.
If the constraints were correct, work would not have to be redone on the block, the block could have progressed further and been put on the shelf sooner (block timing and PD closed), and there would not be a risk of being a long pole alongside the top level.
Improving the block is not a show stopper, but the work done on the block on the first few weeks probably needs to be redone. PD resource would need to redo their work whereas the block could have been an nonissue past week 4 with cleanup on-going and focus mainly on the top level. With this issue, worse case, the block would need to go through PnR, clocking, and routing; thus redoing the work that was done through week 1-3.
Real Life Example Without Check
During next checkpoint netlist drop, with constraints updated and checks with the script, all ports
were matched and avoided rework.
Block Name | Block A | Block B | Block C | Block D | Block E | Block F
# of Unmatched Ports | 10 | 15 | 0 | 26 | 93 | 155
Weeks of Rework | 1 | 1 | 0 | 1 | 2 | 3
Conclusion
This method only requires the Timing Tool to check Block Port Timing between Top Level and Block Level Timing as soon as ZWL.
By having compared results, the timing engineer can investigate discrepancies early on instead of waiting for top level to be mature enough.
Can potentially save weeks from schedule and resource
OR
Block
ü