## Slide 1: A Novel Hardware and Software Architecture Sequencing & Validation Platform
Authors:
Lashminarayan Venkatesan
Raghav Tenneti
Preetika Tandon
Vishal Shah
Edward Riegelsberger

## Slide 2
Motivation
Problem Statement:
When system architects write software sequence speciﬁcations for a System-on-Chip (SoC), they need to analyze platform dependencies and reconcile conﬂicting constraints. The specific is typically a (subjective) document. The issues involved :
For architecture deﬁnition, documentation alone as a means of conveying the architecture intent is error-prone, and hard to maintain.
Ensuring that the production software loyally executes the architects intent is difficult as there is no automated mechanism to match the software sequence or state equivalence.
SW testing is simply limited to ensuring a graceful exit of code to a limited set of directed inputs.
Static performance analysis for varying constraints proves cumbersome
Figure 1: Static vs Dynamic flow
Our Proposal:
We propose a self-checking, executable platform architecture model that serves as a tool for architects to specify, visualize and sanitize software (SW) sequence speciﬁcations. Along with its validation extension, it doubles up as a validation platform for critical production SW code.
vs

## Slide 3
Boot Architectural Model (BAM)
Figure 2: BAM top level diagram
Boot Architectural Model (BAM) is our implementation framework that is a ‘executable speciﬁcation’ for Boot. It takes in Boot conﬁguration ﬁles as inputs and spawns boot sequences, state and latency estimation ﬁles as outputs. BAM models secure boot by sequencing SW steps to initialize the SoC out of its hardware (HW) reset state, to a well-deﬁned secured state upon which the OS and further application layers can run.
Features :
Models SW sequences as parametrized tasks
Embeds a hierarchical state model with functional, security and performance attributes
Maintains temporal HW master and slave state on SOC, per sequence step, for all boot paths and conﬁgurations
Implements self-checking functional, security and latency assertions
Consumes same inputs as fed to production SW in silicon chips to facilitate 1-1 comparison
Produces an auto-generated normative spec from the above model – with visualization extensions
Models the latency per SW task based on static HW calculations

## Slide 4
Implementation
Figure 3: BAM flow diagram
A BAM Task corresponds to a valid boot step or SW function during Boot. It is defined by Boot Function, Boot Mode, Boot Master.
BAM models list of BAM Tasks as a Task List per boot master.
During Boot, we can have more than on processor or master running like Boot processor, security processor, auxiliary processor etc.
BAM dispatches the tasks per master based on the boot mode parsed from input configuration file or based on master interdependency
If a task in Master 1 - Boot Processor(BP) can only be executed after a certain task in Master 2- Auxiliary Processor (AP), the BP executes a wait task. Then a handshake is sent from AP to BP and BP can now resume dispatching its tasks
After a task gets dispatched, it executes the sub-function in that task and performs a multifold operation of:
  Spawning the UML sequence diagram update
  Updating the boot state of all the modules involved at that particular task (in order)
  Recording the latency estimate based on global and task parameters.

## Slide 5
Applications
Figure 4: Automated Boot Specification
Figure 5: Production Boot SW validation Flow
Use-case 1 : Automated Boot Specification
A sequence speciﬁcation for SW/HW designers, including the functions and sub-functional names executed per task along with the interaction with different Boot masters and the slave modules
Use-case 3 : Boot SW validation flow
Golden Boot State is used for Boot SW validation. Boot SW outputs logs for register access, memory access and IP state updates while running on a SoC SystemC simulator. An ofﬂine Boot-Checker tool compares the register and memory access done by Boot SW against the golden reference output generated by BAM for same boot conﬁguration. The Mapper contains the functional translation from unit register accesses to abstract boot state for comparison with the golden.
Use-case 2 : Boot Latency Computation
It provides a clear breakup of time-taken in each boot step and per hardware operation which helps in correlation with latency numbers obtained from the software running on the silicon.

## Slide 6
Conclusion
Self checking assertions and auto-generated visualization of sequence helped in catching architectural bugs in early stages of Boot ROM code development
It provides an automated spec comparison utility replacing code reviews.
Boot SW validation is 10x faster on System SoC simulator using BAM golden output reference compared to RTL simulations.
Automotive markets require Boot SW to be safety complaint (meet ASIL-D certification). BAM validation flow helps create trackable SW flow from specification to implementation.
BAM helped in projecting expected latency per operation. Also the automated implementation helped in reducing boot latency by doing “what-if”
analysis on boot sequences.
Boot Latency correlation with silicon via
latency trials on BAM PoC platform closed in
5x faster man-days than in previous chips.
Figure 6: Boot Latency Computation