## Slide 1
A Lightweight Hardware Architecture for IoT Encryption Algorithm
Khaled Salah, Ph.D.
Technical Lead at Emulation Division
Khaled_mohamed@mentor.com
56th Design Automation Conference, 2019.

## Slide 2: Motivation
2
Popular encryption algorithms such as AES, 3DES, TwoFish, Mars, serpent, RSA and more don’t meet IoT security requirements in terms of power and capacity.
Therefore, different algorithms known as lightweight cryptographic algorithms have been presented in the literature that meet Those IoT requirements.
PRESENT is one of the most famous lightweight cryptographic algorithms and it was standardized by NIST in 2012, which provide the algorithm more credibility in its use.
In this work, A new implementation to PRESENT “a lightweight encryption algorithm” is presented which provides less power and less area than related work.

## Slide 3: Main idea: The Algorithm
3
PRESENT is :
    An ultra-low power encryption algorithm that is based on Substitution (nonlinear transformation) and Permutation ( linear transformation) network.
    It has a 64-bit input plaint text and either 80-bit or 128-bit key.
    It has a 31-round operation in each round:
      An XOR operation is introduced with round Key Ki.
      where
      The substitution and permutation are performed once every round.
      A new key is generated for each round.
      Decryption is the inverse of the encryption process.

## Slide 4: Main idea: The Proposed Architecture
4
Encryption
Decryption
There are 4 main blocks for the Present: AddRoundKey, S-box, P-layer and key schedule. They are working in the following manner.
  Step1: plaintext and the key are stored in a register.
  Step2: the plaintext is XORed with the key.
  Step3: a substitutional step is done to provide the confusion needed.
  Step4: the data is permuted and stored in the register and the counter is increased by 1 and so on.
For the decryption core, the overall steps are similar to the ones explained in the case of encryption but with some key differences.
  The s-box, permutation and key scheduling units are replaced with their inverse modules.
  The inverse permutation layer is carried out before the inverse s-box layer.

## Slide 5: Evidence1
5
Original images versus encrypted and decrypted one
Results for correlation and entropy

## Slide 6: Evidence2
6
To test the proposed encryption/decryption algorithm, we connect them back to back.
The power consumption is about 210 mW which is less power than the related work. Moreover, the overall area is less than the related work.
Metric | [1] | [2] | [3] | This Work
Latency (clock cycles) | 33 | 133 | 295 | 21
Max Freq (MHz) | 306 | 375 | 236 | 400
Throughput (Mbps) | 595 | 180 | 50 | 600
FPGA slices (Vertex 7) | 112 | 124 | 62 | 40
Power (mW) | - | 245 | - | 210
[1] A. Bogdanov et al., PRESENT: An Ultra-Lightweight Block Cipher, in Cryptographic Hardware and Embedded Systems – CHES, 2007.
[2] Borghoff, J., Knudsen, L. R., Leander, G., & Thomsen, S. S. (2011, February). Cryptanalysis of PRESENT-like ciphers with [3] secret S-boxes. In International Workshop on Fast Software Encryption (pp. 270-289). Springer, Berlin, Heidelberg.
[3] Pospiil, J., & Novotný, M. (2012, September). Evaluating cryptanalytical strength of lightweight cipher present on reconfigurable hardware. In Digital System Design (DSD), 2012 15th Euromicro Conference on (pp. 560-567). IEEE.

## Slide 7
Thanks