## Slide 1
Using PSS: An Automotive Case Study
Ben Sutton, Leo Matturi, Dilip Kumar Shankar Dass, Balasubramanian Gopalakrishnan
Infineon Technologies UK Ltd, Bristol, United Kingdom Email:ben.sutton@infineon.com
Motivation – a big integration challenge
The AURIX™ microcontroller family is targeted at Automotive applications, both for Powertrain and Safety. It contains a comprehensive on-chip trace solution.
The TRACE IP supports concurrent trace of many different on-chip sources – via a multiplexing infrastructure.
Functional verification of correct integration at subsystem and SOC level is a big challenge:
  A lot of system connectivity – varies across all family derivatives
  End-to-End verification of trace paths
  Adaptation logic to handle multiple trace source protocols
Existing methodology:
  Platform tests manually coded in C
  Scripted checking to verify trace output
  Maintenance and reuse of these test suites across multiple chip derivatives is both time consuming and expensive.
  Test programmer has to manage system resources – avoiding conflicts between code running on multiple CPUs in parallel
  Legacy scripting checking flow is hard to maintain and not scalable.
Created a model of the TRACE functionality (stimulus and test scenarios).
Written in Perspec SLN (System-Level Notation), one of the bases for Accellera PSS.
Existing SLN models for other key system IP, such as the CPUs and DMA already exist at Infineon. Used in conjunction with TRACE model to provide trace stimuli
Tooling used to generate testcases for different derivatives and integration levels
Solution
Variety of PSS tools available
Chose Cadence Perspec System Verifier PSS tool – already in use at Infineon.
Intention was to automate our testcase generation for reuse in:
  Different derivatives.
  Different integration levels (Subsystem, SOC).
  Different platforms
  (simulation, emulation, validation).
Need to improve efficiency for test generation and reuse
The Accellera Portable Test & Stimulus Standard (PSS) gives a framework to define your high level verification intent in a model (stimulus and test scenarios).
Verification engine generates testcases targeting different integration levels, platforms and chip derivatives.
Model Implementation
Conclusions
Can easily generate hundreds of tests but legacy scripting based verification flow is not scalable.
SVA Assertions are used to prove trace connectivity
The IP reference model (Specman e) is instantiated at the integration level in passive mode to verify the trace flow through the TRACE IP.
Coverage
Basic metric for integration verification is Design Implementation Toggle Coverage, ensuring all IP interfaces have been exercised.
This only provides a measure of activation of the implemented features/connectivity and does not identify those missing.
On top we specify Functional Coverage, ensuring system features are exercised and interesting scenarios covered.
The PSS tooling provides Generation Functional Coverage, allowing us to know before regressing what will be stimulated and hence if all required scenarios will be covered by a generated test suite.
This Generation Coverage is then converted into Runtime Coverage
Checking Flow
Development of the PSS model flow has shown real benefits, including quick setup of new product derivatives and reduced workload for test maintenance.
Very quick to generate 100’s of tests and associated functional coverage shows completeness.
Easy to generate a lot of stimuli but we need robust checkers and coverage - Reuse of IP checkers enabled this
Real benefit reusing existing PSS models of other IPs – can come from other subsystems or SOC level.
Developers don’t need to understand full functionality of the models being utilised.
As new trace sources are developed, their accompanying PSS models can be reused for stimuli in TRACE integration verification with minimal overhead.
Visualization of generated scenarios
MUX Configurations
Trace Source Actions inferred by the MUX configurations
Token passed to relevant Source
(Perspec CHANNEL construct)