## Slide 1: Motivation – Uncertain ATs
Lower Level design (dark blue) will be closed prior to Higher Level design (light blue).
1
The timing and noise analysis uses timing constraints at hierarchical boundary.
Latch
Latch
AT0
Latch
AT0
TIMING
CONSTRAINTS
Notes: <number>

## Slide 2
1
If the Higher Level design is changed (buffer added), the noise solution from Lower Level design may no longer be valid.
Latch
Latch
Notes: <number>

## Slide 3
Motivation –Coupled Noise Exposure Example
Coupled Noise is sensitive to arrival times. Arrival times are used to filter out aggressor nets that are not in sync with the victim (known as windowing).
In figure, no noise is computed at the latch if the aggressor arrives too early to impact the victim signal. Lower Level design is closed with no noise adjustment to timing.
2
Latch
Latch
Latch
Latch
Notes: <number>

## Slide 4
Now Higher Level design is changed. Lower Level was closed with outdated timing constraints. Noise is now missing in Lower Level analysis, putting hardware at risk.
2
Latch
Latch
Latch
Latch
Notes: <number>

## Slide 5
Aggressor are filtered based on timing window (arrival of noise at victim pin), which by default is based on arrival time constraints that are translated from the aggressor driving gate to the victim pin. This is an exposure.
Solution – RAT based Aggressor Windowing
3
Aggressor
Latch
ATAgg
RATAgg
Victim
Latch
ATVic
Coupling
Latch
Aggressor Window
Instead, use Required Arrival Time (dotted+solid arrow) to build possible arrival times.
Notes: <number>

## Slide 6
ATVic
ATLate
time
ATEar;y
RATLate
RATEar;y
Aggressor window using AT constraints
New aggressor window derived from RATs
Proposed window shows it is possible that Higher Level design could be changed to sync with victim AT. Therefore, noise should be computed to include this aggressor.
3
Proposed window is the set of all possible noise arrival at victim pin.
  Independent of Higher Level design changes.
Notes: <number>

## Slide 7
Solution – RAT based Victim Windowing
Aggressor-B
Latch
ATAgg
RATVic
Victim
Latch
ATVic
Latch
Aggressor-A
ATAgg
Latch
Latch
Victim ATVic shown is a constraint, and may change if Higher Level design is changed.
Use Required Arrival Time (RATVIC) to create a range of all possible victim arrival times, that covers all possible Higher Level design changes.
4
Notes: <number>

## Slide 8
Original Constraint ATVic
time
RATVic
Range of all potential victim ATs derived from RAT
Aggressor-A
window
New worst case AT and window
Aggressor-B
window
Use worst victim arrival time (largest coupled noise) within this range of all possible arrival times.
  Higher Level design could change such that this would be the correct coupled noise.
  Lower Level design can be closed with no concerns about missing coupled noise.
4
Notes: <number>

## Slide 9
Results
Plotting slacks in Lower Level design for paths feed by Higher Level design.
New RAT based windows give nearly all the benefit of doing aggressor windowing, without exposure to Higher Level design changes.
5
Notes: <number>

## Slide 10
Windows from AT constraints
RAT windows
No windowing
Slacks for all PI Paths
For example, if this path timing is fixed by speeding up this path, this analysis indicated it will pick up additional noise.
Fixing paths to these slack values (orange curve) derived by the new RAT windowing, will prevent design exposures such as these.
5
Notes: <number>

## Slide 11
Windows from AT constraints
RAT windows
No windowing
Worst Slacks at PI Feed Latch Inputs
Showing slacks at Latch inputs only (subset of previously plotted slacks).
5
Notes: <number>

## Slide 12
Summary
Shown is a new method for doing coupled noise windowing for paths with arrival times constraints.
The new method uses Required Arrival Times to replace Arrival Time Constraints to do victim and aggressor windowing.
Removes the exposure to Higher Level design changes that may happen after the Lower Level design has closed.
6
Notes: <number>

## Slide 13
Say NO To Arrival Time Constraints
Removing the exposure to Higher Level design changes
Hierarchical Coupled Noise Analysis
with Windowing using Required Arrival Times
Jason Morsey, Steven Washburn, Patrick Williams
EDA, IBM Systems, Poughkeepsie, NY
Notes: <number>