## Slide 1
Takashi Hasegawa, Maki Yajima, Makoto Fujiwara, Takanori Saeki
Sony LSI Design Inc., Kanagawa, Japan.
A hybrid clock tree with multi-spine using automated design methodology for low cost and low power complex LSIs
is a trademark or registered trademark of Sony LSI Design Inc.

## Slide 2: Introduction
Several clock distribution concepts have been proposed.
Categorize them from design points of view, as below.
Traditional Mesh(grid)/Fishbone(Spine) , Hybrid Clock
Tuna type
Sardines type
Many clock domains , ICG structure is complex
Low power/cost SoCs, Mix-Signal , IoTs ・・・
MPU, NoC, High Speed IF ・・・
A few clock domains, ICG structure is simple
CTS
Conventional concepts for “tuna” designs is costly and unsuitable for “sardines”
Most of our commercial chips are categorized into “sardines” designs.
The quality of CTS is not enough.
The new concept of lower power and less effort is required.

## Slide 3: Motivation
The conventional hybrid clock tree is not suitable for “sardines” designs (low cost and low power complex LSIs.)
CTS
CTS
CTS
CTS
■Conventional Hybrid Clock Tree
Our common design characteristics
  Middle sized designs (<5M instances)
  Many clock domains (50+)
  Fewer layers (use only IM layers)
  Complicated clock gating(ICG) structure
  Not high speed (several hundreds of MHz)
Design area is divided physically. CTS origins are blue buffer(tap)
A conventional concept is not effective due to the limitation of size and ICG structure.
Our design requires low power and short TAT.
A proposed clock distribution concept and design methodology,
  Much lower power as well as better quality.
  Automated method with custom cells reduces engineering time drastically.

## Slide 4: Comparison with conventional concepts
 |  | CTS by commercial tools | Conventional Hybrid Clock | Conventional Spine | Proposed Hybrid clock
 | Layout image |  |  |  | 
Application |  | “Sardines Type” (Mix-Signal Low-power/cost SoC) | “Tuna Type” (MPU, NoC, High Speed IF) | “Tuna Type” (MPU, NoC, High Speed IF) | “Sardines Type” (Mix-Signal Low-power/cost SoC)
Target Design | Size | Any | Large designs | Large designs | Any
 | Speed | Under GHz | Over GHz | Over GHz | Under GHz
 | structure | Any | simple | very simple | Any
 | Layer number | Any | Need thick metal | Need thick metal | Any
Result | effort | Minimum | A lot | A lot | Minimum
 | skew | Not good | Good | Very good | Good
 | power | Not good | Not good | Good | Good

## Slide 5: Proposed concept : “hybrid clock tree-spine”
 | Proposed concept “Hybrid clock tree-spine” | 
Target Design | Size | Any
 | Speed | Under GHz
 | structure | Any
 | Layer number | Any
Result | effort | Minimum
 | skew | Good
 | power | Good
ICG
BUF
FF
Global CTS and multi-spine structures.
  Global CTS can handle any size , structure.
  Multi small spines doesn’t need thick metal
Optimized super buffers
  STA is able to be used
Optimized spine layout
  Lower power than CTS.
  Better skew than CTS.
  Required to be same effort as CTS.
    Need automated methodology

## Slide 6: Design methodology: ICG Clustering
clustering
Place Optimize
floorplan
Route Optimize
GDS
VNET
SDC
No
change
No
change
Spine layout
Static Timing Analysis (STA)
Clock tree synthesis
Physical Verification
Considering register locations, pre-existed cells are cloned by slew limitation.
Commercial EDA tools have this function.
Pull ICGs/FFs
ICG
BUF
ICG Clustering
Super buffer placement

## Slide 7: Design methodology: Spine wire-width optimizing
clustering
Place Optimize
floorplan
Route Optimize
GDS
VNET
SDC
No
change
No
change
Spine layout
Static Timing Analysis (STA)
Clock tree synthesis
Physical Verification
Pull ICGs/FFs
Spine wires should be narrower for lower power.
  Spine Wire Width = max ( min width by EM criteria , min width by slew criteria )
In-house Script automatically generates the spine layout.
Main spine wire
Sub-spine wire
Spine wire-width optimizing
Super buffer placement

## Slide 8: Design methodology: Super buffer for optimized spines
clustering
Place Optimize
floorplan
Route Optimize
GDS
VNET
SDC
No
change
No
change
Spine layout
Static Timing Analysis (STA)
Clock tree synthesis
Physical Verification
Pull ICGs/FFs
Super buffer placement
INV
DECAP
DECAP
INV
DECAP
DECAP
INV
DECAP
DECAP
INV
DECAP
DECAP
INV
DECAP
DECAP
  The driving strength of super-buffers is decided by the slew criteria.
Key Features of customized super-buffers
  Wide-range buffer-sizing variations (x50～ x1600).
  Transistors in cells are placed carefully to consider noise.
In-house Script automatically calculate cell-size and pre-place.
ICG
ICG
ICG
ICG
ICG
ICG
ICG
ICG
ICG
ICG
Super buffer for optimized spines
Super buffer

## Slide 9: Design methodology: ICGs placement optimization
clustering
Place Optimize
floorplan
Route Optimize
GDS
VNET
SDC
No
change
No
change
Spine layout
Static Timing Analysis (STA)
Clock tree synthesis
Physical Verification
Pull ICGs/FFs
Super buffer placement
INV
DECAP
DECAP
INV
DECAP
DECAP
INV
DECAP
DECAP
INV
DECAP
DECAP
INV
DECAP
DECAP
This flow can reduce engineering time drastically compared with conventional one.
ICG
ICG
ICG
ICG
ICG
ICG
ICG
ICG
ICG
ICG
ICG
ICG
ICG
ICG
ICG
ICG
ICG
ICG
ICG
ICG
ICGs are relocated under sub-spine wire for reducing clock power before ICGs.
In-house Scripts automatically move and optimize them.
ICGs placement optimization

## Slide 10: Application designs
Applied proposed “Hybrid clock tree-spine” into our 3 industrial designs.
 | Design information |  |  |  |  | 
name | Process | # of Instance | # of Clock domain | Clock gating level | # of FF bits | Frequency
Design A | 40nm 6Cu | 1.9M | 45 | 4 | 380K | 200MHz
Design B | 40nm 6Cu | 2.1M | 62 | 5 | 360K | 230MHz
Design C | 40nm 6Cu | 1.7M | 62 | 5 | 360K | 230MHz
Design A
  Compared with a full CTS result, under same netlist and same locations of registers on CAD tool.
Design B and C
  RTL2GDS comparison (same RTL). Compared on Si as well as CAD tool.

## Slide 11
◆Full low-power CTS
◆Hybrid clock tree-spine (proposed)
ClockWire Cap : 16pF
ClockWire Cap : 25pF
The result of the comparison between CTS and “hybrid clock tree-spine” on one clock domain.
Wire Capacitance 37% Reduction
A Detail Result of design “A”
The wire length is apparently improved.
Locations of registers are same.
Highlighted wire from root to sink points
■ Design A
- S/C instances : 1.9M
- clock domains : 45
- process/layer : 40nm 6Cu (5 thin layer)
by commercial tools

## Slide 12: An implementation Result
Chart: latency [ns]
| 3.5 | 3.6 | 3.7 | 3.8 | 3.9 | 4 | 4.0999999999999996 | 4.2 | 4.3 | 4.4000000000000004 | 4.5 | 4.5999999999999996 | 4.7 | 4.8 | 4.9000000000000004
full CTS | 0 | 0 | 0 | 0 | 0 | 0 | 38 | 4322 | 16748 | 54800 | 50048 | 408 | 0 | 4 | 0
new method | 0 | 2975 | 982 | 14538 | 52074 | 37796 | 10701 | 7282 | 0 | 0 | 0 | 0 | 0 | 0 | 0
■The main clock skew/latency histogram (design A)
10% decrease on average
 | Design Layout 40nm 6Cu (5 thin layer) | Clock Power result (TT,25c,rctypical) | 
 | Layout view | Full CTS (commercial tool) | Hybrid clock tree-spine
Design A ※registers‘ locations are same. |  | 24mW | 21mW
Design B |  | 58mW | 42mW
Design C |  | 50mW | 36mW
 | Design A case |  | Tuna design (reference)
 | Full CTS (commercial tool) | Hybrid clock tree-spine | Conventional hybrid clock
Engineer Time | 1 week | 1.5 week | 12 weeks
This method
Full CTS
(SS,-40c,cworst)
“Hybrid cock tree-spine” is proven in Si at design B and C.
  Total power reduction: 15% at CAD tool, 13% at Si. Their yields are same.
60K
50K
40K
30K
20K
10K
15% reduction
27% reduction
28% reduction

## Slide 13: Result and Summary
We proposed hybrid clock tree-spine and the automated design methodology for “sardines” designs (low cost and low power complex LSIs).
Comparing with a full CTS at “sardines” designs.
  Custom cells and an in-house automated flow achieve almost same productivity and engineer time.
  37% capacitance reduction of clock wire in one domain due to optimized spine layout and ICG placement.
  15-28% power reduction of all clock networks, 10% reduction of clock latency from PLL and 50% hold TNS reduction enjoying the benefit of the spine based clock.
These results were proven in Si. A ratio of power reduction was almost same as we expected on EDA tool.