## Slide 1: Early SW Bring-up Methodology using Full-SoC level Virtual Prototyping
Samsung Electronics S.LSI
Woojoo Space Kim, Jongmin Lee, Seonil Brian Choi
2019

## Slide 2: Motivation
Speed [Hz]
Silicon Stage
RTL Simulation
ESL Simulation
Pure Emulation
RTL Design
GL / MTO Stage
100M
0.1 K
1M
2 G
Shift Right
Shift Left: for enough development time
Pre-Silicon Stage  Post-Silicon Stage
Hybrid Platform
Silicon
Test Board
“Fixed Release Date”
Not
Enough
Time !!
FPGA
Shift-left Paradigm :
  Increasing design complexity and insufficient development time
  To ensure development time and quality, early stage SW bring-up/optimization is required

## Slide 3: Main Idea – Virtual Prototyping
ESL environment – SystemC/TLM model based virtual platform environment
  LT (Loosely Timed) based TLM model : for high speed simulation (up to 300MHz)
  Full SoC level virtual platform : ONE branch SW development – SW stability
  At early HW design stage, SW development started
Economical Efficiency
  Replacement of silicon test board : In Automotive, a huge number of SW developers
  Easy board modification for bug fix and enhancement : only code modification
SoC(HW) Development
SW Development
Virtual Prototype Development
SW Development
SW Validation
Shift Left
Incremental Approach
On Virtual Platform (Prototype)
On Silicon Test Board

## Slide 4: Implementation and Validation
Virtual Prototyping Implementation / Validation
  Virtual platform (HW development) development at early RTL design stage
  SW development and test on virtual platform first before MTO/PKG and then on board
  : HW/SW are validated during SW development on both virtual platform and board
About Test Vehicle
  About 1000 IP models in Full SoC level virtual platform
  OS based full BSP and test cases

## Slide 5: Result
Simulation Performance Comparison
User Interface of Virtual Prototyping
 | Simulation | Pure Emulation | Hybrid Platform Emulation | Virtual Prototyping (ESL) | Diff. (Pure vs. VP)
Environment Initialization | 4 min | 5 min | 5 min | 30 sec | x 10
Kernel Boot-up (prompt) | 125,867 min* | 96 min | 2 min | 1 min | x 96
Android Home Screen | 741,517 min* | 661 min | 47 min | 8 min | x 82.6
Total Consumed Time | 867,384 min* | 762 min | 54 min | 10 min | x 76.2
Clock Frequency | 866 Hz | 986 KHz | 13.9 MHz | 75.6 MHz | x 76.2
Useless
x 1138
x 14.1
x 5.4
* Estimated Value

## Slide 6: Conclusion
Early stage SW bring-up
  World first Full SoC Level virtual prototyping for early SW development
  Virtual Prototyping can save development cost by replacing silicon board
  From specification stage, virtual prototyping started
Simulation Performance
  75.6MHz is slower that silicon board by 26.5 times but only 10 minutes are required to boot-up Android Platform
  It is fast enough that SW can be tested dozens of times a day
Advantages for SW development
  Enough time can be secured for SW development and optimization
  Since a separate SW branch for virtual prototyping is not needed, efficiency of SW development can be secured
Future Work
  Design Methodology development for convenient and fast IP modeling
  Automation system for reducing time for virtual prototyping more