## Slide 1: Challenges in Tackling Reset Domain Crossing Verification with Low Power SoC
Francis Chockalingam, Viral Gorasia (Broadcom, India)
Anup Gupta, Amit Goldie (Synopsys, India)
Design Details
RDC issue identified and solutions
Abstract
SoCs require ever-increasing performance requirements at the same or lesser power envelope. Having multiple clock and power domains enables the system to be run at the optimal power-per performance threshold. But the verification of the functionality of this approach poses a greater challenge which the functional simulation-based verification is not able to satisfy. Reset verification in the context of power-up sequence is extremely critical to avoid silicon issues. Proposed verification flow, identifies the RDC issues related to the power-domain crossing taking into account the power-state transition from Simulation. Flow also takes into account the false PDC through power management controller FSM coverage. This method helped to identify RDC issues due to power-domain crossings as well as address the large number of SpyGlass RDC violation pruning.
Conclusion
Initial SpyGlass runs resulted in large number of RDC violations which were addressed using reset_order and reset_filter_path constraints. Automated reset constraints generation using VCS/STA scripts were used to address the power-domain related RDC. This reduced setup time from weeks to less than day. Script based reset constraint generation avoided any mistakes as well as made review easier.
Enhanced verification flow flagged many of the RDC related issues. Identified the Peripheral reset synchronizer retention requirements due to power-gating. Reset synchronizer retention states identified and updated UPF accordingly. Various reset ordering issues were identified and the power-controller updated for proper reset sequence. Updated reset constraints portable for both block and top-level RDC runs. Avoided time-consuming manual review of violations and waivers. CDC/RDC checks were done at a very earlier stage of the project. Helped address the issues well in advance and not wait for timing-closed SDF simulation.
Acknowledgement
New Proposed Flow
Processor complex
  AXI bus fabric, System ROM/Memory, TLBC, Peripherals
Clocks:
  CPU: 1.1GHz, System: 550MHz,
  Peripherals: 25/100/400/550MHz,
  Debug: 10/40/550/595MHz
  Design blocks operate in a range of frequency requiring multiple CDC-modes
CPU complex consists of 5 power-islands
  Clock gating in Standby/Snooze mode
  Low-power modes for memories
  Results in 48 low-power states
CPU | Single-core
Fabric | 26 master 7 slave
Peripherals | 13
Design Size | 2M gates
Memory | 1.2MBytes
Clock domains | 11
Reset domains | 27
Power domains | 5
Power States | 48
Reset-order constraints
UPF power-states and power-mgmt controller state transition is used to create the reset order constraints
PDC Reset-order
Power-states transition from VCS-LP report parsed to identify reset-order changes
False Reset sequence pruning
Power state coverage being used to refine false reset sequence and power domain crossing
nrst_nI2C
nicresetn
Metastability due to D->rstn
SW_PD
Reset synchronizers inside the switchable domain driving logic in more-ON power domains
SW_PD
Fix is to use of retention reset synchronizer to retain the de-assertion value
  No need to propogate the reset de-assertion as the de-asserted value will gets restored