## Slide 1: Hierarchical Power Intent Driven Efficient Power Integration Methodology for Ultra Low Power Mixed-Signal SoC
Aswani Kumar Golla, Venkatraman Ramakrishnan, Gaurav Varshney, Lakshmanan Balasubramanian Texas Instruments (India) Pvt. Ltd., Bengaluru, India

## Slide 2: Acknowledgements
Luke Lang and LP team from Cadence Design Systems for continuous, extensive support towards maturity of all related tools and enabling interception of the Hierarchical CPF methodology, CLP based CPF integration and LP checks
Mark Jung and Nikhil Sangani of Texas Instruments for concept and automation of IP deliverable based isolation rules at SoC level
Vivek Gandhi of Texas Instruments and Sushmitha T G, Sunita T & Abhishek K of Karmic Design Systems for interception of integrated CPF for LP DV & AMS co-simulation
Ayaskanta Behera of Texas Instruments for assisting with CLP based CPF integration
Sunil Kelahatti, Shalini Eswaran, Ajith Subramonia, and Jagdish C Rao of Texas Instruments for their continuous motivation and support

## Slide 3: Motivation & Problem Statement
Increasing functional complexity on mixed-signal (MS) SoCs
Need for achieving lowest power consumption, compressed time to market
Newly evolving ultra-low power SoC architectures require highly complex on chip power management (PM)
Various levels of PM requirements  Architectural, structural and electrical
Existing methods of SoC PI capture are effective, but inefficient  Manual, error prone and time consuming
Necessitates robust power intent (PI) specification, PM integration, implementation and verification methods
Should be consistent at all levels  Library components, IPs (Soft, Hard, digital & MSIPs) and SoC
Notes: Newly evolving ultra-low power SoC architectures require highly complex on chip power management (PM)
Complexity: Multiple voltage / power domains and several hundred power modes
PM functions required at all levels: Library components, IPs (Soft, Hard, digital & MSIP) & SoC

## Slide 4: Integration and Verification Challenges
Low power (LP) methodology formalized only at SoC toplevel  Custom handled at IP level including complex MSIPs
Significant differences between PIs used for implementation and verification
Quality gaps & execution bottleneck due to absence of phased, reusable and hierarchical LP implementation and verification
Power up sequence & verification criticality
Considered AON for implementation
 Verification is critical
Complete Power modes considered for SoC implementation
Notes: Low power (LP) methodology formalized only at SoC toplevel
  PI typically not captured and verified at IP level
  Only hard macros had unverified block box PI
Whole power intent (CPF) was captured only at SoC level (including for IPs)

## Slide 5: Current Low Power Design Methodology
Limitations
IPs developed and verified for functionality only  PPA & schedule surprise after SoC integration
Issue with low power cells in IP  Late IP changes
MSIP cannot be verified until its internal digital is implemented  Delays in MSIP focused verification

## Slide 6: Proposed Solution & Methodology Overview
Goal: Efficient, hierarchical and reusable power intent driven low power implementation and verification methodology
Comprehend architectural intent in the power description
  Custom isolation insertion requirement in addition to other low power design complexities
  Custom design & integration steps
  Tool enhancements for CLP check, integration, and low power mixed-signal simulation
Single standard, uniform PI across flows
Develop IP power intent
Develop SoC power intent
Standardised PI use model across flows

## Slide 7: 2. Single Standard, Uniform PI across Flows
Logical connectivity is fully automated and mature using standard HDLs
Power connectivity and intent
  Independent parsers for various flows/tools
  Difficult to capture flat SoC PI, automate and maintain consistency
  Standard common power format is required
Different PI formats & choice
  Choice between IEEE 1801 (UPF) and CPF
  Used CPF due to better maturity of tools and flows
  Limitations with some PI constructs across tools
Enabled single PI (CPF) across flows
Implementation support
Verification support
Implementation support
Verification support
Secured extended support
Guidelines
Formalised methods for exceptions

## Slide 8: 3. Develop IP Power Intent
“Constrained” power intent strategy for IPs to meet
  Architectural constraints  Boundary port association, power modes, rules, etc.
Enabling early SoC verification with Design CPF of hard IPs
MSIP integration context
CPF flavours
For MSIP Implementation
IP & SoC verification: RTL DV/DMS/AMS + Dig. RTL (Available early)
For SoC Implementation
IP & SoC verification: RTL DV/DMS/AMS + Dig. GL (Late)

## Slide 9: 4. Develop SoC Power Intent
Isolation handling
Only IP interface rules at SoC CPF
IPXACT based automation
NETLIST
IPs PI
IP_1
IP_1
IP_2
…
IP_n
CLP
FLAT SoC PI (CPF)
Multiple closure iterations
Incorrect PI & Manual errors
SoC, IP Internal rules
pass
fail
MANUAL CODING OF PI
MANUAL CODING OF PI
- Simplified, top level only
IP CPFs
MANUAL CODING OF IP PI
SoC rules
HIERARCHICAL SoC PI (CPF)
CLP
INTEG.
Much reduced iterations
VERIFICATION, IMPLEMENTATION etc.
INTEGRATED SoC PI (CPF)

## Slide 10: 5. Standard PI Use Model across Flows
Hierarchical Golden CPF
Simulation (Xcelium®)
Synthesis (Genus®)
Implementation (Innovus®)
Synthesis CPF
Implementation CPF
Implementation (Innovus®) ECOs
Logical LP Checks (CLP®)
Final CPF
Physical LP Checks (CLP®)
XMIPA®
EC
Integrated CPF

## Slide 11: Evidence
Proposed Hierarchical PI (CPF) approach applied on low power mixed-signal SoC development enabled
  Independent & timely IP maturity before SoC
  Methodology & tool enhancements in collaboration with Cadence
  Early verification using Design CPF of MSIPs
  Validated integrated CPF  Through CLP based PI integration
  Early verification before synthesis  Through Logical RTL based CLP check
  PA RTL DV quality improvement & correlation to implementation  Through XMIPA® (LPS EC)
Baseline methodology applied for MS SoC platform development
  Early identification of design and integration issues
Improvement in SoC PI capture complexity (10x) and Cycle times
CLP check statistics
Static PI correctness
LP DV statistics
Dynamic PI correctness
PI creation cycle-time
PI complexity reduction

## Slide 12: Summary
Developed and intercepted efficient, robust, hierarchical low power design, integration, and verification methodology
  Applied with CPF as PI format
  Concepts and flows are generic  Applicable to IEEE 1801/UPF with no or insignificant additional effort
Early maturity of IPs before SoC  Rich portfolio of reusable IPs for future SoCs
Proven, efficient SoC power integration flow  Reusable for future SoCs
Enabled industry leading mixed-signal low power SoC with competitive power performance
Limitations & Future scope
  Enhancement of SoC level IPXACT® based isolation rules automation using pin power domain information
  Full automation for manually coded simplified SoC CPF
  Apply proposed method on a UPF based PI to identify and bridge any PI format specific gaps