## Slide 1: Practical Implementation of Active Mode Power Gating Circuits
Insub Shin, Wook Kim, Kyungtae Do, and Jung Yun Choi
Foundry Business
Samsung Electronics Co., Ltd.

## Slide 2: Motivation
Active mode power gating
  Combination of clock gating and power gating
    Lowering virtual VDD (VVDD) to reduce active mode leakage current while (block-level) clock gating is applied
  The most effective run-time technique to reduce active mode leakage current
Design challenges
  How to lower VVDD level during clock gating period
    VVDD must be higher than the minimum guaranteed voltage for data-retention
  VVDD must be fully charged before releasing from clock gating
  Care of wake-up noise and wake-up time
Logic
block
SLEEP
CMU
Clocks
PMU
VDD
VVDD
Time
VDD
VVDD
Min. voltage
for data-retention
Voltage
Clock
Clock gating period

## Slide 3: Main Idea
Employ (fully digital) voltage monitoring circuit and small number of power switches to control VVDD
  All the existing power switches are turned off during active mode power gating
  If VVDD is lower than Vref, dedicated power switches are turned on (Y = 0), so that VVDD is charged
    Vref can be tuned by user
  Otherwise, dedicated power switches are also turned off (Y = 1)
Utilize the existing block-led clock gating scheme
  Block can request to apply or release clock gating, and also deny the request of CMU to apply or release clock gating
    Release request is forwarded to CMU after VVDD is fully charged
Logic
block
SLEEP
CMU
Clocks
PMU
VDD
VVDD
CG control
CG control
CG
controller
SLEEP
VVDD
Vref ( > minimum voltage for data retention)
Monitoring
circuit
Y
AMPG control

## Slide 4: Main Idea
Wake-up time should be as small as possible to reduce “timing overhead of AMPG”
  SLEEP signal is propagated in daisy chain fashion, and each signal drives multiple power switches
Wake-up noise of AMPG is smaller than that of normal power gating
  The number of dedicated power switches is smaller than that of “PRE-group” power switches
  VVDD is charged from minimum voltage for data-retention to VDD
SCPRE
SCPRE_ACK
SCALL
SCALL_ACK
monitor
AMPG_ACK
monitor
monitor
SCALL
SCALL
SCALL
SCALL
C-element
monitor
power switch
power switch (for AMPG)
2-input AND gate

## Slide 5: Simulation Result
Experimental setup
  Samsung 10-nm technology / test circuit: 5 industrial circuits
  Minimum voltage for data-retention is assumed as 0.475V
  SPICE simulation was performed using gate-level netlists of each circuit and monitoring circuit
Experimental result
  Compared to clock-gated circuit, leakage current is reduced by 89% and 31% when VDD is set to 1.05V and 0.65V respectively
  Overhead of monitoring circuit is negligible

## Slide 6: Summary
Active mode power gating
  The most effective run-time technique to reduce active mode leakage current
  We first employ active mode power gating to commercial design
Our approach to resolve design challenges
  Employ (fully digital) voltage monitoring circuit to control VVDD level
  Utilize existing block-led clock gating scheme
  Special care of wake-up time and wake- noise
Simulation result
  Leakage current can be reduced by more than 89% compared to clock-gated circuit (when VDD = 1.05V and temperature = 25℃)