## Slide 1: Practical cell based analog design methodology Ⅱ (AnaCell)
Promotion of analog automatic cell generation with
the designability in AnaCell
Author Name : Akira Suzuki, Yukichi Todoroki,Tomoyuki Kato,Masanori Kusano, Nobuto Ono, Kazuhiro Miura ,Kazuyuki Kawauchi :Jedat Inc.
Takashi Ida, Yudai Abe, Yukiko Shibasaki, Anna Kuwana,
Haruo Kobayashi : Division of Electronics and Informatics, Gunma University

## Slide 2: Difficulty of analog standard cell design
Cells are highly correlated each other
Cell components are electrically isolated each other
Specifications are diverse and continuous
Number of Cell kinds is unlimited in terms of performance
Process margin depends on W/L and layout
Number of Cell kinds are limited around hundreds
Specification is limited and discrete
Process margin is sufficiently included in cell library
Analog Cell
Digital Cell
Standard Cell design in Analog could not have been applied like digital design.
Notes: We would like to present the cell base Analog design and we were honored to receive the best presentation award in last year DAC.
This year, we further improved the automatic bias setting for each transistor and that will help to design each AnaCell more efficiently.
At first let me explain the AnaCell briefly.
Analog design style is basically transistor base so far.
If we would like to dramatically improve the design efficiency, somehow cell level design style is necessary.
But if we say analogically like digital cell, 2-10 transistor basic analog cell is difficult to be used as hard cell like gate cell.
At first, we have to carefully list up the reason as below.
Most basic difficulty arises from that DC bias should be adjusted dynamically and this depends on each design, thus there is no way of pre determined W/L transistors library.
If we have to prepare sufficient number of hard analog cells, we may have to make massive , unlimited number of cells in terms of performance requests in each design.
Also this implies that the process margin will be clear only during the design because W/Ls are determined only during the design.
Those issue pushes analog designer to design transistor base even many automatic analog design tools have appeared in these 20 years.

## Slide 3: Concept of AnaCell and the difficulty
AnaCell is targeting to become like the digital standard cell in Analog Design
Still designer needs the iteration to find the appropriate DC bias to satisfy the various requirements in AnaCell
-DC bias means circuit’s operating points and each Transistors‘ Vgs/Vds/Vbs etc.
Notes: We proposed Analog Cell design methodology which is targeting to be similar with digital cell design in last year DAC.
Because analog design utilizes non linear Transistor behavior to meet exponential performance requirements, usually it is not practical to set best parameters for multi objective by automatic optimizing algorithm.
AnaCell is practical in the sense of reasonably small size with basic characteristic and it enables to designer to explore the dimensional L and W space which provides the specific bias conditions in the technology.
This helps to avoid empirical limited L W parameters and AnaCell can easily provide best parameters from whole possible candidates with the view of performance trends.
But compared with digital cell, AnaCell still needs some effort to determine final parameters.
It is because , DC bias conditions for each node in AnaCell have to be specified by user. This operation may be easy for experienced analog designer, but not easy for unexperienced analog designer.
In this presentation, we present the DC bias auto setting methodology which should be the key point for AnaCell to be more useful for general analog designer.
With this auto bias setting methodology which does not depends on technology, designer only needs to specify the supply voltage and current to get the initial DC bias conditions which leads designer to be easy to adjust by setting L and W from candidates’ table for best AnaCell performance.

## Slide 4: Design methodology using AnaCell
Cell | Type | TR # | Total #
Differential Input | Current mirror | 5 | 24
 | Constant current mirror | 5 | 
 | Cascode current mirror | 7 | 
 | … | 7-9 | 
Current Source | … | 2-7 | 36
Amplification | … | 2-4 | 22
AnaCell
Library
Tuning each transistor’s Bias and W/L in AnaCell
＊AnaCell is under Patent pending
-Bias conditions
-Performance graph from
gm/gd in exhaustive L/W table
-Test bench and
simulation waveform for
target performance
AnaCell
Notes: AnaCell library consists of around 100 cells currently. It consists of Differential input circuit like differential signaling constant current mirror, Current source like cascode current mirror and so on.
AnaCell itself consists of Schematic and parametric W/L, and dynamically generates L-W table which has exhaustively simulated gm/gd, then predicts multiple performance as graph image.
Designer prepares the schematic design by combining AnaCell. Or user can extract as the AnaCell from given design.
Then apply the process technology.
Designer can specify bias conditions in AnaCell, then AnaCell can generate LW table with gm/gd and performance graph.
During the design, designer makes a lot of iterations to meet the performance and layout sensitivity around specific L, W and can simulate at target design points.
AnaCell can provide candidate L-W metric to designers quickly.

## Slide 5: AnaCell deign usage
■ The circuits that consist of AnaCells are suitable for Current source/OPAMP/Regulator etc.
■ There is no limit in circuit size and number of AnaCells for designing
■ Circuits can be designed combining AnaCells and Pull UP/Down and Gate elements
Pulse Width Modulation Circuit
consists of AnaCell/Pullup/RESISTENCE Ladder/Transmission Gate/User Circuit
Pull Down
Resistance Ladder
Transmission
Gate
User
Circuit
Pull Up
AnaCell
Pull
Down
Notes: Let me show how the AnaCell is used in real circuits.
This figure shows the example of Pulse Width Modulator.
Thus AnaCell is naturally suitable for the design of Current source, OpAmp, Regulator etc.
Any circuit which has this kind of current centric elements combined with other elements like passive elements, gate and user circuit will have the merit for using AnaCells.
Designer can add Pull Up and Down over the AnaCell and Transmission gate
and resistance ladder which impacts on transient simulation.
Adjusting performance by DC bias and gm/gd tuning is much easier in AnaCell after the transient simulation.
Also there is no limits for Circuit size and how many AnaCells are used.

## Slide 6: Concern in DC bias setting and auto selection
■ Vgs, Vds has feasible range to derive a certain Ids regarding gm (W/L)
■ Design space of W and L is discrete and has specific curve
■ Every W/L which satisfies the target Ids may be logically the candidate but in terms of designability
for other metrics every W/L does not fully satisfy
■ Designability: We define the designability as the freedom and allowance for design L/W
for adjusting the multi objects of circuit performance.
Automatic selection of the DC bias which maximizes the designability should be
the best candidates for AnaCell in specific process
＊AnaCell is under Patent pending
Notes: In this slide, we explain how DC biases are set automatically. We emphasize that this is from designer’s point of view and not from algorithmic point of view.
Suppose the transistor needs the specific Ids under the supply voltage.
There are unlimited L and W to realize this conditions in logically, but in reality there are limited design parameters for L and W.
If we draw the each curve corresponds to W/L for Vgs, we have this graph in left hands.
This shows that in order to derive the specific Ids’, W/L namely gm has each slope under Vgs conditions.
Suppose reasonable W/L ratio is from 0.1 to 100.
Also we selects L and W parameters which is uniformly sequenced value which is easy to design.
Each plotted points provide the targeting Ids’, but in the view of designer, it should have a freedom of adjusting L and W around the initial value to get better performance like area/power/gain/resistance/variation/robustness etc.
So AnaCell automatically selects the initial point which has most adjustable value which is shown in red circle.
We call this perspective as the designability which means the initial design value should be easiest to be adjusted in the space of discrete design space in the allowable targeting conditions.
And this auto bias setting should work with any process technology and any supply voltage.

## Slide 7: DC bias setting and Vds tuning 1
⊿I
⊿V
P（gd）=
⊿I
⊿V
W is changed
Derive the lower limit Vds’ based on gd
Vds>Vgs-Vth ∴Saturation Region
Reference Point of gd（slope）
Vds=Vgs ∴Saturation Region
W is changed
Point that acquired Vgs（Designability）
Vds>Vgs-Vth ∴Saturation Region
■ Each transistor starts from Vds=Vdd
■ Valuable Vds of each transistor should be lower than Vdd under the condition of saturation
and reasonable gd slope
Notes: In vertical stacked transistors, Vds of each transistor should be low enough compared to Vdd for design flexibility.
This slide shows how Vds is lowered satisfying the stable conditions.
The plotted vgs in previous slide supposes Vds=Vdd, thus vgs satisfies fully that transistor is in the saturation region as in left figure.
The red region shows the over drive voltage which is vgs-vth.
If vds is in this region, transistor is not in saturation and output resistance is small.
If vds is larger than this red region, transistor is in saturation but output resistance is still small around this border.
In center figure , we set the reference point P. If vds is P, transistor has diode structure and is saturated enough.
In right figure, we define the Vds’(dash), which has almost the same gd as P, as the lowest limit for auto Vds setting.
Designer can also consider the region between this lower limit and the boundary of over drive vds as the margin when adjusting final vds interactively.
Thus, this lower Vds enables the vertical stack transistors in AnaCell

## Slide 8
DC bias setting and Vds tuning 2
■Bias of each transistor is automatically adjusted satisfying VDD-GND voltage
■This feature is also interactively usable and fast in manually adjustment
without the effort of changing all transistors in AnaCell
Notes: In adjustment of bias in AnaCell, it is automatically budgeted as initial value which satisfies the Kirchhoff law in AnaCell.
In reality, designer will change the bias for targeting gain or output resistance or other intention.
AnaCell provides that how each transistor affects to other transistor in advance when modifying current bias and this makes it easier for designers to make decisions.
This will enable to improve design efficiency in all phases of analog design for tuning to targeting final specification.
Designer also can have the view of lower limit of Vgs and Vds which are key of small signal characteristic gm and gd.

## Slide 9: Design methodology using AnaCell with auto DC bias setting
Designer can instantly get the initial appropriate DC bias under only VDD and Ids current.
1. Construct Circuit by AnaCell
2. Apply Technology to AnaCell
Specify only supply voltage(VDD) and Ids to each AnaCell and get the initial DC bias for all Transistors automatically
4. Select and adjust L W which satisfies
AnaCell requirements from candidates
5. Simulation with AC/Transient and evaluate final goal
Feasible bias range considering gm/gd/L/W/Vds/Vgs dependency which satisfies Ids
Notes: We show the AnaCell design flow which uses this auto bias setting.
At first, construct the circuit by several AnaCells and devices. Then apply the technology as in 2nd step.
In 3rd step, Designer specifies the supply Voltage and each current, then gets the each DC bias condition in each node by automatic bias setting.
At this point, designer can adjust the bias points based on allowable space of the gm/gd/L/W/Vds/Vgs which provides targeting Ids.
Once designer changes the bias points in one node, other node’s bias points in AnaCell are adjusted automatically.
Next flow is the same as the one presented in last year DAC in 4th step and 5th step.
Based on determined DC bias conditions, feasible L and W space is generated and checks the AnaCell’s circuits performance like gain or output resistance without spice simulation.
After all transistor’s L and W are determined, designer can run the spice simulation with AnaCell’s internal test bench or designer’s test bench for the circuit level.
With AC/Transient simulation, if it is necessary to change the L W or DC bias, designer can go back to the previous level. But this is also easy to change by L W table selection or auto bias setting.

## Slide 10: 2 Experiments in TPSco 65nm PDK
1. Differential Input Circuit Single-Ended Signaling Type Telescopic Current Mirror
Auto Bias setting
5minute
（60s/1Tr searching for 10 L cases）
Initial Value
Setting of Vgs
Range of effect messages
Setting of Vds
Bias Adjustment
0 ～ 1minute
（60s/1Tr searching）
Ids-Vgs
Ids-Vds
Vgs-Limit
Lower Limit Vds
gm parameter
at DC Bias Point
gd parameter
at DC Bias Point
Bias
Adjustment
Notes: We experimented in 2 circuits.
One is differential circuit which is proven architecture. The other is researching circuit in Gunma university targeting current source circuit which is insensitive to temperature variation by new circuit topology.
In both cases, we applied TowerJazz Panasonic 65nm process PDK.
In differential circuit, we ran auto bias setting and could derive the initial DC
bias in 5 minutes. This shows each Transistor could get the bias in 60 seconds in 10 of L cases.
After this final bias setting, we adjusted the performance metric and derived gain from 80dB to 110dB in 81,000 of L and W combination.

## Slide 11: 2 Experiments in TPSco 65nm PDK
Iout （output Current）
Circuit Registered to AnaCell
2. MOS reference current sources that are insensitive to temperature variation
Cancel the temperature dependency
Trail performance by LW setting for researching
Notes: Gunma university are researching the new circuit architecture which is insensitive for temperature.
It utilizes the point in I-V curve which does not depend on temperature by using different gate bias.
Using AnaCell accelerated this research and will realize the small and simple circuit than general bandgap reference circuit.

## Slide 12: 2 Experiments in TPSco 65nm PDK
Input of Design Information
W/L Combination Selection
Placement on Schematic
STEP1
STEP2
STEP3
START
A diagram of the circuit actually converted to AnaCell
AnaCell Design Flow
W/L Search
7minute
W/L Fix
Improved Circuit
Circuit Registered to AnaCell
（Conventional Circuit）
Improvement Rate 69.6%
Notes: Gunma university registered this current source which is insensitive for temperature to AnaCell and designed using the AnaCell design flow.
After setting the bias to this registered AnaCell, exhaustive candidates of L and W are derived automatically.
Then next step requires only selecting the suitable L and W from derived table, thus AnaCell improved the efficiency of design and research.
AnaCell takes 7 minutes in this circuit in order to get the exhaustible L and W table from bias condition.
As a result of the experiment, the current fluctuation rate on the cold side was 0.195% after the improvement, while that before the improvement was 0.64%.
Final circuit could be improved by 69.5% by modifying circuit topology.

## Slide 13: Summary
AnaCell can be applied for cell base analog design style but previously it requires designers some efforts and skill for DC bias setting.
We propose auto DC bias setting which considers the freedom of design allowance (we call designability) with process free and designer only needs to set VDD and Current.
This DC bias setting data would be reuse in other AnaCell’s bias if condition is same, and it improves the design time significantly.
This will promotes to auto analog generation without loss of multi performance and designer’s intent.
This design methodology changes the design style in proven circuits and also accelerates the research for new circuit.
Notes: Almost as above noted.
Let me summarize the presentation.
…
We believe this AnaCell with auto bias setting would be welcomed by even experienced skillful analog designer.
We appreciate the cooperation to this presentation from Gunma university and TowerJazz Panasonic semiconductor.