## Slide 1
How Much Can One Trust Foundry’s 3-Sigma PEX Corners? Ning Lu IBM, Essex Junction, Vermont, USA
2019 DAC Designer Track

## Slide 2
What is a 3-sigma PEX corner?
Inaccuracy of 3-sigma PEX corners
How to improve the accuracy of wire resistance’s 3-sigma corners?
Future work
Outline

## Slide 3
PEX: Parasitic EXtraction
  Vendor tools: Synopsys StarRC, Calibre xRC, Cadence Quantus QRC, etc.
  Layout  PEX  SPICE netlist
    A netlist contains FET instances, passive instances, many parasitic/interconnect resistive elements, and many parasitic/interconnect capacitive elements
3-sigma Corner: A corner at which a figure-of-merit reaches its 3-sigma min. or max value.
  Implicitly, a single SPICE simulation will “magically” reproduce the 3-sigma min. or max. value for the finger-of-merit using a corner model or a netlist at a 3-sigma corner
3-sigma Rmax (or Rmin) PEX corner: A PEX deck that off-set each metal level’s thickness and width bias by a pre-calibrated and fixed amount. After extraction, the resulting SPICE netlist will reproduce the 3-sigma Rmax (or Rmin) value of each metal level in a single SPICE simulation.
The pre-calibration is typically done for min. design width of each metal level.
Other 3-sigma PEX corners: 3-sigma Rmin, 3-sigma Cmax, 3-sigma Cmin
What is a 3-sigma PEX corner?

## Slide 4
Nominal on-wafer
wire widths
½Dw
Dw is the same for all wires of different design widths (global/correlated variations), and so is Dt.
On-wafer wire widths
at a process corner
There are random variations in both wire width and thickness.
Problem Statement: How to reproduce 3s wire Rmax corner values for all wire widths with a single set of tolerance off-set in width and thickness?

## Slide 5: Wire Resistance’s Statistical Model
Examine Wire R’s 3-sigma max corner using a linearized wire R model.
uw and ut are independent random and normalized variables

## Slide 6: Wire Resistance’s 3-Sigma Corners for One Width
Corner Model: Can reproduce a “figure-of-merit” corner in a single simulation.
Component form:
Vector form:
Many corner solutions for R3sig,max:
ex1. low-probability solution
ex2. high-probability solution
,
j
uw
ut
3
3
-3
-3
3n
R3sig,min
R3sig,max
R0

## Slide 7: Wmin’s High-Probability Corner for a Larger Width
Angle  increases with increasing w0.
A 3-sigma corner for one width is not a 3-sigma corner for another width
j
uw
ut
3n(wmin)
R3sig,max (wmin)
3n(wmid)
R3sig,max (wmid)
j
uw
ut
3n(wmin)
R3sig,max (wmin)
3n(wlarge)
R3sig,max (wlarge)
Projected
point
(very optimistic)
Projected
point
(somewhat
optimistic)
High-prob.
corner

## Slide 8: Wmin’s Low-Probability Corner for a Larger Width
Angle  increases with increasing w0.
A 3-sigma corner for one width is not a 3-sigma corner for another width
j
uw
ut
3n(wmin)
R3sig,max (wmin)
3n(wmid2)
R3sig,max (wmid2)
j
uw
ut
3n(wmin)
R3sig,max (wmin)
3n(wmid1)
R3sig,max (wmid1)
Projected point
(somewhat pessimistic)
(somewhat pessimistic for wmid2)
Low-prob.
corner

## Slide 9: Best-Fit 3-Sigma Corners for a Range of Wire Widths [wmin, wmax]
A user should provide a width range [wmin, wmax] for each metal level in his/her circuit.
Design rules include a min. width and a max. width for each metal level. But, the smaller the range(wmax – wmin) is, the more accurate the resulting 3-sigma corner is.
a. Find boundary:
b. Find center:
c. Move the blue point outward to
minimize the largest distance
to the circle for all projected points
within the range [, ]. +: max. corner; -: min. corner
j1
uw
ut
j0
projected
points

## Slide 10: Improved Corner Model Accuracy for [Wmin, Wmax]
Relative error = (R3sig,fixed corner – R3sig,min/max) / (3sR)
high prob.
high prob.
high prob.
The smaller the angle range 2q is, the more accurate a single fixed corner will be for all wire width within the width range [Wmin, Wmax].

## Slide 11
We have discussed the inaccuracy issue in semiconductor foundry’s 3-sigma PEX corners.
If a PEX corner is set to reproduce the 3-sigma corner of an interconnect R spec at one wire width, then it does not reproduce 3-sigma R corner at other wire widths in general.
We propose to generate a best-fit 3-sigma corner for a range of wire width. The smaller the range, the more accurate the 3-sigma corner will be.
Using a simple diagram, we have shown how to generate best-fit 3-sigma interconnect corners for a given range of wire width.
Summary

## Slide 12
Interconnect Capacitance: 2 more process parameters (interlevel distances to the metal levels above and below) also affect capacitance. One needs to work in a higher dimensional space to find a concrete solution.
  Each independent process variation is a one-dimensional space in the corner analysis.
Future Work