## Slide 1: Improving design performance using Machine Learning in Synthesis
Gaurav Varshney, Akshi Tomar
Texas Instruments

## Slide 2: Introduction
Synthesis results are important in determining the design performance as it is responsible for
  Technology mapping to libraries
  Data-path optimizations and
  Netlist generation that is consumed by the P&R flow.
Typically Synthesis optimization engine concentrates on one critical path at a time, improving it until it is no longer critical, and then moving to another.
Optimization engine ends up spending several iterations in improving timing of top critical path(s) if these paths cannot be optimized due to design constraint or design architecture issues.
  E.g. macro paths with large access time contributing to slack and paths with small logical depth etc.
This results in a large number of sub-optimal paths beneath these paths in the design, which could have been optimized if the tool had spent more effort on it. Thus, improving TNS (Total Negative Slack) significantly.
With the ever-increasing design complexity and shrinking design cycles, there is a growing need for design techniques that optimize timing right from synthesis to closure.

## Slide 3: Problem Statement and Motivation
Getting desired performance through the Synthesis engine involves expert usage of the tool, good understanding of the RTL structures and understanding of technology library
With the increase in complexity of VLSI designs, complexity of design tools (Synthesis) has also increased. Mastery of Synthesis tool to perform experiments to get desired results is becoming difficult task.
Quality of synthesis results is direct function of
  Technology library composition
  Synthesis tool setup (options/parameters, features)
  User expertise
Often designers end up spending significant amount of time and several iterations in understanding technology libraries and customizing tool setup to get the desired results (PPA)
These efforts are not reusable from one design to another design
In this paper, we propose a solution to address these challenges through a Machine Learning model for running synthesis thorough industry tools.

## Slide 4: Proposed Solution – Block Diagram
Previously closed designs and/or test designs
Trained Machine Learning model
ML based ranked paths + Tool Settings + cell swap info
Synthesis Tool
TCL file containing tool settings, path weightage for optimization and instance swapping
Synthesis Results
(Netlist, Reports)
RTL
Library
Synth Setup
Generic
Map
Optimization
Path
Profiler
Command generator
Design
Design Analyzer
Standard Cell Library
Library Analyzer
Machine Learning Module
Library Analyzer: Analyzes standard cell library and generates a DB of cell information with ranking using different parameters
1
Design Analyzer: Analyzes previously closed designs and also run the same design with default flow to generate slack diff per path and other features of the path which are later used for training the module
2
Training Machine Learning Model: ML model is trained using “Library DB” and “Design DB” by running regression.
3
Applying machine learning model
5
Design to be Synthesized for higher performance
4

## Slide 5: Proposed Solution – Details
Machine Learning (ML) Data Preparation
  Library analyser: A DB is prepared for the different parameters which will be utilized by Machine Learning model
  Design analyzer
    Different designs which have been closed by experts through custom flows are analyzed as follows:
      Run design using default synthesis flow till Synthesis-map stage & iterate through all the violating paths in map-DB
      Compare the slack of the violating path with the final slack in closed DB to get the “slack difference”
      Find characteristic of paths (path depth, library cells in the path, cell fanout, etc.) used in custom flow
      Save information in DB (each path details being stored as one record) to be used by Machine Learning model
Feature engineering
  Once the Library DB and Design DB are prepared, slack differences are analyzed to correlate with the other parameters in the DB to identify features to be used by Machine Learning model
Training Machine Learning Model
  Model is trained using “Random Forest Regressor” with the identified features and the target being “slack difference”
Applying trained model on a new design
  For a new design after running Synthesis-map, list of violating path is created along with list of features
  Trained Machine Learning model is applied to predict the slack improvement. This information used to rank the paths.
  Output generated by machine learning model: ranked paths, cell swap strategy for select paths
  This information is converted in Synthesis tool commands to run Synthesis-optimization (and potential incremental optimization). Paths which are ranked higher are assigned higher priority for the slack improvement during optimization.
Results
  With this method we see significant WNS and TNS improvement for the design

## Slide 6: Results
S.No. | Steps | WNS (ps) | TNS (ns) | FEP | Cell Area
1. | Generic | -552 | -138 | 596 | 1,926,074
2. | Map | -502 | -405 | 2227 | 562,363
3. | Optimization | -235 | -99 | 593 | 548,858
4. | Incremental Opt | -226 | -85 | 589 | 538,069
5. | Placement + Opt | -744 | -1045 | 2924 | 584,185
Synthesis CPU time |  | 12,633 (sec) |  |  | 
S.No. | Steps | WNS (ps) | TNS (ns) | FEP | Cell Area
1. | Generic | -552 | -138 | 596 | 1,926,074
2. | Map | -502 | -405 | 2227 | 562,363
3. | Optimization with ML | -263 | -17 | 438 | 558,812
4. | Incremental Opt | -226* | -12 | 196 | 547,341
5. | Placement + Opt | -673 | -981 | 2911 | 590,834
Synthesis CPU time |  | 15,792 (sec) |  |  | 
Reference:
Expert User run with several rounds of tool option fine-tuning
Machine Learning (ML) Based Run showing improved WNS and TNS
Design-1
Design-2
S.No. | Steps | WNS (ps) | TNS (ns) | FEP | Cell Area
1. | Generic | -1240 | -3335 | 7052 | 8,094,030
2. | Map | -728 | -3096 | 13442 | 2,253,562
3. | Optimization with ML | -370 | -394 | 4147 | 2,151,923
4. | 1 Incremental Opt | -283 | -202 | 3027 | 2,058,926
5. | Postroute | -219 | -163 | 3274 | 2,557,921
Synthesis CPU time |  | 84,531 (sec) |  |  | 
ML Based
S.No. | Steps | WNS (ps) | TNS (ns) | FEP | Cell Area
1. | Generic | -1240 | -3335 | 7052 | 8,094,030
2. | Map | -728 | -3096 | 13442 | 2,253,562
3. | Optimization | -412 | -558 | 6179 | 2,146,761
4. | 2 Incremental Opt | -329 | -339 | 5186 | 2,037,588
5. | Postroute | -231 | -229 | 4565 | 2,519,647
Synthesis CPU time |  | 103,346 (sec) |  |  | 
Reference
Testing on multiple designs show consistent performance improvement using proposed methodology. Significant cycle time improvement as the solution works out of the box with no additional input requirement. Results can further be improved by reviewing results generated by Machine Learning model with expert user and fine-tuning the generated commands.
14% WNS and 40% TNS improvement with just 1 incremental Optimization
5% WNS and 29% TNS improvement after postroute Optimization
85% TNS and 67% FEP improvement in incremental Optimization
10% WNS and 6% TNS improvement after placement Optimization
*Memory path

## Slide 7: Summary
Paper presents a method for improving design performance using Machine Learning techniques in Synthesis
  Trains Machine Learning model using information from reference designs (previously timing closed designs and/or input designs covering different scenarios for model training)
  Analyzes early results in synthesis flow (Mapped DB) to profile the violating paths and applies trained Machine Learning model to guide optimization to focus on right set of paths for optimization
  Results in improved WNS and TNS
Methodology can be integrated in any vendor tool
No improvement with proposed methodology would typically indicate a change required in input constraints and/or RTL update
Future work:
  Model performance can be improved by incorporating more features
  Machine learning can be employed for better design space exploration in terms of the number of cost groups that need to be formed and path distribution in each cost to achieve best design time to performance tradeoff
  Exploring training using P&R data to improve correlation between Synthesis and P&R