## Slide 1: Evolving Requirements for Network
Cloud /
Data Center
Infrastructure
Edge
Objective: Deliver highest performance/watt with adaptability
Compute
Data Transfers
Memory Hierarchy
Block RAM

## Slide 2: Introducing Speedster7t: FPGA Devices with ASIC Performance
Speedster7t is a new class of FPGA optimized for high bandwidth workloads
  Break historical bottlenecks that reduce efficiency
ASIC level performance with FPGA architecture
Highest efficiency Compute engines
  New Machine Learning Processor (MLP)
Efficient Data Transfers
  New Network-on-Chip eliminates routing congestion
Balanced Memory Hierarchy
  Highest speed interfaces and external memory bandwidth

## Slide 3: Math Block Optimized for AI/ML
Memory
Cascade in
Operand
Cascade in
BRAM72k
Register File
Integer MAC
Fracturable
Adder / Accumulator
Float MAC
Fracturable
Adder / Accumulator
Tightly coupled memory blocks
Large block RAM (e.g. 72Kbits)
Register File (e.g. 2K bits)
High density MAC arrays
Up to 32 multipliers per MAC block
Integer MAC (e.g. Int16, Int8, Int4)
Flt pt MAC (16bit, 24bit, blk float)
Operand and memory cascade
Create larger functions without using FPGA routing or resources

## Slide 4: MLP Block Floating Point Mode
Cascade_in[47:0]
Cascade_out[47:0]
MAC
[23:0]
Integer Multiply / Add Tree
Convert to Floating Point
Floating Point Accumulate
Multiplier/multiplicand fractions (same exponent)
Block
48-bit Fraction ACC
Round to desired precision
MLP
#1 Find largest exponent
Find difference of other exponents from largest
#2 Right shift mantissa for smaller values
#3 Multiply mantissa values for data and weight
Add exponents and accumulate as floating point number
Block Floating Point Example
Block Floating Point Implementation
#1
#2
#3
exponents

## Slide 5: High Bandwidth Network on Chip in next generation FPGAs
High performance: 20Tbps
Ease-of-use: simple AXI or streaming interface
More efficient: FPGA resources not used for NOC
Better routing
GDDR6 Ctrl + PHy
GDDR6
GDDR6 Ctrl + PHy
GDDR6
GDDR6 Ctrl + PHy
GDDR6
GDDR6 Ctrl + PHy
GDDR6
Traditional FPGA Design
Accelerator
#1
Accelerator
#2
Status
Control
Status
Control
Parameters
Parameters
FIFOs
FIFOs
NAP
NAP
Accelerator
#1
Accelerator
#2
Speedster7t FPGA+ Design

## Slide 6: Benchmarking examples: Conv2d, Yolo-v2 and ResNet-50
 | AC7t1500 Throughput
ResNet50 | 8,600
Yolo-v2 | 1,600
80% MLPs used, 16x 8x8 per MLP
MLP Fmax: 750 MHz
Dimensions batch, in_height, in_width,in_channels filter_height, filter_width, out_channels | Number format | Stride | Performance |  | Resource Usage |  | 
 |  |  | Img/sec | Freq (MHz) | # MLPs | # BRAMs | # LUTs
Conv2d 1,227,227,3,11,11,1 | int8 | 1 | 1 image in 137us | 750 | 1 | 5 | 585
Conv2d 32,227,227,3,11,11,1 | int8 | 4 | 32 images in 137us | 749 | 32 | 36 | 3,413